## Slide 1: Thoughts on TDLS Off-Channel Link
Date: 2024-05-05
Authors:
Name | Company | Address | Phone | Email
Liangxiao Xin | OPPO |  |  | v-xinliangxiao@oppo.com
Liuming Lu |  |  |  | 
Chaoming Luo |  |  |  | 
Wei Dong |  |  |  | 
Ning Gao |  |  |  | 
Yapu Li |  |  |  | 

## Slide 2: Introduction
TDLS is the P2P communication mechanism defined in IEEE 802.11 but we only improve the signaling of TDLS in TGbe.
The TGbn PAR has agreed to improve the P2P commination.
In this presentation, we discuss how to improve the TDLS which utilizes the MLO feature.

## Slide 3: Background
Current TDLS has defined two types of channel.
  Base channel: the channel where the AP is operating.
  Off-channel: a channel where the associated AP is not operating
11be introduces MLO which allows one Wi-Fi device having multiple STAs which operate on different links.
  A TDLS direct link can be established by a TDLS setup procedure is launched over another base link
  When setting up a TDLS direct link, the TDLS direct link is one of the base channels only. (Because the BSSID field of Link Identifier element is set to one of BSSID of the AP that is operating on the link.)

## Slide 4: Current Off-channel TDLS Direct Link
Step1: A TDLS direct link is established successfully over the base channel.
Step2: one of the peer STA launches a TDLS channel switch procedure to switch the off-channel TDLS direct link
Base Channel
Base Channel
Base channel TDLS direct link
AP
STA 1
STA 2
Off-channel TDLS direct link
AP
STA 1
STA 2
Step2: TDLS Channel Switch
Step1: TDLS setup

## Slide 5: New Use Case for TDLS Off-channel Link
Network Scenario:
  A network consist of a legacy AP (single link) and non-AP MLDs.
  Non-AP MLDs can only associate with the AP over the base channel of the AP.
  The other STAs affiliated with non-AP MLDs operates over the off-channel (not used !!!).
Proposed Idea:
  The STAs operating on the off-channel can be used to set up off-channel TDLS link for P2P communication.
Link1: Base Channel
(e.g., 5GHz)
Link1: Base Channel
(e.g., 5GHz)
Link2: Off Channel
(e.g., 2.4GHz)
Pre-EHT AP
（5GHz only）
STA MLD 1
STA MLD 2

## Slide 6: TDLS v.s. Wi-Fi Direct
 | TDLS | Wi-Fi Direct
Setup Procedure | Setup signaling is transmitted through AP | Setup signaling is transmitted between two peer STAs
Association | A TDLS STA can communicate with its AP and its peer TDLS STA at the same time | A non-AP STA can only associate with either AP or peer STA
DL/UL
DL/UL
TDLS link
AP
STA 1
STA 2
DL/UL
Wi-Fi Direct
AP
STA 1
STA 2
(Wi-Fi Direct AP)

## Slide 7: Summary
In this contribution, we provide a scenario to establish off-channel TDLS direct link.
  The TDLS peer STAs may not associate with the BSS
  The MLDs that the TDLS peer STAs affiliated with are associate with the BSS
We discussed the advantages of TDLS compared with Wi-Fi Direct

## Slide 8: SP1
Do you support to include the following in SFD?
  11bn shall improve the TDLS mechanism to allow the P2P transmission over an off channel.
    The TDLS peer STAs may not associate with the AP.

## Slide 9: SP2
Do you support to include the following in SFD?
  11bn shall allow to establish an off-channel TDLS direct link between two TDLS peer STAs that may not associate with the BSS but their corresponding MLDs are associated with the BSS.