## Slide 1: NPCA Primary Channel Selection
Date: 2024-12-12
Authors:

## Slide 2: Introduction
According to SFD [1], TGbn has agreed to define a non-primary channel access (NPCA) mode that enables a STA to access the secondary channel while the primary channel is known to be busy due to OBSS traffic or other TBD conditions.
  A BSS shall only have a single NPCA primary channel
In this proposal, we discuss how to select NPCA primary channel (PCH) in NPCA operation

## Slide 3: Motivation
In current baseline, there is no explicit in-BSS interactive procedure for selecting PCH [2], the location of PCH is predetermined and indicated by the AP
  Such as via some algorithms or pre-configured, using QLoad report, selecting the least occupied channel considering other APs
However, while introducing NPCA technique, things become different
  Non-AP STAs may have limited capability in switching between channels/bands, switching to a sub-band too far away from PCH may take too long, resulting in low efficiency when performing NPCA
  NPCA PCH concerns a set of non-AP STAs that support NPCA, not the entire BSS; in certain scenarios, NPCA PCH only concerns non-AP STAs that have the same OBSS interference as AP [3]
  For non-AP STAs, always enabling NPCA may not be the best option [4], considering statistics of channel occupancy, overhead from switching back and forth, it may choose to enable or disable depending on some conditions, such as the frequency location of NPCA PCH, its switching capability, traffic status etc
  Other interference, coexistence events on particular channels for non-AP STAs

## Slide 4: Proposed Solution – Part I
As such, it would be more efficient if non-AP STAs provide their preference in determining the frequency location of NPCA PCH, to assist AP’s decision
Specifically, NPCA-supporting non-AP STAs indicate information for selecting NPCA PCH (solicited/unsolicited), include
  NPCA Supported Channel list, Preferred NPCA PCH Channel list
  Channel Unavailable Info, OBSS ID list, OBSS PCH list

## Slide 5: Proposed Solution – Part II
Besides, AP may request those non-AP STAs to report the above info, such request may include
  AP Preferred NPCA Channels
  Different considerations:
    considering when P20 is busy, it is more likely that S160 or S80 or S40 is idle (AP Preferred Channel) ;
    considering P160 or P80 or P40 (AP Preferred Channel) is more likely to be within operating BW of non-AP STA for efficient switching
Non-AP STAs may respond with whether to accept this request
  Decline request: If the required measurement is beyond the capability of the STA, may interfere with its normal transmission etc
  Accept request

## Slide 6: Proposed Solution – Part III
Based on the above, AP determines NPCA PCH and indicate
  Frequency location of NPCA PCH
  Access mode: Trigger-only mode or contention-enable mode
  NPCA Parameter
    NPCA Supported BW, NPCA Supported MCS And NSS, Switch Delay etc
    may also include NPCA Parameter for other non-Tx BSSIDs
NPCA OMI: After receiving frequency location of NPCA PCH from AP, non-AP STAs that support NPCA indicate whether to enable or disable NPCA
  NPCA Mode (enable/disable)
  NPCA Parameter Update (Control), NPCA Parameter
  NPCA Link Bitmap for MLD

## Slide 7: Summary
In this contribution, we discussed how to select NPCA PCH efficiently
  NPCA-supporting non-AP STAs indicate their preference in selecting NPCA PCH
  NPCA-supporting non-AP STAs indicate whether to enable or disable NPCA depending on certain conditions
Notes: In this proposal, we focus on the TXOP level preemption, introducing a credibility criterion to assist the fair classification among streams and honest behavior between STAs to further promote the preemption feature

## Slide 8: Straw Poll 1
Do you agree in 11bn that NPCA-supporting non-AP STAs may indicate their preference in selecting NPCA PCH ?
  For example, the preference may include NPCA Supported Channel list, Preferred NPCA PCH Channel list
  Whether to support solicited/unsolicited indication is TBD

## Slide 9: Straw Poll 2
Do you agree in 11bn that NPCA-supporting non-AP STAs may indicate local channel information for selecting NPCA PCH?
  For example, the local channel information may include Channel Unavailable Info, OBSS ID list, OBSS PCH list

## Slide 10: Straw Poll 3
Do you agree in 11bn that NPCA-supporting non-AP STAs may dynamically enable/disable NPCA via OMI?

## Slide 11
Appendix

## Slide 12: Proposed Solution – Part IV
Choosing NPCA PCH
AP creates a list of candidate channels, considering available operating channels, regulation, radar detection, AP’s own channel measurement etc
AP creates an array for each candidate channel that allows the recording of non-AP STAs’ indicated information, consisting of
  OBSS count, OBSS PCH count, recommendation count, (average) channels load, maximum channels load, channel quality etc
According to received non-AP STAs’ indicated information, update this array
AP selects one NPCA PCH from those candidate channels, according to below metric:
  With the least OBSS count or OBSS PCH count, or
  With the most recommendation count, or
  With the least (average) channels load or least maximum channels load, or
  With the best channel quality
If there are multiple channels that satisfy one metric, select one channel randomly or with the highest score considering combination of metrics

## Slide 13: References
11-24/209r6, Specification Framework for TGbn
IEEE P802.11-REVme/D7.0, August 2024
11-23-2005-01-00bn-non-primary-channel-access-npca
Wei, D., Cao, L., Zhang, L., Gao, X., & Yin, H. (2024). Optimized Non-Primary Channel Access Design in IEEE 802.11bn. ArXiv. https://arxiv.org/abs/2405.00227