## Slide 1: Secure E2E Operation for AMP
Authors:
Date: 2024-12-14
Name | Affiliations | Address | Phone | email
Sanket Kalamkar | Qualcomm Technologies Inc. |  |  | sankal@qti.qualcomm.com
George Cherian |  |  |  | 
Alfred Asterjadhi |  |  |  | 

## Slide 2: Introduction
An AMP client needs to carry out a lightweight authentication and encryption process, which:
  Largely follows legacy procedures with enhancements for AMP use cases
  Takes into account the limited capabilities of AMP clients, such as
    Limited energy availability
    Minimal to no persistent memory
This contribution discusses secure end-to-end (E2E) operation for AMP clients

## Slide 3: E2E View of AMP Operation
Offline Onboarding
  Password setting, which establishes the Pairwise Master Key (PMK)
  Note: Likely outside IEEE scope
Initial Info Exchange (Discovery)
  AP and AMP clients exchange basic information
    e.g., MAC addresses and other basic information
  AP uses this mode to determine the presence of active AMP clients
AMP Operation Mode Information Exchange
  AP requests the client's operation capabilities
  The client provides capability and schedule-related information to the AP
    E.g., schedule information, power budget, energy harvesting capabilities
  AP uses this mode to determine the Tx/Rx parameters to reach AMP clients
AMP Trigger/UL Response
  AP triggers the client for uplink (UL) transmissions; client sends UL transmissions
  Happens Per Schedule or On-demand manner
Initial Info Exchange
AMP Trigger/ UL Response
AMP Operation Mode Information Exchange
Offline Onboarding
Once
Once in a while
Once in a while
Per Schedule/ On-demand

## Slide 4: Offline Onboarding
Setting up the pairwise master key (PMK) at AP and client
  Password acts as pre-shared key (PSK)
  PMK is generated from the PSK
In later phases, the PMK is used to generate transient keys, e.g., pairwise transient key (PTK)
  For message integrity and encryption

## Slide 5: Initial Info Exchange
The AP and the client exchange non-sensitive information
  E.g., MAC addresses
No security needed
Since the AP does not know the client's MAC address at this stage, the request will be broadcast, resulting in multiple responses
  Collision control should be addressed later
Initial Info Req
Initial Info Resp
First time after on-boarding
AP
AMP client

## Slide 6: AMP Operation Mode
Operation Info Request:
  AP requests operation capabilities of the client
    Schedule information, e.g., how frequently the AP should trigger the client
    Power budget of the client, e.g., energy harvesting capabilities
    How often the client needs to be asked for operation info request
      Required if the schedule changes
Operation Info Response:
  Client informs capability and schedule related info to AP
  An attacker could use this information to target the client during scheduling
Operation Info Req
Operation Info Resp (Schedule, Power Budget)
Repeats once in a while
AP
AMP client

## Slide 7: AMP Operation Mode (Contd…)
For secure AMP Operation mode, it can be preceded by a transient key generation process
  This step might be required because the AMP client may lack persistent memory to retain the key from previous exchanges with the AP
  Key Req is unprotected
  One way authentication: The client does not authenticate AP during key generation
  Uses PMK obtained during offline on-boarding
The generated key is used to protect:
  Operation Info Req
  Operation Info Resp

## Slide 8: AMP Operation Mode (Contd…)
The Operation Mode Req can be unprotected if:
  AP intends to gather responses from multiple clients
  The Req does not carry sensitive information
In this case, the Operation Mode Req and Key Req can be merged
Similarly, the Operation Mode Resp and Key Resp can be merged
  The Operation Mode Resp can carry MIC
  No Encryption

## Slide 9: Trigger/UL Transmissions
The AP sends AMP Trigger either as per the schedule or per event basis
If the AMP client can’t retain the transient key, the Trigger process can be preceded by a transient key generation process
  E.g., when the AMP Trigger is not sent close to the Operation Mode Req/Resp process
The generated key can be used to protect:
  Trigger frame from the AP
  UL Response from the client

## Slide 10: Trigger/UL Transmissions (Contd…)
The Trigger frame can be unprotected if:
  AP intends to gather responses from multiple clients
  The frame does not carry sensitive information
In this case, the Trigger frame transmission and Key Req can be merged
Similarly, the UL Resp and Key Resp can be merged
  The UL Resp can carry MIC
  No Encryption

## Slide 11: Summary
Secure end-to-end (E2E) operation for AMP clients, focusing on:
  Constraints at AMP Client:
    Limited energy availability and minimal persistent memory
  Authentication and Encryption:
    Lightweight key generation process due to energy constraints
    One-way authentication where the client does not authenticate the AP
Key phases of AMP operation:
  Offline Onboarding:
    Setting up the PMK
  Initial Info Exchange:
    Exchanging basic information like MAC addresses
  AMP Operation Mode:
    AP requests and receives operation capabilities and schedule information from the client
  AMP Trigger/UL Response:
    AP triggers the client for uplink transmissions

## Slide 12: SP
Do you agree that TGbp to define a mechanism to support secure communications for 802.11bp clients?