## Slide 1: Handling Asymmetric Switching for Non-Primary Channel Access
Date: 2024-11-19
Authors:
Name | Affiliations | Address | Phone | email
Jason Yuchen Guo | Huawei Technologies |  |  | guoyuchen@huawei.com
Yunbo Li |  |  |  | 
Guogang Huang |  |  |  | 
Ming Gan |  |  |  | 
Yue Zhao |  |  |  | 
Maolin Zhang |  |  |  | 

## Slide 2: Introduction
TGbn has decided to define NPCA mode which enables a STA to access the secondary channel while the primary channel is known to be busy due to OBSS traffic or other TBD conditions.
NPCA can improve channel utilization when the non primary channels are not occupied by the OBSS transmission, and also reduces latency since it offers more opportunities to use the channel.
However, due to the nature of the wireless transmission, different STAs will see different OBSS transmissions in the air, and we should try to ensure that the transmitter and the receiver switch to the NPCA primary channel synchronously to obtain the above benefit.

## Slide 3: Asymmetric Switching
Due to different channel conditions, different STAs in the same BSS may decode an OBSS packet successfully or unsuccessfully. In that case, some STAs may switch to the NPCA primary channel, while others may not.
Example 1 - Non-AP STA switches, AP does not switch
  If a non-AP STA is closer to the transmitter of the OBSS packet while the AP is relatively far, the non-AP STA may switch to the NPCA primary channel, and the AP may still park on the primary channel
OBSS non-AP STA
OBSS AP
OBSS Packet
Motivation:
If the non-AP STA knows that the AP does not switch, it should also stay on the primary channel:
It can receive some short packet from the AP;
It can perform SR transmission if conditions satisfy

## Slide 4: Asymmetric Switching
Due to different channel conditions, different STAs in the same BSS may decode an OBSS packet successfully or unsuccessfully. In that case, some STAs may switch to the NPCA primary channel, while others may not.
Example 2 – AP switches, non-AP STA does not switch
  If the AP is closer to the transmitter of the OBSS packet while a non-AP STA is relatively far, the AP may switch to the NPCA primary channel, and the non-AP STA may still park on the primary channel
OBSS non-AP STA
OBSS AP
OBSS Packet
Motivation:
If the AP knows that the non-AP STA does not switch, it should avoid transmitting to that non-AP STA when performing NPCA

## Slide 5: Solution
In order to solve the issue in example 1:
AP can announce a list of MAC addresses of OBSS STAs, where the AP switches to the temporary primary channel when receiving the packets from those OBSS STAs
Non-AP STAs will only perform NPCA when receiving OBSS packets transmitted from those OBSS STAs
Simplified solution:
Because OBSS STAs can be moving, it is difficult for the AP and non-AP STAs to manage the list of OBSS STAs in a timely manner. To simplify the solution, the AP can just announce a list of MAC address of OBSS APs (or BSS colors of those APs)
Non-AP STAs will only perform NPCA when receiving OBSS packets with RA/TA matching any of the MAC address (or BSS color) in the list

## Slide 6: Solution
In order to solve the issue in example 2:
Non-AP STA also needs to indicate to the AP: a list of OBSS STA MAC addresses
During NPCA, AP will only transmit to the non-AP STA if the NPCA is performed due to an OBSS packet transmitted by one of those OBSS STAs
A simplified solution could also be:
  The non-AP STA indicates a list of OBSS AP MAC address or BSS colors

## Slide 7: Conclusion
We consider the asymmetric channel switching issue in the NPCA
We can reduce the asymmetric channel switching by announcing the MAC address/BSS color of OBSS STAs/APs whose transmissions cause the NPCA

## Slide 8: SP
Do you support to include in the 11bn SFD:
AP can announce a list (or bitmap) of BSS colors, where the AP and its associated STAs switch to the NPCA primary channel only when receiving the OBSS packets from the BSS(s) whose BSS color is in the list (or indicated as 1 in the bitmap)

## Slide 9: References
[1] 11-23/34, “Non-primary channel utilization,” Sindhu Verma
[2] 11-23/1414, “Secondary channel usage follow up,” Liwen Chu
[3] 11-23/961, “UHR secondary channel access,” Minyoung Park
[4] 11-23/797, “Non-primary channel access,” Yongho Seok
[5] 11-23/1891, “Nonprimary channel access - follow up,” Gaurang Naik