## Slide 1: NPCA Operation with Multi-link Device
Name | Affiliations | Address | Phone | email
Longlong Hong | Ruijie Networks Co., Ltd |  |  | 
Hui Che |  |  |  | chehui@ruijie.com.cn
Ke Zhong |  |  |  | 
Hang Yang |  |  |  | 
Mengying Lin |  |  |  | 
Fachang Guo |  |  |  | 
Date: 2024-12-30
Authors:

## Slide 2: Introduction
TGbn defines the operation mode that enables a STA to access the NPCA primary channel when the BSS primary channel is busy due to OBSS interference or other TBD conditions.
The existing NPCA mechanism focuses on single-link scenarios, where NPCA AP or NPCA STA switch from the BSS primary channel to the NPCA primary channel when the BSS primary channel is busy.
In this contribution, we discuss the NPCA with multi-link device(MLD).

## Slide 3: Issue - Hidden STA
MLD
AP MLD1, AP MLD2, non-AP MLD1, non-AP MLD2 and non-AP MLD3 are MLDs, such as two links, Link1-2.4GHz band, Link2-5GHz band.
AP MLD1 on the NPCA primary channel
For the BSS1’s Link2, AP MLD1 and non-AP MLD2 switch to NPCA primary channel to avoiding OBSS interference from the Link2 of AP MLD2 or non-AP MLD3 in BSS2.
Non-AP MLD1 (Hidden STA) on the BSS primary channel:
  AP MLD1 initiates frame exchange on Link2’s NPCA primary channel with non-AP MLD1 for the BSS1.
  For BSS1’s Link2, AP MLD1 on NPCA primary channel, but non-AP MLD1 on BSS1 primary channel.
Not all NPCA-enabled STAs in the BSS will switch to the NPCA primary channel.
The lack of controlled between AP and associated STAs renders NPCA unreliable and inefficient in many scenarios [1-5].

## Slide 4: Proposal: NPCA with MLD
Multi-Link Operation (MLO) allows APs and STAs to communicate using multi-links, and not all primary channels of multiple links overlap with the OBSS channel
  Link1: BSS1 Primary channel does not overlap with the BSS2 channel.
  Link2: BSS1 Primary channel overlap with the BSS2 channel.
  When BSS1 Primary of Link2 is busy, the NPCA AP-MLD/non-AP MLD can exchange management/control frames on the NPCA primary channel of Link2 or the BSS Primary channel of Link1.
Cross-Link Coordination for MLD:
  AP1(of AP MLD1) can report the interference channel of Link2 to STA1(of non-AP MLD1) by the BSS primary channel of Link1.
  Then, AP2 and STA2 can exchange data in the NPCA primary channel of Link2.

## Slide 5: Conclusion
For the NPCA with MLD, we found the Hidden STA issue.
For the hidden STA issue, NPCA with Cross-Link Coordination may provide higher access efficiency:
  NPCA AP MLD/non-AP MLD may exchange management/control frames on the NPCA primary channel of interfered link (NPCA primary channel is free on this link) or the BSS primary channel of the other links without interference.

## Slide 6: References
[1] 11-24/1596r1, “Consideration of MAP Coordination on NPCA channel,” Yan Li
[2] 11-23/0495r0, “Non-Primary Channel Access (NPCA),” Minyoung Park
[3] 11-24/0318r0, “Robust Secondary Channel Access,” Yanchun Li
[4] 11-24/1093r0, “Special scenarios in Non-Primary Channel Access,” Sindhu Verma
[5] 11-24/1155r0, “Further discussions on NPCA,” Sanghyun Kim