## Slide 1: IDC Scenarios and unavailable period indication
Date: 2024-12-31
Authors:

## Slide 2: Background
Unavailability information could be used for Co-ex and even for power save.
TGbn has passed several motions on TXOP level unavailability information indication and we have following items in SFD [1] [2] :
  [Motion #30]
  11bn defines a mechanism for a non-AP STA to report unavailability at TXOP level and define or reuse/update existing mechanism for a non-AP STA to report long term (periodic) unavailability.
  [Motion #146]
  A non-AP STA that is a TXOP responder can indicate in a response frame 1) for how long it will be available, if known and/or 2) whether it will be unavailable after a specific point in time and, if known, for how long.
    The response frame is a multi-STA BlockAck frame sent by the non-AP STA in response to the initial control frame or to MPDUs that solicit an immediate response.
    Currently, we haven't reached a consensus on the unsolicited unavailability indication yet.

## Slide 3: Current designs
For unsolicited unavailability information indication, there might be two options at present.
  Multi-STA BA [3] and [4] .
  BSRP TF [5] .
• Both of them need to change aggregation rules in some cases.
  A QoS-Null data frame with BSR and a multi-STA Block ACK frame with unavailability information will be aggregated in an A-MPDU as a response in a TB PPDU for the BSRP TF [6].
• Both of them may not be acknowledged to make sure the peer get the information.
  Unless the response rules are changed or newly defined.

## Slide 4: Unpredictable IDC events during a TXOP
It might be possible that a non-AP STA is aware of an upcoming IDC event after responding to an ICF or initiating a TXOP. For some instances:
  Game player’s control information delivered through in-device Bluetooth. In general, the event can be indicated to Wi-Fi about 0.5 ms in advance.
  UL transmission scheduled by gNB can be known about 1 ms in advance.
Such IDC events are unpredictable and may overlap with the remnant TXOP .
  Report them in ICR might be impossible sometime.

## Slide 5: Unavailable period indication by (A-)control field
[7] has mentioned that a new (A-)control field for IDC Info can be included in QoS Data/Null frames, Management frames (similar to BSR).
Indicating unavailable period by A-control field might be an alternative option for both solicited or unsolicited case.
  Can be piggybacked in QoS Data/Null frames and Management frames.
    Easier to indicate a sudden IDC event during a TXOP.
    The aggregation rules needn’t to be changed.
    Unavailability information delivered in A-Control subfield in a frame can be ACKed.
  May reduce signaling overhead.

## Slide 6: Unavailable period indication (UPI) by (A-)control field
There are two options for unavailable period indication by A-control field:
  Opt1. use TBD bits to indicate unavailability duration.
    Imply that the unavailability duration will start after this PPDU or the response PPDU of this PPDU.
  Opt2. use TBD1 bits to indicate unavailability start time and TBD2 bits duration.
    TBD1 and TBD2 can be 9 [5] [8].
Control ID | Unavailability duration
4 bits | TBD bits
Control ID | Unavailability start time | Unavailability duration
4 bits | TBD1 bits | TBD2 bits
The name of such A-control is TBD (e.g. UPI control)

## Slide 7: Cross link Unavailable period indication
[9] proposed Multi-link unavailability indication (MLUI) by which unavailable period can be indicated cross links.
  A 4 bits Link ID can be added in the UPI control field (name TBD) to indicate the unavailable period of a specific link.
Control ID | Link ID | Unavailability duration
4 bits | 4 bits | TBD bits
Control ID | Link ID | Unavailability start time | Unavailability duration
4 bits | 4 bits | TBD1 bits | TBD2 bits

## Slide 8: Summary
This document analyzed requirements of unpredictable IDC events and proposed to use A-Control field for the unavailable period indication.

## Slide 9: SP 1
Do you agree to add the following text to the 11bn SFD?
  A non-AP STA can indicate in A-Control subfield 1) for how long it will be available, if known and/or 2) whether it will be unavailable after a specific point in time and, if known, for how long.

## Slide 10: References
[1] 11-24-0171-21-00bn-tgbn-motions-list-part-1
[2] 11-24-0209-07-00bn-specification-framework-for-tgbn
[3] 11-24-1550-01-00bn-in-device-coexistence-follow-up
[4] 11-24-1558-02-00bn-in-device-coexistence-follow-up
[5] 11-24-1893-00-00bn-icf-follow-up
[6] 11-24-1887-00-00bn-bsrp-tf-response-rules-changes-for-m-ba
[7] 11-24-0834-01-00bn-some-details-on-in-device-coexistence
[8] 11-24-1974-03-00bn-detailed-text-proposal-on-coexistence
[9] 11-24-0806-00-00bn-multi-link-in-device-coexistence-management