## Slide 1: Discussion on the protection of Co-RTWT
Date: 2024-12-31
Authors:

## Slide 2
Recap
TGbn has made progress on Co-RTWT with following passed motions.
[Motion #48]
Define mechanisms that enable APs to coordinate their rTWT schedule(s) and/or to ensure that one AP provides the protection of the rTWT schedule(s) of the other AP.
NOTE – TBD mechanisms including negotiation between 2 APs and advertisement.
[Motion #149]
If an AP extends the protection of the rTWT schedule of another AP, following negotiation or through other means, then:
  The AP shall ensure its TXOP ends before the start time of the corresponding OBSS rTWT SP(s)
  The AP, if it has at least one associated STA that is capable of rTWT, shall advertise in the beacon frames it transmits the OBSS rTWT schedule so that its associated STAs supporting rTWT follow the baseline rTWT rules for the OBSS rTWT schedule.

## Slide 3: Observation & Consideration
Low Latency Traffic (LLT) during Co-RTWT SPs may not occupy the whole operating BW of Co-RTWT coordinated AP.
  The operating BW of the Co-RTWT requesting AP or the targets (associated STAs of Co-RTWT requesting AP) of LLT may be different with the operating BW of Co-RTWT coordinated APs ;
  The Primary channel may not be aligned;
  LLT may not need a wide BW for delivery.
  For avoiding the overprotection of Co-RTWT SP, there might be 3 options:
    A Co-RTWT coordinated AP only provides protection on the Primary 20 MHz channel of the Co-RTWT requesting AP at the start time of Co-RTWT SPs ;
    A Co-RTWT coordinated AP provides protection on the channel indicated by the Co-RTWT requesting AP at the start time of Co-RTWT SPs;
    SP based NPCA [1],[2].

## Slide 4: Option 1. P20 protection for Co-RTWT SP
A Co-RTWT coordinated AP will only terminate the TXOPs occupied the Primary 20 MHz channel of the Co-RTWT requesting AP before the start time of Co-RTWT SPs.
  Simple, no need for additional indication ;
  The BW that can be used by the Co-RTWT requesting AP for LLT may be limit.
  Possible cases:
    The P20 channels of the Co-RTWT requesting AP and the Co-RTWT coordinated AP are not aligned, the Co-RTWT coordinated APs may initiate TXOPs with no overlapped BW with the P20 of the Co-RTWT requesting AP to avoid the termination of their TXOP or else terminate the TXOPs whose BW are overlapped with the P20 of the Co-RTWT requesting AP before the start time of Co-RTWT SPs ;
    The P20 of the Co-RTWT requesting AP and the Co-RTWT coordinated AP are aligned, the Co-RTWT coordinated APs may initiate a TXOP by NPCA before the start time of the Co-RTWT SPs and do not need to terminate it.

## Slide 5: Option 2. Requested BW protection for Co-RTWT SP
A Co-RTWT coordinated AP will terminate the TXOPs that are occupied the BW requested by the Co-RTWT requesting AP to be protected before the start time of Co-RTWT SPs.
  The Co-RTWT requesting AP needs to indicate the protection bandwidth for Co-RTWT SPs ;
  The Co-RTWT requesting AP may access a wider BW for the LLT during Co-RTWT SPs.
  More detail can be found in [3] .
  Possible cases:
    The Co-RTWT coordinated APs may initial TXOPs that is not overlapped with the requested BW of the Co-RTWT requesting AP before the start time of Co-RTWT SPs to avoid the termination of their TXOPs ;
    DSO or enhanced SST can be used when the P20 of a Co-RTWT coordinated AP is not overlapped with the requested BW of the Co-RTWT requesting AP;
    The Co-RTWT coordinated APs may set their NPCA primary channels not overlapped with the requested BW of the Co-RTWT requesting AP and initial TXOPs by NPCA.

## Slide 6: Option 3. SP based NPCA
A Co-RTWT coordinated AP may schedule a NPCA TWT whose SPs are overlapped with the Co-RTWT SPs.
When the Co-RTWT coordinated AP and its associated STAs detect an OBSS transmission during the NPCA TWT SPs (or that will end after the start time of the NPCA TWT SPs), they will switch to the NPCA primary channel for channel access until the end of the SPs.
  It is better for Co-RTWT requesting APs to indicate the expected BW during the Co-RTWT SPs by which Co-RTWT coordinated APs can determine how to set their NPCA primary channel or whether or not to accept to provide the protection for the Co-RTWT SPs.
  more detail can be found in [1], [2].
  Some issues might be introduced while Co-RTWT SP is not fully occupied.

## Slide 7: Summary
  The TXOP termination rules for Co-RTWT coordinated APs are not very clear.
  In some cases, TXOP termination before the Co-RTWT SPs may be unnecessary.
  Options for avoiding the over protection issue in Co-RTWT are discussed.

## Slide 8: SP 1
Do you agree to add the following text to the 11bn SFD?
  with the following exception:
    AP may not end its TXOP that is not overlapped with the Primary 20 MHz channel of the Co-RTWT AP before the start time of the corresponding OBSS rTWT SP(s)
[Motion #149]
If an AP extends the protection of the rTWT schedule of another AP, following negotiation or through other means, then:
  The AP shall ensure its TXOP ends before the start time of the corresponding OBSS rTWT SP(s)
  The AP, if it has at least one associated STA that is capable of rTWT, shall advertise in the beacon frames it transmits the OBSS rTWT schedule so that its associated STAs supporting rTWT follow the baseline rTWT rules for the OBSS rTWT schedule.

## Slide 9: SP 2
Do you agree to add the following text to the 11bn SFD?
  with the following exception:
    AP may not end its TXOP that is not overlapped with the protected BW requested by the Co-RTWT AP before the start time of the corresponding OBSS rTWT SP(s)
[Motion #149]
If an AP extends the protection of the rTWT schedule of another AP, following negotiation or through other means, then:
  The AP shall ensure its TXOP ends before the start time of the corresponding OBSS rTWT SP(s)
  The AP, if it has at least one associated STA that is capable of rTWT, shall advertise in the beacon frames it transmits the OBSS rTWT schedule so that its associated STAs supporting rTWT follow the baseline rTWT rules for the OBSS rTWT schedule.

## Slide 10: References
[1] 11-24-0538-01-00bn-sp-based-non-primary-channel-access
[2] 11-24-1259-02-00bn-sp-based-non-primary-channel-access-follow-up
[3] 11-24-1577-01-00bn-non-primary-channel-access-during-r-twt-coordination