## Slide 1: Discussion on buffered data deliver
Name | Affiliations | Address | Phone | email
Hang Yang | Ruijie Networks Co., Ltd. |  |  | yanghang1@ruijie.com.cn
Ke Zhong | Ruijie Networks Co., Ltd. |  |  | zhongke@ruijie.com.cn
Hui Che | Ruijie Networks Co., Ltd. |  |  | chehui@ruijie.com.cn
Fangchang Guo |  |  |  | 
Date: 2024-12-27
Authors:

## Slide 2: Background
The following text has already been included into TGbn SFD[1]:
As part of the seamless roaming procedure, during roaming,
– after the request/response exchange that initiates notification of the DS mapping change from the current AP MLD to the target AP MLD,
• The current AP MLD may deliver buffered DL data frames for a TBD period of time.
• The non-AP MLD may retrieve buffered DL data frames from the current AP MLD
• The non-AP MLD may send UL data to target AP MLD.
• It is assumed that the target AP MLD is able to deliver data frames to non-AP MLD after the DS mapping change
– The current AP MLD may forward DL data to the target AP MLD.
• When and how to initiate the forwarding of DL data is TBD
[Motion #27]

## Slide 3: Introduction
In TGBn SFD[1], the buffered DL data transfer between current AP MLD and non-AP MLD after DS mapping change is supported to avoid data loss.
In[2,3,4], the buffered DL data transmission may not always being fully supported. During the transmission, the bad link quality between current AP MLD and non-AP MLD may cause transmission failure, thus weakening the effect of buffered DL data transmission.
In this contribution, we would like to discuss some details about enhancing stability when buffered DL data transfers after DS mapping change.

## Slide 4: Recap : buffered DL data transmission in roaming
AP2
AP1
STA
AP 1
(Current AP)
AP 2
(Target AP)
Roaming Request
Context transfer
DS mapping change
Roaming Response
Buffered DL data transmission
DL data from AP2
Link1 disable
Preparation / Link set up Phase
Buffer is cleared
or Reach Timeout
In [5], current AP MLD and non-AP MLD continue to transfer the buffered DL data after DS mapping change in order to avoid data loss.
  In single link case, STA can only communicate with current AP until the buffer of current AP is cleared or timeout is reached.
  In dual link case, STA would leave one link to communicate with current AP until the buffer of current AP is cleared or timeout is reached.
As [3,4] point out, the bad quality link may cause a higher transmission failure issue, and even get no much gain from buffered transmission.
  Considering that the buffered DL data transmission is performed during roaming procedure, the link1 condition between STA and current AP may be less than ideal and may even get worse.

## Slide 5: Discussion on buffered DL data transmission
To improve the stability of transmission, during the buffered DL data transmission, STA could measure the link status and provide feedback to current AP.
Option 1: Based on STA’s measured result, STA may send a leaving request signaling to current AP, requesting to terminate the buffered DL data transmission and switch to target AP immediately.
  Conditions that STA send leaving request may include: ▶ RSSI of Link1 (STA- AP1) is lower than a threshold ▶ RSSI of Link2 (STA-AP2) is much higher than Link1 (if STA could measure the Link2) ▶ Other TBD conditions may cause transmission failure
  After receiving Leaving Request from STA, current AP could instruct STA to disconnect the link1.
  Current AP could forward unsent buffered data to Target AP (if supported).
STA
AP 1
(Current AP)
Buffered data frame
Link1 disable
Roaming Request
Context transfer
DS mapping change
Roaming Response
ack
E.g., RSSI lower than threshold
Leaving Request
Data forward
Communicate with Target AP2
Buffered data transmission

## Slide 6: Discussion on buffered DL data transmission
Option 2: STA provides the measured result to current AP, and the AP decide to terminate the buffered DL data transmission or continues to transfer.
  When link feedback from STA is not suitable for transmission, current AP could instruct STA to disconnect the link1.
  Conditions that current AP decide to terminate transmission may include: ▶ RSSI of Link1 (STA- AP1) is lower than a threshold ▶ RSSI of Link2 (STA-AP2) is much higher than Link1 (if Link2 feedback is available) ▶ Other TBD conditions may cause transmission failure
  Current AP could forward unsent buffered data to Target AP (if supported).
STA
AP 1
(Current AP)
Buffered data frame
Link1 disable
Roaming Request
Context transfer
DS mapping change
Roaming Response
Ack with link feedback
Data forward
Ack with link feedback
Ack with link feedback
  To reduce the impact on data transmission, the feedback from STA could be sent as part of header (e.g., in A-Control field).
Communicate with Target AP2
Buffered data transmission
AP decide to terminate transmission

## Slide 7: Summary
In this contribution, we discussed the details on buffered data transmission during roaming
  During buffered data transmission, STA could measure the link quality and provide feedback to current AP. This will contribute to current AP terminate the buffered data transmission at the appropriate time and avoid poor links affecting transmission.
    Option 1: Based on STA’s measured result, STA may send a request to current AP, requesting to terminate the buffered DL data transmission and switch to target AP immediately.
    Option 2: STA provides the measured result to current AP, and AP decide to terminate the buffered DL data transmission or continues to transfer.
  The feedback from STA may be sent as part of header to reduce the impact on data transmission.

## Slide 8: References
[1] IEEE 802.11-24/0209r7, Specification Framework for TGbn
[2] IEEE 802.11-24/0655r0, Thoughts on SMD Roaming and FT Roaming
[3] IEEE 802.11-24/1476r0, Seamless roaming follow up
[4] IEEE 802.11-24/934r1, Some thought on the data plane of seamless roaming