## Slide 1: MAPC discovery follow up

## Slide 2: Introduction
11bn group agreed on the action frame for MAPC Discovery and the UHR AP is capable of transmitting a TB PPDU with the following motion:
  A UHR AP shall indicate to another AP its capability to respond in a TB PPDU or not[M #120]
  When an AP use Management frames to discover the capabilities and/or parameters of individual M-AP coordination schemes, the AP shall use the defined MAPC Public Action frame with the following setting:[M#359]
  • The action field is set to MAPC Discovery
In this contribution, we propose to define a TB MAPC Discovery procedure

## Slide 3: Recap: M-AP discovery procedure
The characteristic of MAPC discovery procedure
  The purpose of MAPC discovery is to find another AP in the same or the overlapping channel.
  The discovery request and response frame may be only exchanged on their operating channel.
  Possibly to allow the off-channel scan to support the use cases in some special scenario(one AP plans to switch to another channel, also, the off-channel scan operation may be requested by STA for P2P operation).
  In this contribution, we focus on the M-AP scan operation on the current operating channel.
In MAPC, one AP may discover another AP via the MAPC discovery action frame exchange.
  In active scan, one AP may send broadcast discovery request frame, and receives the discovery response frame one by one in different TXOPs, in which a serious overhead issue may happen

## Slide 4: The following figure depicts the overhead issue in actively discovery procedure
discovery
request
discovery
response
T
AP1 AP2 AP3 AP4 AP5
TXOP1
TXOP2
TXOP3
TXOP4
TXOP5
discovery
response
discovery
response
discovery
response

## Slide 5: Propose to define Trigger-based M-AP discovery procedure
Leverage the gain of RA-RU, the initiating AP may transmit a TB frame including multiple RA-RU for the responding AP without AP ID.
  The responding APs that don’t support transmitting TB PPDU won’t make the response.
  Also, the AID12 field can set to AP ID if the target responding AP obtained the AP ID from initiating AP before.
  MAPC discovery request and TB frame can be merged to one frame(like reusing TRS control field or define a new MAPC discovery request polling frame(DRP)).

## Slide 6: The following figure depicts one approach of Trigger Based actively scan procedure(RU size=242-tone)
Note: RU size in DRP may smaller or larger than 242-tone

## Slide 7: Summary
Analysis the characteristic of discovery procedure in MAPC scheme
Propose to define a TB discovery request/response frame exchange to avoid overhead issue.
  Only the responding APs that are capable of transmitting TB PPDU can make the response.
  AID12 field in the Trigger frame can set to RA-RU or set to the responding AP’s AP ID

## Slide 8
THANK YOU 

## Slide 9: Reference
24/209r6 TGbn Specification Framework for TGbn
24/1762r13 PDT-MAC-NPCA

## Slide 10: SP1
Do you agree to define Trigger based MAPC discovery procedure?