## Slide 1: AP ID in NDPA signaling

## Slide 2: Introduction
In Co-BF,11bn agreed on two new sounding sequences: Joint sounding and sequential sounding.
  In Joint/(cross-BSS)Sequential sounding, the NDPA solicits the NDP from the responder AP , and solicits the associated STA receiving the NDP.
  In In-BSS Sequential sounding, the NDPA only solicits the associated STA receiving the NDP.
Conclusion: The NDPA may contain both AP identifier(like AP ID) and STA identifier(like AID)
In this contribution, we would like to discuss the AP ID design in NDPA

## Slide 3: AP ID and AID collision issue in NDPA
Need to well design the new signaling on NDPA to backward compatible with EHT STA.
  The NPDA may silicate either EHT STA or UHR STA,but the new signaling design in NPCA is not visible to EHT STA.
  If AP ID is in AID11 and has the same value with one assigned AID of a EHT STA, EHT STA may decode the AP ID as AID and make the wrong decoding in the sequential subfield.
  If we define the rule to disallow AP ID and AID to be same on one link, the adding link operation via ML reconfiguration may be failure.

## Slide 4: The following figure depicts the adding link failure issue if only consider the different AP ID and AID value on one link
AP1
STA3
AP2
AP3
STA2
AID=10
AID=10
AP MLD
non-AP MLD
AP1
STA3
AP2
AP3
STA2
AID=10
AID=10
AP MLD
non-AP MLD
AP22
AP ID=10
Non-AP MLD can’t add link on link1 via ML reconfiguration, as the value of 10 is a AP ID on link1, can’t be used as AID any more.
STA1
T1
T2
T3

## Slide 5: All possible solution to address the AP ID and AID collision issue
  Opt1: (Link level AP ID) The value of AP ID and AID shall be different on one link, disable the function of adding link operation via ML reconfiguration in UHR (not good).
  Opt2: Define MLD level AP ID (Preferred).
  Opt3: (Link level AP ID) The value of AP ID can be same to the AID on one link, use two IDs approach to differentiate AP ID from AID if AP ID and AID appear in one frame(like NDPA).

## Slide 6: Opt2: define MLD level AP ID
AP shall ensure that the AP ID value is not assigned by the AP or by its affiliated MLD to the STAs as bellow
  E.g. STA is an associated non-AP STA, an unassociated non-AP STA that has been allocated a RSID , or any other coordinated AP
  The AP ID value is greater than 2^n in MBSSID case as 1-2^n are reserved for MBSSID index(be carefully to use such range).

## Slide 7: Opt3: The proposal of AP ID design in NDPA
In one STA Info field, one Reserved AID(like AID 2042) is filled in AID11 and AP ID or responder AP’s BSS color is filled in AP ID field if the responder AP’s information is included.
e.g. 0b0010

## Slide 8: The proposal of AP ID design in Trigger frame
In M-AP Trigger frame, the AID12 field used to identify each shared AP.
  Quoted the passed motion as bellow:
    The sharing AP, that transmits a Trigger frame as part of a transmission sequence in a Multi-AP coordinated transmission scheme, identifies the shared AP via an AP ID carried in the AID12 field of the User Info field of the frame
    Note: the name of "sharing AP" and "shared AP" are TBD
    Note: Multi-AP coordinated transmission schemes are Co-SR, Co-BF and Co-TDMA
    [Motion #135]]
If a M-AP Trigger frame solicits the response from both AP and STA, the MSB of AID12 subfield can differentiate AP ID from AID.
  The MSB of the AID12 subfield is set to 1 to indicate the AP ID
  The MSB of the AID12 subfield is set to 0 to indicate the AID（baseline）
e.g. 0b10....010

## Slide 9: Summary
Analysis the potential AP ID and AID collision issue in NDPA
Analysis the potential non-AP MLD adding link failure issue due to the AP ID and AID collision issue.
Propose three possible options as bellow:
  Opt1: (Link level AP ID)The value of AP ID and AID shall be different on one link, disable the function of adding link operation via ML reconfiguration in UHR.
  Opt2: Define MLD level AP ID.
  Opt3: (Link level AP ID) The value of AP ID can be same to the AID on one link, use two IDs approach to differentiate AP ID from AID if AP ID and AID appear in one frame(like NDPA)

## Slide 10
THANK YOU 

## Slide 11: Reference
24/209r6 TGbn Specification Framework for TGbn
24/2028r1 PDT-Joint-Sounding procedure

## Slide 12: SP1
As a part of M-AP coordination agreement procedure, an AP may assign an AP ID to another AP with the following constraints:
The AP ID field has the same size and the field value has a range as defined in AID field (see 9.4.1.8)
AP shall ensure that the AP ID value is not assigned by the AP or by its affiliated MLD to any other STA (e.g., STA is an associated non-AP STA, an unassociated non-AP STA that has been allocated a RSID , or any other coordinated AP), or a non-AP MLD that is associated with the AP MLD
The AP ID value is greater than 2^n where n is the maximum of the value carried in the MBSSID Indicator (n) field of the Multiple BSSID element for any AP affiliated with AP of the AP MLD that belongs to a multiple BSSID set

## Slide 13: SP2
Do you agree the following red field design when the responder AP’s information is included in NDPA?
  AID11 field is filled with a Reserved AID. the value of Reserved AID is TBD.
  AP ID field is filled with the responder’s AP ID, the length is TBD.
Reserved AID: 2042
other TBD information
responder AP ID or BSS color
Bits: 11 11 or 6 10 or 15
AID11 AP ID
STA Info field