## Slide 1: An optimization for NPCA
Date: 2025-01-02
Authors:
Name | Affiliation | Address | Mail
Xiangxin Gu | Spreadtrum | Spreadtrum Center, Lane 2288, Zu Chongzhi Road, Shanghai | Xiangxin.gu@unisoc.com
Yingqiao Quan | Spreadtrum |  | Yingqiao.quan@unisoc.com
Lei Zhou | H3C |  | zhou.leiH@h3c.com

## Slide 2: Recap
TGbn defines a mode of operation that enables a STA to access the secondary channel while the primary channel is known to be busy due to OBSS traffic or other TBD conditions.
  The mode of operation shall not assume that the STA is capable to detect or decode a frame and obtain NAV information of the secondary channel concurrently with the primary channel.
  A BSS shall only have a single NPCA primary channel (name TBD) on which the STA contends while the primary channel of the BSS is known to be busy due to OBSS traffic or other TBD conditions.
An NPCA STA shall initiate frame exchange on the NPCA Primary channel with an NPCA Initial Control Frame in the non-HT PPDU or non-HT duplicate PPDU format using a rate of 6 Mb/s, 12 Mb/s, or 24 Mb/s
  Details on NPCA ICF are TBD
The event that triggers switching to the NPCA primary channel shall be
  OBSS Control frame exchange (e.g., (MU-)RTS/CTS) or
  OBSS HE/EHT/UHR PPDU
  Note: Other conditions TBD
We have made a good progress on NPCA. This contribution provides one possible condition to trigger switching to the nonprimary channel.

## Slide 3: Issues in NPCA
A STA that accesses the BSS primary channel and transmits to its associated AP will encounter transmission failure and invoke error recovery procedure during the AP switch to the NPCA primary channel.
  The STA may access the BSS primary channel subject to its location .
  The transmission failure may even lead to the STA downgrading its transmission rate.
NPCA transmission may fail if there is a STA accessing the BSS primary channel with BW overlapping NPCA channel.
  Same scenario as previous one.
The target STA of an NPCA transmission may not be on the NPCA primary channel.
  With ICF on the NPCA channel first, more questions:
    What’s the next behavior if no ICR received ?
    How to set the duration field in ICF ?

## Slide 4: Solution
The AP sends a CTS frame on the BSS primary 20 MHz with limited TX power, if the least NPCA switching delay gives the AP the chance.
  To block STAs not switching to the NPCA primary channel from sending to the AP.
  To indicate NPCA STAs to switch to the NPCA primary channel.
    A reserved bit in CTS can be used to the indication.
  The CTS has little harm to the OBSS PPDU transmission.

## Slide 5: SP
Do you agree to that the AP sends a CTS frame on the BSS primary 20 MHz channel at the time it decides to switch to the NPCA primary channel if the least switching delay gives the AP the chance?
  The CTS frame is to block STAs not switching to the NPCA primary channel from sending to the AP.
  The CTS frame is to indicate NPCA STAs to switch to the NPCA primary channel.

## Slide 6: References
[1] 11-24-0171-25-00bn-tgbn-motions-list-part-1.pptx Alfred Asterjadhi
[2] 11-24-1762-13-00bn-pdt-mac-npca.docx Matthew Fischer