## Slide 1: Discussion on AMP Energizer: Function and Operation Frequency
Date: 2025-01-07
Authors:
Name | Affiliation | Address | Phone | Email
Yinan Qi | OPPO |  |  | v-qiyinan@oppo.com
Weijie Xu |  |  |  | 
Chuanfeng He |  |  |  | 
Doc.: IEEE 802.11-25/0010r0
January 2025

## Slide 2: Abstract
In this contribution, we discuss the function and operation frequencies of AMP energizers.
Doc.: IEEE 802.11-25/0010r0

## Slide 3
Recap of Energizer Definition [1]
  Integrated Type A: AP and energizer are integrated
    AP can operate in both 2.4G and S1G frequency bands
    No signalling exchange between AP and energizer
  Independent Type B: energizer is an independent device
    Wired/wireless connection between AP and energizer
    Signalling between AP and energizer
  Energizer functions: at least excitation, WPT and wakeup [1]-[2]
Yinan Qi (OPPO)
Slide 3
Doc.: IEEE 802.11-25/0010r0
January 2025

## Slide 4
AP and Energizer Type
  AP
    Type-A, Single frequency: 2.4GHz
    Type-B, Dual frequency: 2.4GHz and S1G
    Type-C, Single frequency: S1G
  Energizer
    Type-1, Dual frequencies: 2.4G for communication and excitation, S1G for communication and WPT
    Type-2, Single frequency: S1G for WPT only (must be wired connected with AP)
    Type-3, Single frequency: S1G for communication and WPT
    Type-4, Single frequency: 2.4GHz for communication and excitation
    Type-5, Dual frequency: 2.4G for communication and excitation and S1G for WPT only
Yinan Qi (OPPO)
Slide 4
Doc.: IEEE 802.11-25/0010r0
January 2025

## Slide 5
AP and Energizer Type
  Three main functions for energizer
    Communication
      Between energizer and AMP non-AP STAs, e.g., wakeup signal
      Between AP and energizer via legacy interface
    Excitation: activation and backscattering
    WPT
  Type 1 energizer is the most complicated
  Type 2 to 5 energizers’ functions sets are subsets of type 1 energizer with reduced complexity and cost
  Two operation frequencies including 2.4GHz and S1G
    2.4GHz for communication and excitation
    S1G for WPT and communication
  Different AP type and energizer type can be paired
Yinan Qi (OPPO)
Slide 5
Doc.: IEEE 802.11-25/0010r0
January 2025

## Slide 6
AP and Energizer Pair 1
  Pair 1: Type-A AP + Type-5 energizer
    Communication at 2.4GHz
      WPT protocol
        AP and energizer: AP controlling energizer signalling
        AP and AMP non-AP STAs: e.g., EH capability feedback
      Configuration of Energizer Tx
        Excitation signal: energizer excites AMP devices
        Wakeup signal: energizer wakes up AMP devices
    Excitation at 2.4GHz
      Energizer sending excitation signals to AMP devices
    WPT at S1G
      Energizer wireless charging signal to AMP devices
Yinan Qi (OPPO)
Slide 6
Doc.: IEEE 802.11-25/0010r0
January 2025

## Slide 7
AP and Energizer Pair 2
  Pair 2: Type-A AP + Type-4 energizer
    Communication at 2.4GHz
      WPT protocol
        AP and energizer: AP controlling energizer signalling
        AP and AMP non-AP STAs: e.g., EH capability feedback
      Configuration of Energizer Tx
        Excitation signal: energizer excites AMP devices
        Wakeup signal: energizer wakes up AMP devices
    Excitation at 2.4GHz
      Energizer sending excitation signals to AMP devices
    WPT at S1G
      Energizer wireless charging signal to AMP devices
    No S1G thus no WPT protocol or WPT signal
    Reduced complexity and cost for 2.4GHz deployment only
Yinan Qi (OPPO)
Slide 7
Doc.: IEEE 802.11-25/0010r0
January 2025

## Slide 8
AP and Energizer Pair 3
  Pair 3: Type-B AP + Type-3 energizer
    Communication at S1G, e.g., 802.11ah
      WPT protocol
        AP and energizer: AP controlling energizer signalling
        AP and AMP non-AP STAs: e.g., EH capability feedback
      Configuration of Energizer Tx
        Excitation signal: energizer excites AMP devices
        Wakeup signal: energizer wakes up AMP devices
    Excitation at S1G
      Energizer sending excitation signals to AMP devices
    WPT at S1G
      Energizer wireless charging signal to AMP devices
    Co-existence of WPT signal and 802.11ah signal in S1G needs to be considered
Yinan Qi (OPPO)
Slide 8
Doc.: IEEE 802.11-25/0010r0
January 2025

## Slide 9
AP and Energizer
  Prioritize pair 1 and 2 considering different energizer capability, e.g., some of them may only work in 2.4GHz due to simplicity and cost.
  Pair 3 can be further studied for future S1G
  Backscattering mode
    Coordinated DL PPDU transmission by AP and energizer may not be feasible
      Very different Rx power from AP and energizer due to different Tx power, distance, etc., may be challenging for very simple Rx circuit of AMP devices.
      AP may not know the exact excitation field length, e.g., AP has no information of UL payload size.
    Energizer is expected to be relatively complicated, thus able to transmit entire DL PPDU
    Need to clarify what energizers can do.
Yinan Qi (OPPO)
Slide 9
Doc.: IEEE 802.11-25/0010r0
January 2025
Excitation
SYNC
SIG
Data
Excitation
Preamble

## Slide 10: Reference
[1] “Further Consideration of WPT for AMP,” IEEE 802.11-24/1781r2, Nov. 2024
[2] “Further Discussion on the AMP WPT Protocol,” IEEE 802.11-24/1769r0, Nov. 2024
Doc.: IEEE 802.11-25/0010r0
January 2025

## Slide 11: SP 1
Doc.: IEEE 802.11-25/0010r0
January 2025
  Energizer should be allowed to transmit the entire DL PPDU when configured by the AP.