## Slide 1: Co-RTWT follow up
Date: 2025-1-22
Authors:
Name | Affiliation | Address | Mail
Xiangxin Gu | Spreadtrum | Spreadtrum Center, Lane 2288, Zu Chongzhi Road, Shanghai | Xiangxin.gu@unisoc.com
Yingqiao Quan | Spreadtrum |  | Yingqiao.quan@unisoc.com
Lei Zhou | H3C |  | 

## Slide 2: Recap
TGbn has made progress on Co-RTWT with following motions passed.
[Motion #48, [1]]
Define mechanisms that enable APs to coordinate their rTWT schedule(s) and/or to ensure that one AP provides the protection of the rTWT schedule(s) of the other AP.
NOTE – TBD mechanisms including negotiation between 2 APs and advertisement.
[Motion #149, [1]]
If an AP extends the protection of the rTWT schedule of another AP, following negotiation or through other means, then:
  The AP shall ensure its TXOP ends before the start time of the corresponding OBSS rTWT SP(s)
  The AP, if it has at least one associated STA that is capable of rTWT, shall advertise in the beacon frames it transmits the OBSS rTWT schedule so that its associated STAs supporting rTWT follow the baseline rTWT rules for the OBSS rTWT schedule.

## Slide 3: More considerations on Co-RTWT
A BSS may have R-TWT SPs that are time overlapped with OBSS R-TWT SPs requiring Co-RTWT protection.
Proposal: Co-TDMA or Co-SR or Co-BF may be negotiated to be used during the overlapped periods.
  Co-RTWT negotiation may piggyback some information for the Co-TDMA/Co-SR/Co-BF.

## Slide 4: More considerations on Co-RTWT
A non-AP STA in a BSS may have different OBSS R-TWT SPs with the AP, subject to its location.
  In the following figure, STA21 may suffer from packet loss during R-TWT SPs of BSS1, which is not protected in BSS2.
AP1
AP2
STA21
STA22
STA23
STA11
Proposal: a non-AP STA may indicate its associated AP OBSS R-TWT SPs if the SPs are not protected by the AP.
  RCPI of the OBSS Beacon frame may be included in the indication for sake of spatial reuse.

## Slide 5: More considerations on Co-RTWT
Overprotection is a drawback and may be avoided by spatial reuse.
  In the following figure, AP1 and STA11 may have frame exchange with spatial reuse above transmission from AP2 to STA23 during the corresponding R-TWT SPs of BSS2, which is protected by AP1 based on Co-RTWT.
AP1
AP2
STA21
STA22
STA23
STA11
Proposal: A non-AP and its associated AP may have frame exchange via spatial reuse during Co-RTWT protected OBSS R-TWT SPs.
  For the spatial reuse operation, RCPI of the OBSS Beacon frame is included in the BSS Beacon frame.

## Slide 6: More considerations on Co-RTWT
In general, the BSS R-TWT SP that is scheduled to protect an OBSS R-TWT SP is ahead of the OBSS R-TWT SP because of 1 TU granularity of R-TWT wake time.
No LLT to be transmitted in the R-TWT SP usually.
How to avoid the wasting?
Proposal: Non-LLT may be transmitted in the R-TWT SP that is scheduled to protect an OBSS R-TWT SP.

## Slide 7: More considerations on Co-RTWT
In general, 1 TU quiet interval can’t be scheduled right at the start time of the OBSS R-TWT SP because of 1 TU granularity of the start time of the quiet interval.
How to protect an OBSS R-TWT SP from accessing the channel by STAs that don’t support R-TWT ?
Proposal: The AP starts a transmission in the R-TWT SP with frame exchange ending before the OBSS R-TWT SP wake time and TXOP ending at 1 TU after the OBSS R-TWT SP wake time.

## Slide 8: Summary
In this contribution, following considerations are discussed for Co-RTWT.
  Co-TDMA/Co-SR/Co-BF may be used during overlapped period of BSS and OBSS R-TWT SPs.
  A non-AP STA may suffer from unprotected OBSS R-TWT SPs.
  Overprotection is a drawback and may be avoided by spatial reuse.
  Granularity issue in Co-RTWT and solutions.

## Slide 9: SP 1
Do you agree to add the following text to the 11bn SFD?
Co-TDMA or Co-SR or Co-BF may be negotiated to be used for Co-RTWT during the overlapped period of BSS R-TWT SPs and OBSS R-TWT SPs.

## Slide 10: SP 2
Do you agree to add the following text to the 11bn SFD?
A non-AP STA may indicate its associated AP OBSS R-TWT SPs if the SPs are not protected by the AP.

## Slide 11: SP 3
Do you agree to add the following text to the 11bn SFD?
A non-AP and its associated AP may have frame exchange via spatial reuse during Co-RTWT protected OBSS R-TWT SPs.

## Slide 12: SP 4
Do you agree to add the following text to the 11bn SFD?
Non-LLT may be transmitted in the R-TWT SP that is scheduled to protect an OBSS R-TWT SP.

## Slide 13: SP 5
Do you agree to add the following text to the 11bn SFD?
To protect an OBSS R-TWT SP, the BSS AP starts a transmission in the R-TWT SP with frame exchange ending before the OBSS R-TWT SP wake time and TXOP ending at 1 TU after the OBSS R-TWT SP wake time.

## Slide 14: References
[1] 11-24-0171-21-00bn-tgbn-motions-list-part-1, Alfred Asterjadhi (Qualcomm Technologies Inc.)
[2] 11-23-2212-01-00bn-R-TWT-protection-in-11bn, Xiangxin Gu(Spreadtrum)
[3] 11-24-1457-00-00bn-r-twt-sharing, Gaius Wee (Panasonic)