## Slide 1: Dynamic Power Save Operation for Sounding Procedure
Date: 2025-03-11
Authors:

## Slide 2: Introduction
Dynamic power saving (DPS) is one of the features being considered for 802.11bn. TGbn has agreed to define:
  A power save (PS) mode for a STA wherein the STA may transition from a lower capability (LC) mode to a higher capability (HC) mode upon reception of an ICF (Mar. 2024).
We consider a DPS assisting AP that intends perform sounding procedure with a DPS non-AP STA while the DPS non-AP STA initially operates in the LC mode. The DPS non-AP STA transitions from the LC mode to the HC mode to complete the sounding procedure.

## Slide 3: Sounding Procedure during DPS Operation
A DPS assisting AP (AP1) intends to perform a sounding procedure with a DPS non-AP STA (STA1) to transmit traffic using transmitter beamforming (or DL MU-MIMO).
The AP1 may transmit an ICF to the STA1, so that the STA1 transitions from the LC mode to a HC mode.
While the STA1 operates in the HC mode, the AP1 then transmits an NDP Announcement (NDPA) followed by a NDP to initiate a sounding sequence (e.g., an EHT non-TB sounding sequence).
Problem
  STA1 that receives NDPA during the HC mode may spend full receive power. As such, power efficiency of DPS non-AP STA operating in PS mode is reduced.
  Since the ICF already start the TXOP for sounding procedure, it is redundant to send a separate NDPA frame to initiate the sounding procedure.

## Slide 4: DPS Operation for Sounding Procedure (Solution)
A DPS assisting AP (AP1, beamformer) sends an NDPA to a DSP non-AP STA (STA1, beamformee).
  The NDPA requests the STA1 for transitioning from the LC mode to the HC mode.
  The NDPA further announces a NDP to be transmitted by the AP1 to the STA1, after the STA1 transitions to the HC mode.
The STA1 receives the NDPA and transitions from the LC mode to the HC mode during a padding of the NPDA and a following SIFS .
  After receiving the NDPA, the STA1 receives the NDP while operating in the HC mode.
  The STA1 responses a BF/CQI report to the AP1 SIFS after receiving the NDP.

## Slide 5: Summary
In this contribution, we shared some thoughts of DPS operation for sounding procedure.
  An DPS assisting AP initiates a sounding procedure while a DPS non-AP STA operates in a LC mode by using an NDPA frame operating as an ICF.

## Slide 6: Straw Poll
SP1. Do you support defining a DPS operation that includes the following?
  While a DPS non-AP STA (beamformee) operates in a lower-capability mode, a DPS assisting AP (beamformer) may initiate a sounding procedure using a NDPA that operates as an ICF. The NDPA announces that a sounding NDP will be transmitted by the DPS assisting AP and solicits the DPS non-AP STA a transition from a lower capability mode to a higher capability mode to receive the sounding NDP.
  Yes
  No
  Abstain

## Slide 7: References
Draft P802.11bn D0.1
Draft P802.11be D7.0
24/0209r9: Specification Framework for TGbn, Ross Jian Yu (Huawei)
24/2016r3: PDT MAC Power Save, Liwen Chu (NXP)
24/1987r2: Detailed text proposal for dynamic power save and eMLSR, Liwen Chu (NXP)
23/1875r1: Power save proposal for non-AP/mobile-AP, Shubhodeep Adhikari (Broadcom)
23/1965r2: Dynamic power save follow-up, Alfred Asterjadhi (Qualcomm)
23/2003r1: Client power save, Laurent Cariou (Intel)