## Slide 1: UL Data rates for AMP
Date: 2024-11-09
Authors:
Name | Affiliation | Address | Phone | Email
Weijie Xu | OPPO |  |  | xuweijie@oppo.com
Wang Ke |  |  |  | 
Shengjiang cui |  |  |  | 
Chuanfeng He |  |  |  | 
Yinan Qi |  |  |  | 
Jinyu Zhang |  |  |  | 
Zhisong Zuo |  |  |  | 
Doc.: IEEE 802.11-25/0033r0
Jan. 2025

## Slide 2: Abstract
In this submission, we further discuss the UL date rate for AMP and give our proposals.
Doc.: IEEE 802.11-25/0033r0

## Slide 3
Weijie Xu (OPPO)
Slide 3
Doc.: IEEE 802.11-25/0033r0
Jan. 2025
  In November meeting last year, the DL data rate is agreed in the following motion:
  Move to include the following content to sub-clause 4 of SFD:
  The AMP Downlink PPDU in 2.4 GHz shall support the following data rates:
    1 Mb/s (for non-Backscatter STAs only)
    250 kb/s
  [Reference DCN# 11-24/1793r1]
Recap: DL data rate for AMP

## Slide 4
Weijie Xu (OPPO)
Slide 4
Doc.: IEEE 802.11-25/0033r0
Jan. 2025
  When determining data rates, the following needs to be taken into account:
    Use cases
      Both integrated and non-integrated deployment are needed, e.g.,
        For smart home case, it needs integrated deployment
        For kinds of vertical applications, e.g., logistics, fresh food transportation etc., non-integrated deployment are needed to reduce the deployment cost and extend the coverage
          Distributed energizers are much cheaper than AP
    Various Ambient power source
      In some cases, e.g., sensors deployed in factories, light can be used to drive AMP STA thus WPT will not be the coverage bottleneck, the communication coverage can be large.
    Output power from AMP STA
      The transmission power from active device can be as low as -20dBm
      The backscattering power from BC device is even lower, considering BC loss
    For backscattering, the residual interference will affect the data transmission.
Recap: what needs to be considered

## Slide 5
Link budget for UL
Weijie Xu (OPPO)
Slide 5
Doc.: IEEE 802.11-25/0033r0
Jan. 2025
  For active device,
  For integrated case, the link budget for DL = ~65dB[4], X0= 9dB,X1=19dB and X2=29dB.
  For non-integrated case, the link budget for DL = ~90dB[4] (-70dB is assumed as the receiver sensitivity), X2 = -6dB and X3=4dB.
  For BC device,
  The link budget for DL = ~65dB[4] (same as that for active device), X4=-1dB.
Parameter | Active AMP(1) | Active AMP(1) | Active AMP(2) | BC
TX Power(dBm) | -20 | -10 | 0 | -30
Thermal Noise Floor(dBm) (@20MHz) | -101 | -101 | -101 | -101
Noise Figure(dB) | 7 dB | 7 dB | 7 dB | 7 dB
Noise Power Level(dBm) | -94 | -94 | -94 | -94
Required SNR (dB) | X1 | X2 | X3 | X4
Receiver Sensitivity (dB) | -94+X1 | -94+X2 | -94+X3 | -94+X3
Link Budget | 74-X1 | 84-X2 | 94-X3 | 64-X3

## Slide 6
Simulation assumptions for AMP UL
Weijie Xu (OPPO)
Slide 6
Doc.: IEEE 802.11-25/0033r0
Jan. 2025
  Link level simulations are performed for AMP UL data rate evaluations with the following simulation assumptions.
Parameters | Values
Date Rate | 250kpbs/1Mbps/2Mbps/4Mbps
Waveform | OOK
Channel model | Channel B/Channel D
Chip duration | 2µs/0.5µs/0.25µs/0.125µs
Sampling rate at AMP AP | 20MHz
Coding | Manchester
Receiver type | Correlation detection

## Slide 7
Simulation results for AMP UL date rate (Channel B)
Weijie Xu (OPPO)
Slide 7
Doc.: IEEE 802.11-25/0033r0
Jan. 2025

## Slide 8
Simulation results for AMP UL date rate (Channel B)
Weijie Xu (OPPO)
Slide 8
Doc.: IEEE 802.11-25/0033r0
Jan. 2025

## Slide 9
Simulation results for AMP UL date rate (Channel D)
Weijie Xu (OPPO)
Slide 9
Doc.: IEEE 802.11-25/0033r0
Jan. 2025

## Slide 10
Simulation results for AMP UL date rate (Channel D)
Weijie Xu (OPPO)
Slide 10
Doc.: IEEE 802.11-25/0033r0
Jan. 2025

## Slide 11
Impact of channel on OOK decoding
Weijie Xu (OPPO)
Slide 11
Doc.: IEEE 802.11-25/0033r0
Jan. 2025
  Chanel delay spread will make it difficult and even impossible for OOK decoding, especially at high data rate.
    Take 1Mbps as example, 10 sampling for each Manchester chip(assuming 20MHz sampling rate), there may be several high power sampling of in Manchester OFF chip due to delay spread from Manchester ON chip
    OOK signal before experience of channel D
    OOK signal after experience of channel D

## Slide 12
Observations
Weijie Xu (OPPO)
Slide 12
Doc.: IEEE 802.11-25/0033r0
Jan. 2025
  Date rate of higher than 4Mbps is not feasible due to:
    Impact from complicated fading channel (e.g. channel D)
    Maximum clock rate of 8MHz for the AMP device(i.e. active device)
      also considering Manchester coding
  Higher date rate can be achieved for AMP UL due to better receiver and high sampling rate at the AP.
    250kbps/1Mbps/2Mbps and 4Mbps are achievable data rates for AMP UL
    For integrated case, up to 4Mbps is achievable.
    For non-integrated case, lower data rate of 250kbps is needed.
    For long-range backscattering, lower data rate of 250kbps/1MHz is needed.

## Slide 13
Summary and proposals
  In this submission, AMP UL link date rate is evaluated and discussed, considering the following
    Link budget (receiver sensitivity, output power from AMP device), device capability(receiver type, clock capability etc.)
    Interference, impact from propagation channel etc.
  With intensive evaluation and comprehensive analysis, the following are proposed:
    250kbps/1Mbps/2Mbps and 4Mbps are AMP UL data rates.
      4Mbps is only for active AMP device
Weijie Xu (OPPO)
Slide 13
Doc.: IEEE 802.11-25/0033r0
Jan. 2025

## Slide 14
Straw Poll #1
Weijie Xu (OPPO)
Slide 14
Doc.: IEEE 802.11-25/0033r0
Jan. 2025
Do you agree with the following text:
    250kbps/1Mbps/2Mbps and 4Mbps are AMP UL data rates.
      4Mbps is only for active AMP device
Yes
No
Abstain

## Slide 15: Reference
IEEE 802.11-24/0853r0, Design target and device capabilities for AMP IoT
IEEE 802.11-24/1802r0 OOK generation for AMP DL
IEEE IEEE 802.11-24/1237r0 AMP Tag Requirements for Close-range Mono-Static Backscattering
IEEE 802.11-24/1801r1 data rate for AMP
Doc.: IEEE 802.11-25/0033r0
Jan. 2025

## Slide 16: Appendix
Doc.: IEEE 802.11-25/0033r0
Jan. 2025
Model | rms Delay Spread (ns) | Number Of Clusters | Taps/Cluster | Propagation Scenario | Usage Model
A | 0 | 1 | 1 | Flat fading | Gaussian Channel-like
B | 15 | 2 | 5,7 | Indoor Residential | Intra Room, Room to Room
C | 30 | 2 | 10,8 | Indoor Residential/Small Office | Enclosed Offices Meeting, Conference or Class rooms
D | 50 | 3 | 16,7,4 | Indoor Typical Office | Offices – cubes farms, open areas and large classrooms
E | 100 | 4 | 15,12,7,4 | Indoor Large Office/Warehouse | Indoor Hotspots with large rooms
F | 150 | 6 | 15,12,7,3,2,2 | Large Space Indoor (pseudo-outdoor). | Large Indoor Hotspot – Airport
  Indoor spatial channel models
TGn and TGac spatial channel models are adopted as IEEE 802.11ax indoor channel
models [1-2] for link level and system level performance evaluation for indoor scenarios.
The delay spreads and cluster parameters of indoor TGn and TGac spatial channel models
are listed in the Table I.
Table I. Delay spreads and cluster parameters of indoor TGn and TGac channel models