## Slide 1: Sync field for AMP PPDU
Date: 2025-1-10
Authors:
Name | Affiliation | Address | Phone | Email
Wang Ke | OPPO |  |  | wangke6@oppo.com
Jinyu Zhang |  |  |  | xuweijie@oppo.com
Weijie Xu |  |  |  | v-qiyinan@oppo.com
Yinan Qi |  |  |  | 
Sehngjiang Cui |  |  |  | 
Doc.: IEEE 802.11-25/0034r2
Jan. 2025

## Slide 2: Abstract
In this contribution, we will firstly discuss the requirement for the Sync field and then propose candidate sync sequence.
Doc.: IEEE 802.11-25/0034r2

## Slide 3: High-level requirements for AMP sync(1)
In [1]. the following requirements for AMP sync are discussed.
  Different sync sequences for DL/UL for indication.
  Support two different AMP DL rate
    e.g. 1Mbps and 250kbps using 2 different sync
    A correlator can distinguish between Sync length 16 and 32.
  The Sync sequence has the same number of 1 and 0.
  Good auto-correlation
  The sequence have 3 consecutive 1/0, which can help distinguish synchronization field and data field with Manchester coding.
Doc.: IEEE 802.11-25/0034r2

## Slide 4: High-level requirements for AMP sync(2)
During previous meeting, sync field for different receiver type have been discussed.
  For some device type, e.g. close-range dual-mode RFID-like AMP STA, it may not have correlator in the its receiver
Therefore, it needs to consider both receiver types with and without correlator inside.
For the AMP device without correlator, it will use sequence matching for AMP sync field detection.
  False alarm rate is the key metric, which relates to the length of sync sequence
  The sync sequence needs to be decode by the receiver, Manchester coding is necessary to guarantee the decoding performance
Doc.: IEEE 802.11-25/0034r2

## Slide 5: Proposed methodology
Doc.: IEEE 802.11-25/0034r2
In order to fulfill the requirement for both receiver types, the following methodology is proposed:
Step 1: design AMP sync that fulfill the requirements for AMP receiver with correlator
Step 2: check whether sync sequence is applicable for AMP receiver without correlator

## Slide 6: Recap: Auto-Correlation Metrics
For high data rate：[]
For low data rate: [S S]
Local reference sequence:
Doc.: IEEE 802.11-25/0034r2

## Slide 7: Recap: Cross-Correlation Metrics
The Sync sequence will be correlated with other filed of the UL/DL PPDU e.g., random Manchester coding symbols to see the cross-correlation property
  The sync sequence shall maintain low cross-correlation with other filed of UL/DL PPDU
Doc.: IEEE 802.11-25/0034r2

## Slide 8: Sync sequence length(1)
For length 8, the auto-correlation is not so good and cross-correlation with random Manchester symbols become unacceptable.
  One sequence after computer searching is '10001101'
Doc.: IEEE 802.11-25/0034r2
AC_H: -4 AC_L: 2
Cross-correlation with Random Manchester symbols

## Slide 9: Sync sequence length(2)
For length 16, the auto-correlation is better and cross-correlation with random Manchester symbols is good
  One candidate sequence after computer searching is '1100100101011100'
Doc.: IEEE 802.11-25/0034r2
AC_H: -4 AC_L: 2
Cross-correlation with Random Manchester symbols

## Slide 10: Synchronization performance(1)
The synchronization performance is evaluated with the following assumptions:
Doc.: IEEE 802.11-25/0034r2
Parameters | Values
Length of AMP sync sequence | 16
Waveform | DSSS-OOK
Channel model | Channel B
Chip duration | 0.5/1/2µs
Sampling rate at AMP device | 2MHz/8MHz
Receiver type | ED receiver

## Slide 11: Synchronization performance(1)
  Simulation results for 2MHz sampling rate at AMP STA. Note that the sync error is represented as the number of sampling points. The probability of different error samplings are recorded.
Doc.: IEEE 802.11-25/0034r2
Table 1: Sync performance when chip duration is 0.5 µs
Table 2: Sync performance when chip duration is 1 µs
Table 3: Sync performance when chip duration is 2 µs

## Slide 12: Synchronization performance(2)
  Simulation results for 8MHz sampling rate at AMP STA. Note that the sync error is represented as the number of sampling points. The probability of different error samplings are recorded.
Doc.: IEEE 802.11-25/0034r2
Table 4: Sync performance when chip duration is 0.5 µs
Table 5: Sync performance when chip duration is 1 µs

## Slide 13: Impact on decoding performance(1)
  When there is synchronization error, the impact on data decoding performance is evaluated with the following assumptions:
Doc.: IEEE 802.11-25/0034r2
Parameters | Values
Date Rate | 250kpbs/1MHz
Waveform | DSSS-OOK
Channel model | Channel B
Chip duration | 2µs/0.5µs
Sampling rate at AMP device | 2MHz/8MHz
Coding | Manchester
Receiver type | ED receiver
synchronization error | 1 Sampling point

## Slide 14: Impact on decoding performance(2)
  Simulation results for data rate of 250kbps in channel B
Doc.: IEEE 802.11-25/0034r2
Figure 1: DL PPDU decoding performance @sampling rate of 2MHz
Figure 2: DL PPDU decoding performance @sampling rate of 8MHz

## Slide 15: Impact on decoding performance(3)
  Simulation results for data rate of 1Mbps and sampling rate of 8MHz
Doc.: IEEE 802.11-25/0034r2
Figure 3: DL PPDU decoding performance （Channel B）

## Slide 16: Observation
Based on the simulation above, we have the following observations
  For AMP sync field, the synchronization will be affected by:
    Length of sync filed
    Chip duration
    Sampling rate of AMP STA’s receiver
  For AMP sync of length 16, the sync performance for chip duration of 1µs and 2µs is acceptable.
Doc.: IEEE 802.11-25/0034r2

## Slide 17: Summary
In this submission, sync sequence for AMP is discussed. Based on the discussion, the following is proposed.
  Basic sync length is 16, one proposed sequence is
    S1= '1100100101011100’
  Chip duration of sync field is 2 µs or 1 µs .
Doc.: IEEE 802.11-25/0034r2

## Slide 18
Straw Poll #1
Weijie Xu (OPPO)
Slide 18
Doc.: IEEE 802.11-25/0034r2
Jan. 2025
Do you agree with the following text:
  Basic AMP sync length is 16, one proposed sequence is
    S1= '1100100101011100’
  Chip duration of sync field is 2 µs or 1 µs .
Yes
No
Abstain

## Slide 19: Reference
IEEE 802.11-24/1802r0 Sync field for AMP PPDU
Doc.: IEEE 802.11-25/0034r2
Jan. 2025