## Slide 1
Name | Affiliation | Address | Phone | Email
Ian Bajaj | Huawei | Singapore |  | ian.bajaj@huawei.com
Lei Huang |  |  |  | 
Rojan Chitrakar |  |  |  | 
Use Case for AMP STA Reporting
Date: 13 Jan 2025
Notes: Jul 12, 2010
Page 1

## Slide 2
Introduction
AMP STA reporting can provide feedback on the Energizing link, AMP STA energy storage capacity and current energy level [1]-[4].
For the Energizer to coexist on sub1-GHz band, it needs information regarding AMP STAs charging requirements.
  Argument:
    Energizer can be triggered prior to AMP Trigger, without any reporting from the AMP STAs.
    AMP trigger likely will follow a duty cycled approach, and this is deterministic. All energizers can be triggered to be switched on before operational state of the AMP STA.
  Counter:
    Different AMP STAs can have different energy storage capacity, charging efficiency (RF-DC), path loss (distance) to Energizer, mobility and antenna polarization – the AMP STA’s charging needs are granular.
    Duration of Energizing also depends on AMP STA RF-EH sensitivity (limits coverage), and Energizer transmit power limitation (regulatory).
    Without knowledge of these variables, the Energizer deployed may need to be always on, or frequent periodic charging (which can both congest the channel)

## Slide 3
Use Case for AMP STA reporting
AMP STA reporting can optimize periodic energizing by:
  Reducing the on duration
  Reducing the transmission power
Drawbacks to AMP STA reporting:
  AMP STAs that are not charged by the deployed energizers’ periodic transmissions will never charge deployment specific issue that is not solved by AMP STA reporting
  Mobility of AMP STAs may make AMP STA report or its application inaccurate AMP STA reporting frequency has to match mobility, may not be feasible.
AMP STA reporting may therefore be best suited to:
  Stationary AMP STA deployment, or conditioned mobility (every 10mins, at a feasible AMP STA reporting frequency)
  Majority of AMP STAs not at energizing link edge (as seen in simulation to follow)

## Slide 4
Simulation (1/2)
Setup: 1 AP, 1 AMP Energizer, 4 AMP STAs
Assumptions:
  Received power at the AMP STAs includes all losses, namely path loss, antenna polarization, RF harvesting efficiency, etc.
  AP sends a trigger to AMP STAs. AMP STAs sense the channel and transmit, with no collision. The channel sense and transmit durations for each AMP STA are fixed.
  The clock drift/inaccuracy issues are not considered.
  The AMP STA returns to idle state after RX+TX operation.
Tx power of the AMP STA: 100uW [5]
UL Payload: 100 bits @ 1Mbps = 0.1ms (>1Mbps UL data rate maybe supported)
Channel sensing time: 5ms (frame reception ~ 240us @ 250Kbps [11-23/1601r1]
Channel sensing power: 10uW [5]
Idle power: 0.1uW [5]
AMP STA received power (in dBm): Case 1: [-5, -10, -15, -20]; Case 2: [-5, -10, -5, -10]
AMP STA capacitor: 500nF (Total energy storage, =0.25uJ, for a nominal voltage of 1V)

## Slide 5
Total simulation time of 60s
The AP sends out the AMP Trigger every 10s (AMP Trigger Interval)
The WPT waveform is sent based on the implementation method:
  Periodically with a random period
  Periodically based on energy capacity, and idle power consumption of the AMP STA
  On-demand based on energy available (as a percentage of energy capacity), and/or any method to determine periodicity based on RF EH feedback
Simulation (2/2)

## Slide 6
Simulation Results (1/2)
# | Case | Energizer Periodicity | Energizer On Duration (s) | Failed RX+TX events (6) |  |  |  | Dead AMP STAs |  |  | 
 |  |  |  | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4
1 | Energizer with control but no information (randomly decided periodicity) | 200ms every 1s | 12s | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 |  | 20ms every 5s | 0.24s | 5 | 5 | 5 | 5 | 1 | 1 | 1 | 1
2 | Energizer with control and capability information* (fixed periodicity) | 25ms every 1s | 1.5s | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 |  | 25ms every 2s | 0.75s | 5 | 5 | 5 | 5 | 0 | 0 | 0 | 0
3 | Energizer with control and dynamic RF EH feedback (1s – 10s report trigger) | Condition: | 0.62s | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
# | Case | Energizer Periodicity | Energizer On Duration (s) | Failed RX+TX events (6) |  |  |  | Dead AMP STAs |  |  | 
 |  |  |  | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4
1 | Energizer with control but no information (randomly decided periodicity) | 200ms every 1s | 12s | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 |  | 20ms every 5s | 0.24s | 5 | 5 | 5 | 5 | 1 | 1 | 1 | 1
2 | Energizer with control and capability information* (fixed periodicity) | 25ms every 1s | 1.5s | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 |  | 25ms every 2s | 0.75s | 5 | 5 | 5 | 5 | 0 | 0 | 0 | 0
3 | Energizer with control and dynamic RF EH feedback (1s – 10s report trigger) |  | 0.62s | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
AMP STA’s RX power (dBm): [-5, -10, -15, -20]
*Capability information is provided one-time during probing, association or through OOB procedural setup
Enabled by AMP STA Reporting

## Slide 7
Simulation Results (2/2)
# | Case | Energizer Periodicity | Energizer On Duration (s) | Failed RX+TX events (6) |  |  |  | Dead AMP STAs |  |  | 
 |  |  |  | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4
1 | Energizer with control but no information (randomly decided periodicity) | 200ms every 1s | 12s | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 |  | 20ms every 5s | 0.24s | 5 | 5 | 5 | 5 | 1 | 1 | 1 | 1
2 | Energizer with control and capability information* (fixed periodicity) | 25ms every 1s | 1.5s | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 |  | 25ms every 2s | 0.75s | 5 | 5 | 5 | 5 | 0 | 0 | 0 | 0
3 | Energizer with control and dynamic RF EH feedback (1s – 10s report trigger) | Condition: | 0.065s | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
# | Case | Energizer Periodicity | Energizer On Duration (s) | Failed RX+TX events (6) |  |  |  | Dead AMP STAs |  |  | 
 |  |  |  | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4
1 | Energizer with control but no information (randomly decided periodicity) | 200ms every 1s | 12s | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 |  | 20ms every 5s | 0.24s | 5 | 5 | 5 | 5 | 1 | 1 | 1 | 1
2 | Energizer with control and capability information* (fixed periodicity) | 25ms every 1s | 1.5s | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 |  | 25ms every 2s | 0.75s | 5 | 5 | 5 | 5 | 0 | 0 | 0 | 0
3 | Energizer with control and dynamic RF EH feedback (1s – 10s report trigger) |  | 0.065s | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
AMP STA’s RX power (dBm): [-5, -10, -5, -10]
*Capability information is provided one-time during probing, association or through OOB procedural setup
Enabled by AMP STA Reporting

## Slide 8
Simulation Results (for a smaller energy storage capacitor)
# | Case | Energizer Periodicity | Energizer On Duration (s) | Failed RX+TX events (6) |  |  |  | Dead AMP STAs |  |  | 
 |  |  |  | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4
3 | Energizer with control and dynamic RF EH feedback | Condition: | 0.058s (~0.4ms every 0.7s) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
# | Case | Energizer Periodicity | Energizer On Duration (s) | Failed RX+TX events (6) |  |  |  | Dead AMP STAs |  |  | 
 |  |  |  | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4
3 | Energizer with control and dynamic RF EH feedback |  | 0.058s (~0.4ms every 0.7s) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Case B: [-5, -10, -5, -10], 150nF capacitor, 1ms CS time, with rest of the parameters unchanged
Duty cycle of 10s can still be supported (i.e. AMP Trigger interval) with more frequent Energizing (total duration is lesser)
Considerations for AMP STAs with smaller energy storage capacity:
  Appropriate duty cycle (on/off) period that allows the capacitor to fully charge between RX+TX events
  Reducing AMP STA power consumption particularly in idle mode
Without any considerations made for smaller energy storage capacitor, energizer on/off control maybe practically infeasible for low duty cycle setups.

## Slide 9
On average, energizer operational duration savings scaled over a day, can amount to half an hour to several hours (for larger energy capacity AMP STAs) with triggered AMP STA reporting versus one-time capability reporting.
Recap on the energy cost for AMP STA reporting [6]: Idle power consumption (0.1uW @ 1hour = 360uJ) is orders of magnitude larger than RX+TX (60nJ as seen in simulation setup), and is inconsequential for low duty cycle setups.
The duty cycle that can be supported by the AMP STA is proportional to the energy storage capacity, and is bounded by , where is the maximum idle period for an AMP STA, is the energy storage capacity, is the energy consumed by one RX+TX event, and is the idle power consumption.
Energizer duration with only capability information will be based on the worst case AMP STA RF-EH sensitivity, total energy storage capacitor, and idle power consumption. Charging time/on-time can be computed as , where is the AMP STA received power (incl. all losses), expressed in watts. The off duration can be computed as, , where is the idle power consumption (Note: The off duration is not deterministic since the TX-RX power consumption is unknown, without any feedback).
  For =0.25uJ, = 0.01mW (-20dBm), =0.1uW, then =25ms and <2.5s.
Simulation Analysis

## Slide 10
Summary
The use case for AMP STA reporting in the context of WPT was presented, with the most benefits seen for the following scenarios:
  Stationary AMP STA deployment, or conditioned mobility (infrequent mobility, or a feasible AMP STA reporting frequency)
  Majority of AMP STAs not at energizing link edge
Simulation results demonstrate the significant energizing operational duration savings possible with triggered AMP STA reporting, and the need for Energizer control to avoid failed RX+TX events and dead AMP STAs.
Simulation analysis shows that the duty cycle that can be supported for AMP STAs is limited by the energy storage capacitor, and idle power consumption.

## Slide 11: SP
Do you agree to add the following text to TGbp SFD?
IEEE 802.11bp defines a mechanism that allows an AMP STA to report its energy harvesting and power related information. The parameters that are included in the report and how to report such information is TBD.
[Reference: 11-24/1208r1, 11-24/1381r0, 11-24/1524r2, 11-24/1539r0, 11-24/1561r1, 11-24/1769r0, 11-24/1781r2, 11-24/1939r0, 11-25/0038r0]

## Slide 12: References
[1] 11-24/1208r1, Thoughts on the AMP WPT Protocol
[2] 11-24/1381r0, AMP Device Power Status
[3] 11-24/1539r0, Energy-Level Status Reporting for AMP Devices
[4] 11-24/1561r1, AMP Power Budget Negotiation
[5] 11-23/2203r1, Technical Report on support of AMP IoT devices in WLAN
[6] 11-24/1524r2, Follow-up on the AMP WPT protocol