## Slide 1: AMP Mono-static Backscattering Operation
Date: 2025-01-09
Authors:

## Slide 2: Introduction
[1, 2] proposed to reuse EPC Gen2 logical interface and channel access for backscattering tag
  Simplify backscattering tag design
  Facilitate the synergy with UHF RFID tag
In this contribution:
  Discuss about EPC Gen2 logical interface
  Propose the simplified protocol for AMP
  Discuss about the inter-frame space definition

## Slide 3: Recap: High-level Protocol Flow
AMP reuses the logical interface of EPC Gen2 protocol [2]:
  Physical layer  AMP will redefine AMP PHY
  Tag-identification layer  the UHF RFID commands are tunneled via the AMP MAC/PHY layer

## Slide 4: EPC Gen2 Logical Interface [3]
Tag memory definition and access commands
Inventory operation command and flags/state
  Select command: choose certain tags to identify
  Inventory command: identify all Tags
  Sessions, A/B flag per session, Tag state
Advanced operation
  Authentication
  Secured communications

## Slide 5: AMP Backscattering Tag
Tag memory definition and access commands
  Propose no change to the interface, and selective useful commands
Inventory operation
  Propose to reuse most commands
    Query command to be updated based on new AMP PHY
  Comply with TXOP or PPDU limit
    Tag to hold status/flag among read TXOP or PPDU
  Inter-frame space: “link timing”
    To be updated based on AMP PHY definition
Advanced operation
  Propose to support authentication only
  Secured communication does not fit into WiFi: ~100ms

## Slide 6: AMP Reader Commands
Command | Tag support | Remark
Select | mandatory | as EPC Gen2 Reader usage is optional
Query | mandatory | As EPC Gen2 Update based on AMP PHY
Query rep | mandatory | as EPC Gen2
Ack | mandatory | as EPC Gen2
NAK | mandatory | as EPC Gen2
Read | mandatory | as EPC Gen2
Write | mandatory | as EPC Gen2
Authenticate | optional | as EPC Gen2
Extend | mandatory | New command to be defined in AMP To accommodate TXOP limitation
Minimum set

## Slide 7: “Extend” Command
AMP reader channel access needs to coex with regular WiFi and comply with TXOP
Some operation sequence may take longer time
  e.g. multi-tag inventory, delayed replay
  Finish the operation sequence in multiple TXOPs or PPDUs
A new “Extend” command can be defined
  Reader to indicate to the tag
  The next command is an extension from previous operation
  Tag to maintain a persistent status and to response in next TXOP or PPDU

## Slide 8: Examples
TXOP-1 + TXOP-2 is too long
  may take milli-second processing time
  e.g. Write process, Authenticate process
  Tag may lose energy after TXOP-1
  “Extend” command instruct tag to retain state for in persistent memory
AMP
Reader
Tag
TXOP-1
TXOP-2
CCA

## Slide 9: Inter-Frame Space
UHF RFID link timing is very flexible due to
  flexible data rate, and
  diverse regulatory requirement in various geographical regions
AMP backscattering definition can be much simplified
  Single DL data rate: 250kbps
  Single channelization and spectrum mask definition in 2.4GHz
Backscattering sequences
  Immediate reply: inventory operation
    e.g. Single-Tag reply, and Multi-Tag reply
  Delayed reply:
    operations that tags need more time to process before response
    e.g. Authentication, Write

## Slide 10: Immediate Reply
Both Reader and Tag shall response within pre-defined time window during the frame exchange
  T1: Tag response time
  T2: Reader response time
  T3: No reply time wait time
AMP
Reader
Tag
AMP
Reader
Tag
No
reply
Invalid ACK
No reply

## Slide 11: Delayed Reply
Reader shall provide energy for the specified time for Tag to process and prepare response
Tag shall response within pre-defined time window
T5: wait time for Reader
AMP
Reader
Tag
AMP
Reader
Tag

## Slide 12: Examples
Reuse some of existing WiFi IFS time definition
Time | Description | AMP | Note
T1 | Tag Response time | 16us (+/-10%) | EPC Gen2: value dependent on Tari, minimum 15us
T2 | Reader Response time | 10 or 16us (+/-10%) | 
T3 | No replay Reader wait time | TBD | EPC Gen2: min 0us, no max
T4 | Reader minimum inter-command time | 10 or 16us (+/-10%) | EPC Gen2: min T1+T3, no max
T5 | Tag processing time for delayed reply | TBD | EPC Gen2: [250us, 20ms]

## Slide 13: Summary
Discuss about EPC Gen2 logical interface
  Memory and access, inventory operation, advanced operation
Propose the simplified protocol for AMP
  Reuse memory definition and access command
  A subset of required commands
  New “Extend” command for TXOP/PPDU limit
Discuss about the inter-frame space definition
  Try to reuse existing IFS values
  Not to exceed the requirement of the UHF tag

## Slide 14: References
[1] 11-24/0836, thoughts-on-amp-uhf-rfid-tags
[2] 11-24/1805, time-based-channel-access-discussions
[3] EPC UHF Gen2 Air Interface Protocol | GS1

## Slide 15: SP
Do you agree to add the following to the TGbp SFD?
  The AMP backscattering tag reuses the memory definition and access commands as in EPC Gen2 protocol.

## Slide 16: SP
Do you agree to add the following to the TGbp SFD?
  The AMP defines an Extend command to request the tag to extend the operation sequence in the next TXOP or PPDU.
  The name and content of the command is TBD

## Slide 17: SP
Do you agree to add the following to the TGbp SFD?
  The nominal response time for AMP backscattering tag is 16us.