## Slide 1: More Consideration for feedback information
Date: 2025-3-xx
Authors:
Name | Affiliation | Address | Phone | Email
Hongwon Lee | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | hongwon.lee@lge.com
Insun Jang |  |  |  | insun.jang@lge.com
Geonhwan Kim |  |  |  | geonhwan.kim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Sunhee Baek |  |  |  | sunhee.baek@lge.com
Yelin Yoon |  |  |  | yl.yoon@lge.com
Dongju Cha |  |  |  | dongju.cha@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Sanggook Kim |  | 10680 Treena St, San Diego CA 92131 , USA |  | sanggook.kim@lge.com

## Slide 2: Introduction
The Motion to allow Multi-STA BA to carry one or more types of feedback(e.g., unavailability) information was passed during the November F2F meeting
There are several options to include multiple types of feedback information
  If we consider ICR and CRF, the M-BA is a good option
This contribution focuses on how to incorporate multiple types of feedback information into the M-BA

## Slide 3: Feedback information in M-STA BA
Basically, it is straightforward that Multi-STA BA as CRF (rather than ICR) can carry unavailability information (if present) as well as BA information (baseline as usual)
Additionally, we can have the following potential information per our current agreements
  Unavailability information [7]: Unavailability Target Start Time, Unavailability Duration
  Cross-link Power Save(CLPS) information [5]: Link ID info, PM bit per link, Power Save scheduling information, etc.
  Low Latency Traffic(LLT) information [4]: LLT indication(the low latency traffic indication for TXOP responder)
  MAPC information: Time allocation(intention to receive/not to receive), Required TXOP Duration, LLT Traffic indication
  Buffer Status Report information [1][2][3]: BSR and/or BSRE(BSR Enhancement)
    This can be included in a CRF to perform unsolicited manner if necessary
    This can also be included in case the BSRP solicits a non-HT (dup) PPDU
  Etc.

## Slide 4: M-BA with feedback information use case
UHR AP
STA1
(Legacy)
AP’s TXOP
BSRP
QoS Null
STA2
(UHR)
M-BA + QoS Null
DATA
BA
BA
BA
M-BA
DATA
Frame Control | Duration | RA | TA | BA Control | BA Information | FCS
AID – for UHR AP
Per AID TID Info (BlockAck) | AID11 | Ack Type = 0 | TID = 13 | Fragment Number | Feedback
12 bits + 4, 8, 16, or 32 octets
Per AID TID Info for feedback information
DUO, LLT, CLPS, unsolicited BSR(if necessary)
Unavailable Time
IDC event recognized
X
Basic TF

## Slide 5: Multiple feedback information in the Per AID TID of M-BA
Option1 – Multiple Per AID TID info subfields for multiple types of feedback information (Preferred)
  Each Per AID TID subfield has the Type field (e.g. 4 bits)
    Similar method for BSRP Trigger frame – a feedback type field (4 bits) based on the motion 261
Option2 – Multiple feedback information in the Feedback subfield
  BA bitmap(Feedback) size determination based on the fragment number(e.g. 4, 8, 16 or 32 octets)
  Multiples types of information could be included in the BA bitmap(Feedback) subfield and should be distinguished using certain methods
    Number of feedback information + T[L]V structure
    Presence bitmap + fixed location for information
Both options can include with BA and feedback information in the Multi-STA BA together

## Slide 6: Option 1
Multiple Per AID TID info subfields for multiple types of feedback information
  The Feedback subfield is indicated by setting the Ack Type to 0, and the TID to 13
  The AID11 is the intended recipient AID or 2008 for All STAs
BA for TID 0
BA for TID 1

## Slide 7: Option 2-1
Multiple types of feedback information(w/ Type) in the Feedback subfield
BA for TID 0
BA for TID 1
  The Feedback subfield is indicated by setting the Ack Type to 0, and the TID to 13
  The Number of Info is required to specify the actual length of feedback information in Feedback subfield. It could also be used for future extensions
  The Length for each feedback type can be omitted if the feedback information has a pre-determined length

## Slide 8: Option 2-2
Multiple types of feedback information(w/ Presence Bitmap) in the Feedback subfield
BA for TID 1
BA for TID 0
  The Feedback subfield is indicated by setting the Ack Type to 0, and the TID to 13
  The number of info is unnecessary, as the presence bitmap indicates the number of feedback entries
  If the Presence Bitmap is included, ID(for Type) is not necessary

## Slide 9: Conclusion
We discussed several options to include multiple types of feedback information in the Multi-STA BA
  Option 1 : Multiple Per AID TID info subfields (w/ Type) for multiple types of feedback information (Preferred)
  Option 2-1: Multiple feedback information(w/ Type) in the Feedback subfield
  Option 2-2: Multiple feedback information(w/ Presence Bitmap) in the Feedback subfield
Both options can include with BA and feedback information in the Multi-STA BA together

## Slide 10: Straw Poll 1
Do you agree to include the following into the 11bn SFD?
  11bn allows a Multi-STA BA frame to include both Block Ack Bitmap and Feedback information if the preceding PPDU includes QoS Data frame(s) that solicit an immediate response (e.g., Ack or BlockAck context) and the non-AP STA is operating in a mode that allows inclusion of feedback information(e.g. DUO mode)

## Slide 11: References
[1] 11-24/834r1, Some Details on In-Device Coexistence
[2] 11-24/1490r1, More Consideration of ICR/CRF for in-device-coexistence
[3] 11-23/2007r2, Enhancement of BSR
[4] 11-/24/0389r0, Preemption for Low Latency
[5] 11-24/0602r0, Multi Link Power Management for MLO
[6] 11-24/1221r3, ICF ICR follow up
[7] 11-24/1558r2, In-Device Coexistence – Follow Up
[8] 11-24/1887r0, BSRP TF response rules changes for M-BA