## Slide 1: Further Thoughts on AMP DL PPDU for Mono-static Backscattering
Date: 2025-01-09
Authors:

## Slide 2: Introduction
The group is trying to unify the DL PPDU design
  support multiple use cases and hardware capabilities
  agreed on one PPDU format
[1], we proposed unified SYNC design
  The group agreed on SYNC chip duration of 2us for backscattering
In this contribution, some further thoughts on DL PPDU design
  Potential benefits of separate DL PPDU definition
  Backscattering PPDU design

## Slide 3: AMP Tag DL Rx Capability
DL (2.4 GHz) | Backscattering Tags | Active Tags | Wakeup Tags/function
Rx RF/analogue | WideBW (~80MHz) | WideBW (~80MHz) | NarrowBW (~4MHz)
Operating RSSI | up to -20dBm | up to -70dBm | up to -70dBm
Operating clock | ~2MHz 100kppm | ~8MHz 1000ppm | ~8MHz 1000ppm
2.4GHz Excitation | Yes | No | No

## Slide 4: Unassociated AMP Tag operation
AMP backscattering tags are in unassociated operation
AMP reader needs to discover (“inventory”) the available tags within coverage
  This process is based on random access in nature
  The number of tags is unknown, “counting pupils in the dark room”
  The inventory time is dynamic
AMP reader needs some flexibility to control TXOP
  Achieve better medium utilization

## Slide 5: Inventory Operation Examples
  The inventory round duration can vary by many factors:
    Number of tags, error recovery, etc.
  PHY preamble LENTH cannot be revised after transmission
  MAC has more flexibility to end TXOP using CF-end frame
    Better channel utilization efficiency
CTS
CF-end
CTS
Invalid ACK
No reply
No reply
Successful Read
Tag 1
Tag 1
Tag 2
TXOP
Successful Read

## Slide 6: Revisit DL PPDU Design
[3] asks the question whether to have separate SYNC?
AMP DL PPDU
  WideBW 802.11 preamble + Narrowband single carrier
  LENGTH field indicates the entire PPDU duration
 |  |  |  |  | … |  | 
WiFi preamble
Excitation
SYNC-Data
Excitation
Excitation
Excitation
SYNC-Data
SYNC-Data

## Slide 7: Another Option
AMP DL only PPDU: simplified
  WideBW 802.11 preamble + narrowband single carrier
    No excitation field
  Used for Active Tag DL control and Wakeup Tag
    SYNC and data rate based on up to -70dBm RSSI and 8MHz clock rate
Proposal: Backscattering PPDU
  Narrowband (or WideBW) single carrier with Excitation fields
  Optional WideBW 802.11 preamble
  Must precede with an MAC control frame, e.g. CTS
SYNC (SIG) | Data
WiFi preamble
 | SYNC | Data |  | SYNC | Data |  | … | SYNC | Data | 
Excitation
Excitation
Excitation
Excitation

## Slide 8: Backscattering PPDU
Carrier waveform format
  DSSS PPDU is preferred [2, 4, 6]
    Open to DSSS PPDU new spreading code [6]
    This one has small change to existing WiFi
  Single carrier is preferred for OOK modulation [2, 4, 5]
  Create synergy to reuse the Tx path of regular WiFi
    AMP backscattering reader is likely part of a WiFi-compatible device
  Note:
    SC portion of DL only PPDU may share the same carrier

## Slide 9: Simulations
Spectrum of 11b with OOK

## Slide 10: SYNC for Backscattering PPDU
Pulse width (PW) of 2us is agreed for DL SYNC for backscattering case [1]
  [1] 16-bit long SYNC sequence is proposed for all cases
For Backscattering PPDU, Shorter SYNC is possible
  Rx power is high, e.g. -20dBm
  Proposal: 8-bit [0 1 1 1 1 1 0 1]
    The first OFF PW indicate the start of DL modulation
    5 PW ON carrier is a code violation (non Manchester) to confirm
      This duration also differentiates from data-0 signal of any Tari/PW in EPC Gen2
    The last 0/1 transition provides timing for Data Manchester decoding

## Slide 11: Simulations
  Pfalse = 0 in the simulated SNR region
  In real operation, the Rx SNR is much higher.

## Slide 12: Summary
Propose another thought about DL PPDU design
Propose a spin-off Backscattering PPDU
  Optional 802.11 preamble
  Always precede with initial control frame
  More efficient design and better network efficiency
DSSS PPDU is the preferred carrier
  Open to new spreading code for narrow bandwidth
SYNC design
  Short 8-bit sequence works well

## Slide 13: References
[1] 11-24/1797, Design Considerations of DL Data Rate and SYNC
[2] 11-24/1557, dl-ppdu-design-considerations
[3] 11-24/1816, downlink-sync-field-options
[4] 11-24/1803, sync-field-for-amp-ppdu
[5] 11-24-1163, wur-for-integrated-energizer-case
[6] 11-24-1802, ook-generation-for-amp-dl.pptx

## Slide 14: SP
Do you agree to add the following to the TGbp SFD?
  IEEE 802.11bp will specify, in 2.4 GHz, an AMP Downlink PPDU for backscattering
    The PPDU contains at least an AMP-Sync field, an AMP-Data field, and an Excitation field
    Additionally, AMP-Sync precedes each AMP-Data field
    Note:
      Name of this Downlink PPDU is TBD.
      The first PPDU transmission in an TXOP is always preceded by an initial control frame to protect the medium.

## Slide 15: SP
Do you agree to add the following to the TGbp SFD?
  The AMP Downlink PPDU for backscattering can use DSSS PHY PPDU defined in Clause 15.3 (DSSS PHY) as the carrier for OOK modulation and Excitation.

## Slide 16: SP
Do you agree to add the following to the TGbp SFD?
  The AMP-Sync field of the AMP Downlink PPDU for backscattering consists of 8-bit

## Slide 17: Appendix

## Slide 18: PHY PPDU: Alternative Definition
AMP DL PPDU
  WideBW 802.11 preamble + Narrowband single carrier
AMP NB-only PPDU:
  UL active transmission or Backscattering PPDU
  UL active transmission:
    Excitation fields is not needed
    Always precedes with a DL control/polling frame
  Backscattering:
    Excitation fields exists
    Always precede with an MAC control frame, e.g. CTS
SYNC (SIG) | Data
WiFi preamble
 | SYNC | Data |  | SYNC | Data |  | … | SYNC | Data | 
Excitation
Excitation
Excitation
Excitation