## Slide 1: Sounding PDT related issues
Date: 2025-01-13
Authors:
Name | Affiliations | Address | Phone | Email
You-Wei Chen | Mediatek | 2840 Junction Ave. San Jose, CA, 95134 |  | You-Wei.Chen@mediatek.com
Eric Pc |  |  |  | 
Jianhan Liu |  |  |  | 
Shengquan Hu |  |  |  | 
Thomas Pare |  |  |  | 

## Slide 2: Introduction
COBF/COSR motion passed in IEEE [1].
  There is no UHR sounding sequence for SU TxBF or DL MU-MIMO. UHR SU TxBF and UHR DL MU-MIMO uses EHT sounding sequence.
  UHR sounding sequence uses EHT NDP. I.e., there is no UHR NDP.
    UHR COBF sounding sequence is the only UHR sounding sequence
  NDP Announcement Variant subfield shall be set to 3 for COBF NDPA in UHR. (EHT variant)
The general direction is minimizing the STA side modification to support UHR Co-BF transmission.
In this presentation, we are going to discuss comments on sounding PDT :
  CSI feedback/ TB PPDU
  CSI segmentation/ retransmission
  Sounding feedback type

## Slide 3: CSI feedback
Should we reuse EHT or define a UHR compressed beamforming/CQI report?
  Currently, there is no proposal to define a new feedback type.
  To reuse STA side design as much as possible, we propose to use EHT Compressed Beamforming/CQI report.
A UHR STA is also an EHT STA. After BFRP trigger, the STA replies a TB PPDU.
  The STA receives UHR Co-BF NDPA and treats it as an EHT NDPA (it does not required to understand the UHR Co-BF NDPA).
  The STA receives EHT sounding NDP and response an EHT Compressed Beamforming/CQI report.
  To minimize the STA side modification, we propose to use EHT TB PPDU.
TBD

## Slide 4: CSI feedback segmentation and retransmission
A UHR Co-BF beamformee transmits EHT compressed beamforming/CQI report following the segmentation rules defined in 35.7.4 (Rules for generating segmented feedback).
  Note: UHR Co-BF beamformee reuses EHT segmentation rules.
A UHR Co-BF beamformer that fails to receive some or all of the feedback segments of the EHT compressed beamforming/CQI report from the UHR Co-BF beamformee shall not use a BFRP Trigger frame to request retransmission of the feedback segments.
  In this case, the UHR Co-BF beamformer may repeat the entire sounding sequence.
  It means there is something wrong during the sounding process. Even we ask for retransmission of the CSI feedback, we cannot know if the feedback result is reliable.

## Slide 5: Sounding feedback type
EHT TB sounding can be used for SU, MU and CQI feedback.
For Cross-BSS UHR TB sounding and UHR TB joint NDP sounding, UHR Co-BF sounding use EHT MU full bandwidth feedback.
TBD

## Slide 6: Straw Poll #1
Do you agree to include the following text to the 11bn SFD?
UHR Co-BF sounding reuses EHT Compressed Beamforming/CQI report.

## Slide 7: Straw Poll #2
Do you agree to include the following text to the 11bn SFD?
EHT Compressed Beamforming/CQI report containing UHR Co-BF sounding feedback shall be carried in EHT TB PPDU.

## Slide 8: Straw Poll #3
Do you agree to include the following text to the 11bn SFD?
UHR Co-BF sounding reuses the EHT sounding segmentation and retransmission rules.

## Slide 9: Straw Poll #4
Do you agree to include the following text to the 11bn SFD?
UHR Co-BF sounding uses EHT MU full bandwidth feedback.

## Slide 10: References
[1] TGbn Motions List - Part 1, 24/171r26