## Slide 1: CFO Correction for COBF
Date: 2025-03-10
Authors:
Name | Affiliations | Address | Phone | email
Sameer Vermani | Qualcomm Technologies Inc. |  |  | svverman@qti.qualcomm.com
Sherief Helwa |  |  |  | 
Alice Chen |  |  |  | 
George Cherian |  |  |  | 
Bin Tian |  |  |  | 
Youhan Kim |  |  |  | 

## Slide 2: Introduction
CFO correction for COBF is an open topic in 802.11bn
In this document we propose CFO correction schemes for COBF
Outline
  Sync-reference and Sync-follower
  Sounding stage CFO correction
  General principles for transmission stage pre-corrections
  Two cases for transmission stage
    Sync-reference as TxOP owner or sharing AP
    Sync-follower as TxOP owner or sharing AP
  Simplifications to make the protocol agnostic to the above two possibilities
  Summary

## Slide 3: Sync-reference and Sync-Follower
We introduce the concept of Sync-reference and Sync-Follower APs
They are defined as follows:
  Sync-reference AP: The AP acting as a frequency reference during sounding stage and beyond
    Does not need to remember CFO re-corrections
  Sync-Follower AP: The AP that aligns its frequency with respect to the Sync-reference AP during sounding stage and beyond
    Remembers pre-corrections
How to decide which AP gets to be the sync-reference is out of the scope of this presentation

## Slide 4: Sounding stage CFO correction
Sync-Follower AP can estimate CFO from that NDPA frame and pre-compensate for it in its future NDP transmissions when doing cross-BSS sounding
  Note, we propose only cross-BSS NDP pre-correction as a mandatory requirement
  The in-BSS NDP of follower AP is recommended to be pre-corrected (but not mandatory)
    Since the pre-correction only impacts performance of STAs in that BSS, and there might be other ways to perform post-correction of in-BSS channel estimates to avoid performance loss, we refrain from mandating this
Same idea applies for joint sounding
Sync-Follower AP (AP2) estimates CFO w.r.t. Sync-Reference AP
Sync-Follower AP pre-compensates CFO before Tx
Sequential Sounding
AP1
AP2
NDPA
NDP
CSI
SIFS
SIFS
SIFS
BFRP
SIFS
Measurement Phase
STA1
STA2
NDPA
NDP
CSI
BFRP
SIFS
SIFS
SIFS
NDPA
NDP
CSI
SIFS
SIFS
BFRP
SIFS
NDPA
CSI
BFRP
SIFS
NDP
SIFS
SIFS
SIFS
SIFS

## Slide 5: General principles for transmission stage
Want to keep transmission stage protocol as consistent as possible regardless of which AP is sync reference
The sharing AP is the AP that transmits the final sync frame
  Regardless of who is the sync-reference and sync-follower
  Consistent behavior for sharing AP
Additionally, we propose that the shared AP always pre-corrects COBF PPDU based on the final sync
  To bring the two APs within a small frequency range of each other (e.g. ~350Hz)
  Regardless of who is the sync-reference, consistent behavior at shared AP
Also need the sounding stage frequencies be carried over to the transmission stage
  When the sync follower is the sharing AP, it uses the same pre-correction values as sounding stage to send the COBF sync and the COBF PPDU
  Note that the carrier frequencies at both APs may drift in the time elapsed since sounding
    But this drift does not impact the performance even if it is up-to a few kHz

## Slide 6: Transmission stage CFO correction: Sharing AP is the Sync reference
For the transmission phase, if the TXOP owner (sharing AP) is the Sync-reference AP, the Sync-Follower AP can align its frequency based on CFO estimate from the CoBF Sync frame
Sync-Follower AP (AP2) estimates CFO w.r.t. Sync-reference AP
Sync-Follower AP pre-compensates CFO before Tx
Sync-reference AP
Sync-Follower AP
Sync-reference AP is TXOP owner
AP1
AP2
DL PPDU
Sharing AP
DL PPDU
Shared AP
BA
BA
CoBF
Invite
SIFS
SIFS
CoBF
Response
SIFS
Shared TXOP
CoBF
Sync
SIFS
STA1
STA2

## Slide 7: Transmission stage CFO correction: Sharing AP is the Sync Follower
Sharing AP still transmits the COBF Sync frame
COBF Sync and DL PPDU needs to be close in frequency to the sounding stage frequency of AP1
  Can be easily achieved through remembering the sounding stage pre-correction
Shared AP still aligns its frequency based on CFO estimate from the COBF Sync frame
  No change in behavior at a shared AP in response to a COBF sync
Shared AP (AP2) estimates CFO w.r.t. sharing AP
Shared AP pre-compensates CFO before Tx
Sync-Follower AP
Sync-reference AP
Sync-follower AP is
TXOP owner
AP1
AP2
Transmitted with same pre-correction as sounding phase
DL PPDU
Sharing AP
DL PPDU
Shared AP
BA
BA
CoBF
Invite
SIFS
SIFS
CoBF
Response
SIFS
Shared TXOP
CoBF
Sync
SIFS
STA1
STA2

## Slide 8: Summary
Define the concept of Sync-reference and Sync-Follower
  Sync follower remembers frequency offset to the follower that is needed for pre-correction, during the sounding stage and the transmission stage
Proposed solution
  Sync follower AP corrects its NDP transmissions during the sounding stage
    Correction of cross-BSS NDPs is mandatory
  Sharing AP transmits the final COBF sync for the COBF PPDU
  Shared AP always pre-corrects based on the final COBF sync from the sharing AP
  When the sync follower is the sharing AP, it uses the same pre-correction values as sounding stage to send the COBF sync and the COBF PPDU

## Slide 9: SP1
Do you support defining the concept of a sync-reference AP and a sync-follower AP for CFO corrections in COBF?
  Sync-follower AP pre-corrections needed
    For sequential sounding:
      All the NDPs sent by it during sounding phase that are sent for the purpose of sounding the STAs in the other BSS (Mandatory)
      For the NDPs sent by it for sounding the STAs in its own BSS, it is recommended but not mandatory that the sync follower AP pre-correct those NDPs
    For joint sounding:
      All the NDPs sent by it during the sounding phase
    The COBF sync and COBF PPDU during transmission phase using the same frequency pre-correction value as the sounding phase, when it is the sharing AP
  Sync-reference AP does not pre-correct during transmission phase when it is the sharing AP

## Slide 10: SP2
Do you support that in the sounding phase of COBF, the sync-follower AP shall use the NDPA frame sent by the sync-reference AP to pre-correct the NDP frequency to be within a TBD range (e.g., 350Hz) of the sync-reference AP’s frequency?
  Applies to sequential and joint sounding
  The pre-correction of cross-BSS NDP and joint NDP is mandatory
  The pre-correction of in-BSS NDPs is recommended but not a mandatory requirement

## Slide 11: SP3
Do you support that in the COBF transmission phase, the sharing AP is the AP that transmits the final sync frame before the COBF PPDU
  Regardless of who is the sync-reference
  Note: This ensures a consistent protocol and a consistent behavior at sharing AP

## Slide 12: SP4
Do you support that in the COBF transmission phase, the shared AP always pre-corrects COBF PPDU based on the final sync
  To bring the two APs within a small frequency range of each other (e.g., ~350Hz)
  Note: Regardless of which AP is the sync-reference, this ensures consistent behavior at shared AP

## Slide 13: appendix
Protocols for joint and sequential sounding

## Slide 14: Joint Sounding protocol needs CFO Pre-correction of NDP frames
Sounding happens one BSS at a time
  Below shows the 2 AP, 1STA per AP case
NDPA
NDP
Sharing AP1
Shared AP2
NDP
STA1 associated
with AP1
STA2 associated
with AP2
BFRP
BFRP
NDPA
NDP
NDP
Large V based feedback
Large V based feedback
Needs precorrection to bring
within 350 Hz
This frame is transmitted at
the same pre-correction as previous NDP

## Slide 15: Sequential Sounding CFO Issues
Sounding happens one BSS at a time (shown by BRCM[1])
  Below shows the 2 AP, 1STA per AP case
  Phase 1 sounds STA1 in BSS1 and phase 2 sounds STA2 in BSS2
If the two APs just transmit NDPs at their frequency, the feedback tones at the two APs may differ by up-to 40ppm
During actual transmission stage, we will have to make shared AP synchronize to sharing AP for the joint LTF phase
Ran sims to evaluate performance impact of precoding tones being different than transmission tones
NDPA
Sharing
AP1
Shared
AP2
NDP
STA1
associated
with AP1
STA2
associated
with AP2
CSI
BFRP
BF
RP
NDPA
NDP
CSI
NDPA
BFRP
NDP
CSI
NDPA
NDP
CSI
BFRP
Phase 1
Phase 2

## Slide 16: Possible solution for the sequential sounding CFO Issues
All NDP frames are synced to sharing AP (transmitter of the first NDPA)
  First yellow NDP needs to perform pre-correction to sync to the green NDPA before it
  Second yellow NDP needs to use the same pre-correction as the one during first yellow NDP
    Shared AP needs to remember the correction from the phase 1, to use it during the second phase when it is the transmitter of the NDP
NDPA
Sharing
AP1
Shared
AP2
NDP
STA1
associated
with AP1
STA2
associated
with AP2
CSI
BFRP
BF
RP
NDPA
NDP
CSI
NDPA
BFRP
NDP
CSI
NDPA
NDP
CSI
BFRP
Phase 1
Phase 2
CFO
Precorrection
CFO
Precorrection