## Slide 1
January 2025
Fairness Issue in Co-TDMA
Date: 2025-01-09
Authors:
Name | Affiliations | Address | Phone | email
Si-Chan Noh | Newracom |  |  | sc.noh@newracom.com
Joonsoo Lee |  |  |  | js.lee@newracom.com

## Slide 2: Introduction
TGbn define a Coordinated TDMA (Co-TDMA) procedure for an AP to share its time resources of an obtained TXOP with a set of APs
The fairness issues in Co-TDMA are discussed :
  Neighboring STAs which are not participated in Co-TDMA due to NAV protection [1]
  Shared AP might get additional airtime through Co-TDMA [2]
In this contribution, we consider the fairness issue of the shared AP and non-AP STAs that are hidden to the sharing AP, especially focus on extending the advancement approach where TXOP sharing (TXS) is applied in 11be

## Slide 3: Recap : TXS in 11be
MU EDCA parameter update
  When a non-AP EHT STA that receives an MU-RTS TXS frame from its associated AP that contains a User info field address to the STA shall update its CWmin/max[AC], AIFSN[AC], MUEDCATimer[AC];
  From which at least one QoS Data frame was transmitted successfully in a non-TB PPDU to the AP within the allocated in the Trigger frame
    Start time of MUEDCATimer[AC] is depends on whether the QoS Data frame includes immediate acknowledgment or not
It means that in cases where TXOP is granted through TXOP sharing procedure in 11be is rather than through fair contention-based access, it can be considered that a certain degree of channel access control was applied for a specific period(e.g., MUEDCA Timer) to those ACs that benefited

## Slide 4: Problem definition of Fairness Issue in Co-TDMA
In 11be, it can be considered that fairness with neighboring devices was taken into account when applying TXS in a single BSS
In Co-TDMA, where TXOP is shared between multiple BSSs, it may be necessary to control fairness in the same manner as in as single BSS for the following scenario
  For example, the shared AP participating in Co-TDMA may be efficient from a low-latency perspective by being shared TXOP;
  However, for other neighboring STAs(i.e., especially STA that hidden with the sharing AP) that are not participating in Co-TDMA, this could be a form of channel access that is not fair contention-based;
    Especially, while the original TXOP holder was the sharing AP, the shared AP uses the channel through Co-TDMA without occupying the channel for the allocated time it received
    This could potentially raise considerations regarding fairness in channel usage
Therefore, a method to control this may be necessary

## Slide 5: Problem definition of Fairness Issue in Co-TDMA
Proposal : To address fairness issue/QoS guarantee/efficient channel usage, a limitation can be applied to the shared AP
As part of the proposal, in a manner comparable to the introduction of multiple EDCA tables such as MU EDCA, it is suggested that multiple EDCA tables be adopted in cases where APs perform an M-AP coordination scheme (i.e., Co-TDMA)
  Through this, it can ensure QoS as much as possible without compromising fairness during Co-TDMA
 | 11be | 11bn (Co-TDMA)
TXOP sharing | single BSS | Multiple BSSs
Subject of multiple EDCA parameter tables | For a non-AP EHT STA that receives MU-RTS TXS | For a shared AP that receives MU-RTS TXS

## Slide 6: Summary
In this presentation, we discussed on fairness issues and ways to address them in the Co-TDMA scenario, where TXOP can be shared, rather than relying on contention-based channel access
  Allow having multiple EDCA parameter set for the shared AP

## Slide 7: Reference
[1] 11-24/0375r1, NAV protection for C-TDMA
[2] 11-24/0093r3, NAV setting for Coordinated TDMA

## Slide 8: SP1
Do you agree to allow a mechanism to control fairness issue in Co-TDMA?
  Signaling details are TBD