## Slide 1: Further Considerations on NPCA Switching Operation
Date: 2025-03-07
Authors:

## Slide 2
Introduction
The conditions for an NPCA STA to switch from a BSS primary channel to an NPCA primary channel has been defined in IEEE P802.11bn™/D0.1 [1].
The conditions for an NPCA STA switching back from the NPCA primary channel to the BSS primary channel has not yet been defined in IEEE P802.11bn™/D0.1 [1]. However, it is expected that the main consideration for an NPCA STA to switch back to the BSS primary channel should be to switch before the end of the NAV duration on the BSS primary channel.
While switching back to the BSS primary channel before the end of the NAV duration helps the NPCA STA fairly contend for the BSS primary channel, some exceptions to this switching back condition may be necessary, where an NPCA AP STA may prefer to operate accordingly.
In this contribution, we present some scenarios where an NPCA AP STA may need to switch back to the BSS primary channel after the end of the NAV duration on the BSS primary channel.

## Slide 3: Arrival of LL Data During NPCA Operation
On detecting an inter-BSS PPDU, NPCA AP and NPCA STA may set their basic NAVs on the PCH and switch from the PCH to the NPCA PCH. Then, they perform UL/DL comms. on the NPCA PCH, if the NPCA PCH is available.
While on the NPCA PCH, new data may arrive at NPCA AP for transmission to NPCA STA. NPCA AP may determine whether it can transmit the new data (e.g., LL data) before the end of the NAV duration on the PCH. In case NPCA AP determines that it cannot transmit the new data before the end of the NAV duration, it may switch back to the BSS PCH, contends for the channel and transmits the new data after winning the channel access.
NPCA STA
AP/STA
PCH
NPCA PCH
PCH
OBSS AP/STA communication within BSS-2
NPCA AP
PCH
NPCA PCH
ICF
Switch to NPCA PCH
NPCA PCH
NAV
Switch to PCH
NAV
Switch to NPCA PCH
Switch to PCH
BSS-1
BSS-2
PPDU
BA
ICR
Arrival of new data
New data
BA

## Slide 4: Problem After Switching Back to Primary Channel
As illustrated in the previous example, NPCA AP may transmit the new data after switching back to the BSS primary channel. However, when the NPCA AP and the NPCA STA switch back from the NPCA PCH to the PCH, NPCA AP may not always be able to win the channel access, and thus, may observe the PCH to be busy (e.g., another OBSS STA may already be communicating).
Not winning the channel access, NPCA AP may not be able to transmit the new data to the NPCA STA timely. The new data may be discarded or lost.
NPCA STA
AP/STA
PCH
NPCA PCH
PCH
OBSS AP/STA communication within BSS-2
NPCA AP
PCH
NPCA PCH
ICF
Switch to NPCA PCH
NPCA PCH
NAV
Switch to PCH
NAV
Switch to NPCA PCH
Switch to PCH
BSS-1
BSS-2
PPDU
BA
ICR
Arrival of new data
Busy
Busy
Discarding new data

## Slide 5: Switching Back to PCH after the NAV duration
As one solution, NPCA AP may determine a new switch back time (beyond the NAV duration) and transmit the new data before switching back to the BSS primary channel.
On receiving the frame containing the new data, NPCA STA updates its switch back time.
NPCA AP and NPCA STA switch back at the new switch back time.
As another solution, NPCA AP may transmit a frame to announce the new switch back time to its associated NPCA STAs before transmitting the new data.
NPCA STA
AP/STA
PCH
NPCA PCH
PCH
OBSS AP/STA communication within BSS-2
NPCA AP
PCH
NPCA PCH
ICF
Switch to NPCA PCH
NPCA PCH
NAV
Switch to PCH
NAV
Switch to NPCA PCH
Switch to PCH
BSS-1
BSS-2
PPDU
BA
ICR
Arrival of new data
New data

## Slide 6: Updating Switch Back Time for Short TXOP Duration
Arrival of new data
In another scenario, new data may have arrived at NPCA AP for transmission to NPCA STA while on the PCH, but the NPCA AP may not have the channel access on the PCH. As NPCA AP switches to the NPCA PCH, it may determine that the time required to transmit the new data exceeds the duration of OBSS activity on the PCH.
NPCA AP may then determine a new switch back time (beyond the NAV duration) and transmit the new data before switching back to the BSS primary channel. NPCA AP may announce the new switch back time to its associated NPCA STAs while transmitting the new data or before transmitting the new data.
NPCA STA
AP/STA
PCH
NPCA PCH
PCH
OBSS AP/STA comm. within BSS-2
NPCA AP
PCH
NPCA PCH
ICF
Switch to NPCA PCH
NPCA PCH
NAV
Switch to PCH
NAV
Switch to NPCA PCH
Switch to PCH
BSS-1
BSS-2
BA
ICR
New data

## Slide 7: Conclusion
In this contribution, we considered some scenarios where an NPCA AP may need to switch back to the BSS primary channel after the NAV duration (e.g., same as the duration of OBSS activity) on the BSS primary channel.
While the baseline for an NPCA STA to switch back to the BSS primary channel should be to switch before the end of the NAV duration on the BSS primary channel, some exceptions to this switching back condition may be defined:
  E.g., if an NPCA AP determines the duration required to transmit buffered data (e.g., LL data) on the NPCA primary channel to exceed the duration of the OBSS activity on the BSS primary channel.
  TBD some other conditions
Defining some exceptions to switching back to the BSS primary channel before the end of OBSS activity may be helpful especially when there is buffered low latency traffic at the NPCA AP.

## Slide 8: References
[1] IEEE P802.11bn™/D0.1, January 2025

## Slide 9: Straw Poll – 1
Do you agree to add the following text to the TGbn SFD?
• NPCA AP that has switched to the NPCA primary channel shall be switched back to the BSS primary channel before the expected duration of the OBSS activity that makes the BSS primary channel busy ends, unless NPCA AP has buffered data that cannot be transmitted on the NPCA primary channel before the expected duration of the OBSS activity that makes the BSS primary channel busy ends.
  Buffered data may be low latency data.
  Yes
  No
  Abstain
  Y/N/A: