## Slide 1: Multicast/Broadcast Segmentation within a BSS
Date: 2025-01-14
Authors:

## Slide 2: Abstract
There are multiple initiatives/programs outside 802.11 that require segmentation/limiting broadcast/multicast traffic to single device or group of devices connected to the same BSS.
This submission covers:
- Use cases
- Possible solutions

## Slide 3: Background
The Group Temporal Key (GTK) is bound to a single BSS
All STAs within a BSS share the same GTK – resulting in broadcast/multicast traffic being visible to every STA.
Certain network protocols utilize multicast to advertise services and capabilities from the STAs (mDNS, SSDP etc) and potentially expose privacy information to the BSS
Shared GTKs in public networks (guest/passpoint) exposes PII within the BSS
There have been attacks between stations, leveraging multicast destination address, bypassing peer-to-peer blocking mechanisms
Constraint: Network Operators and users want to limit the number of advertised BSSs while providing privacy for connected STA
Additional requirement to group devices using various mechanisms (SAE, .1X, Matter etc) for Multi-Dwelling Units, Dorms, home automation etc

## Slide 4: Current deployments
WFA Passpoint: current recommendation is to disable GTKs within a BSS (or provide a random GTK per device) – to prevent multicast
Vendors have implemented their own solutions to solve these requirements
Requirements for Segmentation within a BSS are increasing from network operators
Shared GTK within the BSS result in the use of the lowest cryptographic strength group cipher to promote interoperability with legacy STAs
Disabling GTKs may cause issues for STAs

## Slide 5: Possible Solutions
Use already defined cipher suite selector 00-0F-AC:7 (Group addressed traffic not allowed)
  what to do with GTK/IGTK delivery when that cipher suite is used?
  IEEE 802.11 standard should be extended to either mandate that behavior for this group data cipher suite cases or at least point out that that design has been deployed. It would also be helpful to define non-STA behavior when this group data cipher is used in the network.
  That 00-0F-AC:7 cipher suite selector could be used for group management cipher as well. That should also be described in the standard.
Assign a GTK per group of devices
  How the devices are grouped are outside the scope, could be any mechanism such as SAE, .1X/RADIUS etc
  What to do with the IGTK? Per group of devices?