## Slide 1: Support NPCA in CTDMA
Date: 2025-01-7
Authors:
Name | Affiliation | Address | Phone | Email
Lyutianyang Zhang | Huawei |  |  | zhanglyutianyang@huawei.com
Zhenpeng Shi |  |  |  | 
Yunbo Li |  |  |  | 
Ming Gan |  |  |  | 
Jason Yuchen Guo |  |  |  | 
Guogang Huang |  |  |  | 
Yue Zhao |  |  |  | 
Maolin Zhang |  |  |  | 

## Slide 2: Background of CTDMA
[Motion #135] The sharing AP, that transmits a Trigger frame as part of a transmission sequence in a Multi-AP coordinated transmission scheme, identifies the shared AP via an AP ID carried in the AID12 field of the User Info field of the frame.
Negotiated AP ID is used to share TXOP portion to shared AP.
[Motion #156] The Duration field of the frame is set to the length of time required to transmit the solicited response frame plus one SIFS.
Short NAV set by duration field in ICF polling frame, need to indicate the CTDMA operation duration for NPCA.

## Slide 3: Recap of CTDMA
AP1
AP2
AP3
Polling
Resp
PPDU
AP1 <-> STA
TXOP sharing
MU-RTS TXS
CTS
PPDU
AP3 <-> STA 3
Short NAV
Announcement
Short NAV
Sharing AP sends Polling to ask if AP is willing to join CTDMA with Response. Then sharing AP make announcement about the shared TXOP portion to shared AP.
ICF frame exchanges are all short NAV.
Whole TXOP duration
Whole CTDMA duration

## Slide 4: Motivation
Case 1: AP 2 is not polled (no AP 2 ID in ICF Polling).
Case 2: AP 1 polls AP 2 but AP 2 decides to not participate in CTDMA (No AP 2 ICR)
Case 3: AP 1 polls AP 2 and AP 2 decides to participate in CTDMA (AP 2 ICR)
All above cases, there are exploitable unavailable medium duration for AP 1, 2 and 3, to which NPCA operation can take advantage of with additional information provided, i.e., CTDMA duration.
NPCA operation requires that both STA and AP to use the AP ID and CTDMA duration/shared TXOP duration to do NPCA when they are not shared with TXOP within CTDMA.

## Slide 5: ICF Announcement Signaling
AP ID | Start time of Shared TXOP | Duration of Shared TXOP
ICF Announcement frame - User Info
ICF Polling Frame– Common/Special User Info
Whole TXOP/CTDMA Duration
NPCA enable bit
BSRP Trigger Frame: EHT Variant

## Slide 6: NPCA in CTDMA case 1
AP1
AP2
AP3
Resp
AP1 <-> STA
TXOP sharing
MU-RTS TXS
Not interested in CTDMA in this TXOP Unpolled
CTS
AP3 <-> STA 3
STA 2
NPCH
AP2
STA 2
1) both AP 2 and STA 2 to know AP 2 ID beforehand, they both know that AP 2 is not polled by AP 1
2) ICF polling frame include the whole TXOP duration so that AP2 and STA 2 can use it for NPCA operation
Polling
Short NAV
Announcement
AP ID Notification before CTDMA
Whole TXOP duration
Notes: Txop return modification.

## Slide 7: NPCA in CTDMA case 2
AP1
AP2
AP1 <-> STA
STA 2
NPCH
AP2
STA 2
1) both AP 2 and STA 2 know AP 2 ID, they both know that AP 2 is polled by AP 1
2) STA 2 receive no non-HT PPDU feedback from AP2.
3) ICF polling frame include the whole TXOP duration so that AP2 and STA 2 can use it for NPCA operation
Polled but no response
Polling
AP ID Notification before CTDMA
Short NAV = SIFS + Est. ICR Duration
Whole TXOP duration

## Slide 8: NPCA in CTDMA case 3
Slide 8
AP1
AP2
AP1 <-> STA
TXOP sharing
MU-RTS TXS
STA 2
AP2
STA 2
Resp
CTS
AP2 <-> STA 2
both AP 2 and STA 2 to know AP 2 ID beforehand, they both know that AP 2 is polled by AP 1.
2) STA 2 receives the non-HT PPDU ICR from AP 2.
3) ICF announcement frame include the start time of the shared TXOP for AP2. This info is used for NPCA.
NPCH
Polling
AP ID Notification before CTDMA
Short NAV
Announcement

## Slide 9: Summary
Propose NPCA + CTDMA operation
Utilization of AP ID, whole TXOP/CTDMA duration, and start time of shared TXOP to support NPCA within CTDMA

## Slide 10: References
[1]:Sanket Kalamkar, “Initial Control Frames in C-TDMA”, IEEE 802.11-24/1225r1, June 2024
[2]: Sanket Kalamkar, “C-TDMA Follow-up: Additional Details on Framing Sequence”，
IEEE 802.11-24/1016r, Feb 2024
[3]: Sanket Kalamkar, “PDT MAC Co-TDMA”, 2024-12-19

## Slide 11: SP
SP 1: Do you agree that AP notify its AP ID to its associated non-AP STAs?
SP 2: Do you agree that NPCA operation can operate within CTDMA under TBD conditions.