## Slide 1: High Priority Channel Access Follow Up
Date: 2025-01-22
Authors:
Name | Affiliation | Address | Mail
Xiangxin Gu | Spreadtrum | Spreadtrum Center, Lane 2288, Zu Chongzhi Road, Shanghai | Xiangxin.gu@unisoc.com
Yingqiao Quan | Spreadtrum |  | Yingqiao.quan@unisoc.com
Lei Zhou | H3C |  | zhou.leiH@h3c.com

## Slide 2: Recap
Move to add to the TGbn SFD the following:
TGbn improves EDCA to reduce tail access delay of Low Latency traffic in multi-BSS dense scenarios in presence of best effort traffic
  The solution to improve EDCA is distributed
  The impact on legacy device has to be balanced
  Low Latency traffic is treated as AC_VO traffic. Other cases are TBD
Move: Dmitry Akhmetov Second: Peshal Nayak
Discussion: None.
Result: Approved with unanimous consent.
Reference documents:[11-24/114r1, 11-23/2126r0, 11-23/1065r0, 11-24/0467r1 and 11-24/0840r0, 24/0864r1, 24/733r1]. SP result:152Y, 39N, 36A.

## Slide 3: Recap
Move to add to the TGbn SFD the following:
Define HIP EDCA in UHR where a STA with Low Latency traffic may be allowed, based on TBD conditions, to send a Defer Signal (it is TBD whether CTS or RTS is used) to start a protected short contention for pending LL data
  Conditions to be allowed to send a Defer Signal is TBD
  STA in HiP EDCA always use RTS/CTS as initial frame exchange and retry.
  Duration of protected short contention is TBD.
  Access parameters (AIFSN, CW and the expansion rules) used to transmit the Defer Signal are TBD. The retry count where the Defer Signal is allowed to be sent is TBD
  Contention parameters for the protected short contention are TBD. The STAs that transmitted a Defer Signal but did not win the protected short contention will initiate a new retry.
  Low Latency traffic is treated as AC_VO traffic. Other cases are TBD.
  The solution would provide control on the degree of collisions that may occur while using it and, allows for autonomous randomness or/and controlled by the AP
  No new mandatory synchronization requirement on STA side
  HIP EDCA is used by the STAs in a BSS only when this feature is enabled by the AP
Move: Dmitry Akhmetov Second: Kiseon Ryu
Discussion: None.
Result: Approved with unanimous consent.

## Slide 4: Considerations
The purpose can be achieved through 2 means.
  Improving EDCA mechanism.
  Improving AP EDCA for scheduling UL LLT.
    AP has priority EDCA parameters to access channel.
Improving EDCA mechanism with DS signal or serval rounds of short signal
  Brings much impact to EDCA algorithm, complexity, TX-RX transition, etc.
  LLT delay can not be guaranteed in case collision happened.
  Can’t leverage MU operation.
Improving AP EDCA for scheduling UL LLT with LLT indication signal from non-AP STA(s).
  Is in line with the trend that AP takes more control.
  Simpler and lower contention.
  With gain of MU operation.

## Slide 5: Improving AP EDCA for scheduling UL LLT

## Slide 6: Improving AP EDCA for scheduling UL LLT
STA(s) that have LLT send LLT indication signal, DIFS after the channel changes to idle.
  The LLT indication signal can be CTS frame, or Zadoff Chu sequence.
    Different ZC sequences transmitted in same duration on the channel can be addressed simultaneously.
The AP accesses the channel and schedules UL LLT.
  The AP invokes backoff SIFS after LLT indication signal.
  If the target STAs are not identified by LLT indication signal, NFRP or BSRP procedure can be invoked.
The TX power for the LLT indication signal can be determined by.
  Measured path loss and target power to receive.
Zadoff Chu sequences.
  1 symbol on 52 subcarriers can have 46[*] root ZC sequences, which have good autocorrelation and low cross correlation.
  Each root ZC sequence can generate M ZC sequences by cyclic shift, which are easy to be addressed by autocorrelation with the root ZC sequence. M is 4 if the coverage radius is less than 100 meters.
  Different ZC sequences transmitted in same duration on the channel can be addressed simultaneously.
  A ZC sequence can be assigned to a STA that has potential LL traffic in association procedure.
Notes: [*] The prime integer which is less than and closest to 52 is 47. So the length of the ZC sequences is 47 and the number of the root ZC sequences is 46.

## Slide 7: Improving AP EDCA for scheduling UL LLT

## Slide 8: Summary
In this contribution, we give considerations on improving EDCA to reduce tail access delay of Low Latency traffic in multi-BSS dense scenarios in presence of best effort traffic.
  EDCA mechanism with DS signal or serval rounds of short signal
    Brings much impact to EDCA algorithm, complexity, TX-RX transition, etc.
    LLT delay can not be guaranteed in case multiple LLT STA accessing the channel.
    Can’t leverage MU operation.
  Improving AP EDCA for scheduling UL LLT with LLT indication signal (CTS frame, etc) from non-AP STA(s).
    Is in line with the trend that AP takes more control.
    Simpler and lower contention.
    With gain of MU operation.

## Slide 9: SP
Do you agree to improve AP EDCA for scheduling UL transmission with LLT indication signal (CTS frame, etc) from non-AP STA(s) (as in the figure, details can be further discussed) ?
  LLT indication signal can be further discussed.

## Slide 10: Appendix
ZC sequence has been used as msg1 in LTE/NR for contention free random access
  The Base Station can simultaneously detect ZC sequence(s) transmitted in one timeslot on the channel and address the User Equipment(s) that sent the msg1(s), i.e. ZC sequence(s).
  It has been verified in real deployment.
ZC sequence
  q is from 1 to Nzc -1 for Nzc -1 root sequences
  Each root sequence can generate Nzc -1 sequences by cyclic shift.
  For a receiver to differentiate cyclic shifted sequences, the cyclic shift length must be > (RTTmax/Tsym)*Nzc
The advantages of ZC sequence
  Constant envelop (low PAPR)
  Good autocorrelation and low cross correlation (outstanding detection performance)
  Output of a ZC sequence through FFT is still a ZC sequence. (simple signal processing)

## Slide 11: References
[1] 11-24-0171-25-00bn-tgbn-motions-list-part-1.pptx Alfred Asterjadhi
[2] 11-24-1144-01-00bn-hip-edca-proposal-follow.pptx Dmitry Akhmetov
[3] 11-24-1481-00-00bn-csma-with-enhanced-collision-avoidance-follow-up.pptx Sigurd Schelstraete