## Slide 1: IMMW System Reuses
Date: 2025-02-08
Authors:
Name | Affiliation | Address | Phone | Email
Yanchun Li | Huawei |  |  | liyanchun@huawei.com
Yunbo Li |  |  |  | 
Ming Gan |  |  |  | 
Fan Xu |  |  |  | 
Yan Xin |  |  |  | 
Maolin Zhang |  |  |  | 
Xiang Wang |  |  |  | 
Xin Li |  |  |  | 
Xuming Wu |  |  |  | 
Jian Li |  |  |  | 
Yanchun Li (Huawei)

## Slide 2: Introduction
IMMW PAR[1] defined the basic requirements and scope of the new mmW spec, which emphasizes the reuse and MLO framework:
Use non-standalone operation in unlicensed bands in 42~71 GHz using SU OFDM based transmissions
Expand the multi-link operation (MLO) defined in the sub-7.25 GHz band specifications to support non-standalone operation in the unlicensed bands between 42 GHz and 71 GHz.
By reusing sub-7 GHz MAC/PHY, the system complexity and cost can be reduced.
This contribution considers the tradeoff between reuse and efficiency. Moderate beam searching procedure is needed to support indoor low mobility use cases.

## Slide 3: Proposed IMMW MAC Reuse/Amendment
 |  | IMMW Initial Link Setup |  |  |  |  | Beam searching /tracking | Digital MIMO | Data Transmission |  |  | Power Saving | 
 |  | Scan | Synchronization | Authenticate/ Deauthenticate | Associate/ Reassociate/Disassociate | Measurement Request/ Report |  | NDP Sounding | Block Ack | TDLS/ P2P | Multi-link Operation | TWT Power Saving | SMPS /OMI /etc.
Reuse (or minor changes) |  |  |  | ● | ● |  |  | ● | ● | ● | ● | ● | ●
Amendment | Sub- 7GHz based | ● | ● |  |  | ● | ● |  |  |  |  |  | 
 | mmW | ● |  |  |  | ● | ● |  |  | ● |  |  | 
Initial Considerations on MAC Design
Reuse and perform most of management procedures in sub-7GHz band
NAV (Channel Sensing/RTS/CTS/NAV) in mmW band
Amend mmW Beam sweeping process to keep efficient and timely beam searching/tracking
Note: black dot sign means involves amendment/reuse
Notes: Data Transmission
1）TWT enhancement for mmW, Amend

## Slide 4: Proposed IMMW PHY Reuse/Amendment
 | Reuses |  | 
 | 11be | 11bn | Amemded in 11bq
PPDU Structure | ● | ● ELR PPDU | 
OFDM Symbols | ● | ● | 
MCS | ● | ● UEQM New MCS 2x LDPC | 
Beamforming | RTS/CTS based |  | Beam searching/tracking
Tx specification Spectral Mask Spectral Flatness EVM |  |  | ●
Rx specification CCA sensitivity |  |  | ●
Channelization/ Ch Numbering |  |  | ●
11be + 11bq RF spec allows quick adoption of IMMW in Initial Phase.
11bn + 11bq new beam searching + 11bq RF spec allows advanced experience with enhanced coverage and better Beam Tracking later on.

## Slide 5: Summary
This contribution discussed the detailed reuse and amendment under the scope of IMMW PAR.
A flexible reuse framework allows IMMW system to be built on both 11be and 11bn. Such two-phase approach has benefit of promoting early adoption of IMMW/make use of 60GHz spectrum and also provide advanced performance.

## Slide 6: References
[1] IMMW proposed PAR, https://mentor.ieee.org/802.11/dcn/24/11-24-0116-07-immw-immw-draft-proposed-par.docx
Yanchun Li (Huawei)

## Slide 7: SP
SP : Do you support to define a flexible reuse framework that allows IMMW system to be built on 11be and 11bn, in SFD?
Yes
No
Abs
Yanchun Li (Huawei)