## Slide 1: Follow Up on DRUs
Jan 2025
Authors:
Name | Affiliation | Phone | email
Brian Hart | Cisco Systems |  | brianh@cisco.com
Binita Gupta | Cisco Systems |  | 
Malcolm Smith | Cisco Systems |  | 
Juan Carlos Zuniga | Cisco Systems |  | 
Stephen Orr | Cisco Systems |  | 
Javier Contreras | Cisco Systems |  | 
Pelin Salem | Cisco Systems |  | 

## Slide 2: Situation (1/3) Specification Framework Document Calls out certain DRU sizes versus DRU distribution bandwidth [1]
The following DRU sizes are defined in the SFD:
  20MHz: RU26, RU52, RU106
  40MHz: RU26, RU52, RU106, RU242
  80MHz: RU52, RU106, RU242, RU484

## Slide 3: Situation (2/3) APs are familiar with constraints on minimum RU allocation requirements for HE and EHT MU PPDUs
To simplify FFT implementations in non-AP STAs, APs have always had to support minimum RU allocation requirements for OFDMA MU PPDUs:
  HE: 26.5.1.3 (RU allocation in an HE MU PPDU); changed to 26.5.1.3a (Minimum RU allocation in an HE MU PPDU) in 11be)
  Ditto EHT by reference, from 35.5.1.1 (General)
…

## Slide 4: Situation (2/3) The optimal Rate-versus-Range strategy can newly favor sparse tones
Consider a non-AP STA starting at farthest range from its 80 MHz AP and approaching the AP
Four scenarios: (PSD-limited spectrum or not) Ⓧ (DRU available or not)
To a first order approximation*, the non-AP STA’s optimal rate-versus-range MCS+RU+BW strategy is:
Scenario* | Legacy 2.4/5GHz: spectrum is not PSD-limited, no DRUs | Legacy 6GHz: spectrum is PSD-limited, no DRUs | 11bn@ 2.4/5GHz: spectrum is not PSD-limited, DRUs are available | 11bn@ 6GHz: spectrum is PSD-limited, DRUs are available
Initially, at farthest range with minimum data rate | MCS0@RRU26 | MCS0@RRU26 | MCS0@RRU26/DRU26 | MCS0 and no more than 1 tone per MHz E.g., RU26 in 40 MHz
To increase rate as range decreases … | Either changing from BPSK to QPSK or doubling the RU size (a wash, to first order). E.g., MCS1@RRU26 or MCS0@RRU52  MCS1@RRU52 or MCS0@RRU106 in 20 MHz | MCS0@RRU52 RRU106  RRU242 in 20 MHz | Either changing from BPSK to QPSK or doubling the RU size (a wash, to first order). E.g., MCS1@RRU26/DRU26 or MCS0@RRU52/DRU52  MCS1@RRU52/DRU52 or MCS0@RRU106/DRU106 | More DRU tones, until at least 1 tone per 1MHz E.g., RU52 in 80 MHz, then RU106 in 80 MHz
 |  | MCS0@RRU484 in 40 MHz  RRU996 in 80 MHz |  | Either changing from BPSK to QPSK or doubling the DRU tone density (a wash, to first order). E.g., MCS1@RU106 or MCS0@RU242 in 80 MHz
 | Better to pick more tones per RU then select a constellation higher than QPSK E.g., MCS1@RRU106  RRU242 in 20 MHz  RRU484 in 40 MHz  RRU996 in 80MHz | MCS1@RRU996 in 80MHz | Better to pick more tones per RU then select a constellation higher than QPSK E.g., MCS1@RRU106  RRU242  RRU484  RRU996 in 80MHz | Better to pick denser tones than select a constellation denser than QPSK E.g., MCS1@DRU106  DRU242  DRU484  RRU996 (all in 80MHz)
 | Once all tones are occupied, no choice except to select a denser constellation& |  |  | 
*Ignoring preamble effects (which is reasonable for TB) and frequency diversity. &Ignoring more SSs, which is complicated by SV quality and thence antenna counts |  |  |  | 

## Slide 5: Problem (1/2) Sparse tones without the users means more spectrum is affected and at a lower spectral efficiency
Scenario | With DRUs and PSD-limited spectrum | Tone efficiency | Affected spectrum | Without DRUs (or without PSD-limited spectrum) | Tone efficiency | Affected spectrum
Initially, at farthest range with minimum data rate | E.g., RU26 in 40 MHz | 2.6% | 80 MHz | MCS0@RRU26# | 11% | 20MHz
To increase rate as range decreases … | E.g., RU52 in 80 MHz, then RU106 in 80 MHz | 5.2% then 10.6% | 80MHz | MCS0@RRU52 RRU106  RRU242 in 20 MHz | 11% or 21%  21% or 44% | 20MHz
 | MCS1@RU106 or MCS0@RU242 in 80 MHz | 11% or 24% | 80 MHz | MCS0@RRU484 in 40 MHz  RRU996 in 80 MHz |  100%  100% |  40MHz  80MHz
 | E.g., MCS1@DRU106  DRU242  DRU484  RRU996 in 80MHz | 11%  24%  59%  100% | 80 MHz | MCS1@RRU996 | 100% | 80MHz

## Slide 6: Problem (2/2) Frequency Reuse and NPCA by OBSS is harder if a nearby BSS is using more spectral inefficiently
Consider two enterprise APs using the same 80 MHz, with their P20 channels on different 40 MHz
  Typical situation in dense enterprise networks:
    When lightly loaded, either BSS can use 80 MHz
    When one is beaconing/groupcasting/etc or heavily loaded, then they can use 40 MHz in parallel (FDM)
  However, if we replace one of those enterprise APs by an AP using one DRU52/106 across 80 MHz, the efficiency and available capacity to the remaining enterprise AP is markedly degraded
Consider two 80 MHz BSSs using same P20
  If one BSS transmits using 20 or 40 MHz PPDU, then the other can use NPCA to use the remaining 40 MHz
  But if one BSS transmits using an 80 MHz PPDU, as incentivized by DRU, then the other is locked out of that entire 80 MHz of spectrum, even if it is only carrying a single RU52.

## Slide 7: Solution Add minimum RU allocation requirements for DRU allocations
Loosely speaking, MU PPDU requirements are for an average of at least four RU26s’ worth of tones per 20 MHz
This same rule – or something similar – can be applied to the Trigger frame for the DRU (aggregate) distribution bandwidths of TB PPDUs
  See backup for sample normative text

## Slide 8: Summary
At longer range, APs are newly incentivized by the Distributed RU feature spread their tones to 1 tone per 1 MHz or thereabouts
This makes frequency use via FDM and NPCA less easy to realize
We propose to add requirements, modelled on existing Minimum RU Allocation requirements for MU PPDU requirements, to the triggering of TB PPDUs

## Slide 9: Strawpoll 1
Do you agree to add the following text to the 11bn SFD:
    UHR defines Minimum RU allocation requirements for DRU distribution bandwidths
Y / N / A

## Slide 10: References
[1] XXXX, 2.2.2 (Tone Plan)
[2] “Discussion on DRUs”, 24/332r0, Brian Hart

## Slide 11: Backup

## Slide 12: Sample rewriting of 26.5.1.3a Minimum RU allocation in an HE MU PPDU for DRU
The aggregate of the distribution bandwidths of triggered UHR TB PPDUs shall have a sufficient number of RUs allocated to users such that the following condition is satisfied:
At least N × 4 × 26 subcarriers are signaled to be triggered within the aggregate of the DRU distribution bandwidths of the triggered UHR TB PPDUs, where N is the number of 20 MHz subchannels that are not preamble punctured within the aggregate of the DRU distribution bandwidths.