## Slide 1: A Service Period Based Integrated mmWave Link Operation Scheme
Date: 2024-12-05
Authors:

## Slide 2: Abstract
Background
An Example of Integrated mmWave Link Operation in a BSS
Problems in Integrated mmWave Link Operation
The SP based Integrated mmWave Links Operation
An Example of SP Based Integrated mmWave Link Operation
Summary

## Slide 3: Background on Integrated mmWave Link Operation
According the 11bq PAR, 11bq will expand the multi-link operation defined in the sub-7.25 GHz band specifications to support non-standalone operation in the unlicensed bands between 42 GHz and 71 GHz (mmWave).
An AP is expected to use sub-7GHz links to assist STAs with IMMW capability (mSTAs) to set up mmWave and communicate via mmWave links.
It is likely that mSTAs transmit data to each other via mmWave links with directional transmissions.

## Slide 4: Illustration of Integrated mmWave Link Operation
AP sets up the mmWave link (mwLink) between mSTAs.
  Information such as Tx ant sector/beam, Rx ant sector/beam, operated channels, etc. are needed to set up a link.
Multiple pairs of mSTAs can exist in a BSS.
Figure 1. Integrated mmWave Links operating in a BSS
mSTA_5
mwLink_3
IMMW AP
mSTA_2
mwLink_1
mSTA_1
mSTA_4
mwLink_2
mSTA_3
AP sets up mwLink_2 between mSTA_4 and mSTA_3. AP may end mwLink_2 and sets up mwLink_3 between mSTA_4 and mSTA_5 at another time.

## Slide 5: Problem of Integrated mmWave Link Operations
It is not desirable that each mmWave transmission requires AP coordination using sub-7 GHz channels.
  AP may not gain the sub-7 GHz channel access immediately when mSTAs requires coordination. This can cause delay of mmWave transmission and therefore reduce the spectrum efficiency.
  Frequent AP co-ordinations on IMMW transmissions introduce a lot interruptions in sub-7GHz and reduce sub-7GHz network efficiency.
  The mmWave transmissions should require least coordination in sub-7 GHz channel such that mmWave links truly offload the data from sub-7GHz band.
We expect that once an mmWave link is set up between a pair of mSTAs, the mmWave link remains until it’s assisted by AP to change.

## Slide 6: Service Period (SP) Based Integrated mmWave Link Operation
AP sends a sub-7GHz announcement frame to configure the SP duration and set up mmWave Link (mwLink) between each pair of mSTAs.
During the SP, sub-7GHz AP coordination is not needed for each mmWave link transmission.
Figure 2. Illustration of SP Based Integrated mmWave Link Operation
mwSP1: mwLink1, mwLink2
time
mwSP announcement
mwSP1 start
mwSP1 duration
Sub-7GHz pkt
…

## Slide 7: An Example of SP Based Integrated mmWave Link Operation
mwSP2 start
mwSP1: mwLink_1, mwLink_2
mwSP2: mwLink_1, mwLink_3
time
mwSP announcement
mwSP1 start
mwSP1 length
mwSP2 length
Sub-7GHz pkts
…
For the example shown in Figure 1, AP schedules and coordinates:
  Pairs of mSTAs on mwLink_1 and mwLink_2 to operate in mwSP1;
  Pairs of mSTAs on mwLink_1 and mwLink_3 to operate in mwSP2;
AP sends mwLink info and mwSP schedule info in announcement frames to each pair of mSTAs using sub-7GHz links to assist them to set up mmWave Link operations in the coming mwSPs.
Figure 3. An Example of SP Based MmWave Link Operation

## Slide 8: Summary
A Service Period (SP) based integrated mmWave link operation scheme is proposed.
  Enable AP to assist multiple mwLinks to operate in a BSS without causing excessive interruptions to sub-7GHz communications.

## Slide 9: Straw Poll
Do you support the service period (SP) based Integrated mmWave Link Operation?
  AP sends a sub-7GHz announcement frame to configure the SP duration and set up mmWave Link (mwLink) between each pair of mSTAs.
  The mwLink between each pair of mSTAs remains until AP informs change.