## Slide 1: TGbi – AID-List distribution close to epoch end
Date: 2025-03-04
Authors:
Name | Affiliations | Address | Phone | email
D. Ficara | Cisco |  |  | dficara@cisco.com
J. Contreras | Cisco |  |  | jacontre@cisco.com
U. Campiglio | Cisco |  |  | ucampigl@cisco.com
J. Henry | Cisco |  |  | jhenry@cisco.com
F. Lovison | Cisco |  |  | flovison@cisco.com

## Slide 2: Problem
11-24/1714 introduces the AID-List choreography for distributing AIDs to non-AP MLDs.
1st AID present in Association Response
AID-List provided by AP MLD via AID Assignment frame.
What if non-AP MLD associates very close to end of the current epoch? (comment #762)
=> 1st AID exhausted right away.
=> Potential ambiguity for this AID (current/next epoch?)
=> What shall we do? Wait? Send AID assignment response asking for AID?

## Slide 3: Problem scenario
Assoc Req
Assoc Resp
No AID!
AID assignment the

## Slide 4: Problem scenario
Association request can come at any point in time
From there to reaching state 4, it might take some time
In the meantime we can go through EDP Epoch completion and transient period
And AID Assignment frame has to reach non-AP MLD to be fully functional
=> need to reduce scenarios/complexity/ambiguity

## Slide 5: Proposal
Introduce AID-List Element in Association Response
Assoc Req
Assoc Resp with AID-List

## Slide 6: Summary
Problem Statement
Proposal of AID-List in Assoc Response

## Slide 7: Straw Poll
Do you agree on adding AID-List Element in the Association Response to guarantee AIDs at any moment in the EDP epoch timeline?
Yes
No
Abstain