## Slide 1: AMP Backscattering PPDU and SYNC Design
Date: 2025-03-10
Authors:

## Slide 2: Introduction
Excitation field is sent by the reader for AMP backscattering tags to modulate the information
Up to 100kppm tag clock inaccuracy induces large variation of backscattering frame starting point
SYNC field preceding the backscattered data is needed for the reader to detect the start of frame.
In this contribution, backscattering PPDU structure and SYNC field design for OOK backscattering are proposed

## Slide 3: Recap: Backscattering PPDU
[3] AMP UL PPDU for Backscattering?
  The UL frame is always “polled” by DL frame, no SIG needed
  Overlapped with Excitation field in DL PPDU
AMP UL PPDU format: SYNC + Data
  UL SYNC sequence can be different for Active Tx and backscattering
UL SYNC | UL Data

## Slide 4: Backscattering SYNC Design (1/2)
Backscattering tags with OOK modulation has clock inaccuracy of up to 100k ppm
  The modulated information will not be aligned with Excitation field symbol boundaries
  Each modulated bit will have up to 10% uncertainty in duration
Needs transition for each SYNC bit to detect the SYNC sequence
  Manchester coded OOK sequence is preferred
0 0 1 1 1 0 0 1 0 1

## Slide 5: Backscattering SYNC Design (2/2)
Backscattering data rates:
  250kbps and 1Mbps
One SYNC sequence with variable rate to support both rates
  The chip rate of SYNC matches with data OOK
  Simpler implementation for tags
  Reader knows the data rate of the backscattering PPDU
  SYNC is not used for coex

## Slide 6: UL SYNC Proposal
SYNC LEN = 16 is sufficient for synchronization
  e.g. Manchester bit sequence [0 1 1 1 0 1 0 0 0 1 1 1 0 0 0 1]
  False alarm rate is ~ 2% in noise period (e.g. 360 us long)
  Add zero-energy bit (non-Manchester) to distinguish from data pattern
    z bit: [0 0]  “OFF” for 2 chips
    Rx: compare the power at z bit with Manchester bit
Proposal: [0 1 1 1 0 1 0 0 0 1 0 0 1 0 z 1]
  Len 16 sequence with z-bit
SYNC sequence/Pfalse | 250kbps | 1Mbps
0 1 1 1 0 1 0 0 0 1 1 1 0 0 0 1 | 0.02 | 0.02
0 1 1 1 0 1 0 0 0 1 0 0 1 0 v 1 | 0.002 | 0

## Slide 7: Simulation Settings
2x2 WiFi device in “1Tx + 1Rx” mode
  Antenna isolation is 20dB  Rx power of -20dBm
    Effective Rx noise floor varies from -35dBr to -50dBr
    Note: assume TxEVM after differential is below Rx NF
AMP tag backscattering
  Manchester coded OOK modulation: -20 dBr Tx noise
  Data rate: 250kbps and 1Mbps
  Payload: 1000 bits
WiFi reader Rx BW = 40MHz, 10-bit ADC
  Fixed AGC gain to get I/Q samples
  Leakage removal using reference symbols
  Matched filter to detect modulation boundary
Leakage signal: 0dBr
Rx noise floor: e.g. -45dBr
BS signal level: e.g. -30dBr

## Slide 8: UL SYNC Performance: 250 Kbps
Pmiss is lower than backscattering data PER

## Slide 9: UL SYNC Performance: 1 Mbps
Pmiss is lower than backscattering data PER

## Slide 10: Summary
Backscattering tag with OOK modulation has high ppm
UL SYNC field is needed in backscattered PPDU for AMP Reader to detect the start of PPDU
Single SYNC sequence with variable chip rate corresponding to each data rate is preferred
SYNC sequence of length-16 Manchester sequence plus zero-energy bit is proposed
  Good Pfalse performance and Pmiss performance

## Slide 11: SP
Do you agree to add the following to 11bp SFD?
AMP UL PPDU is defined for backscattering and active transmission, and consists of two fields: UL SYNC and UL Data.
  UL Data field immediately follow UL SYNC field
  For backscattering, AMP UL PPDU is modulated on the Excitation field of the AMP DL PPDU.

## Slide 12: SP
Do you agree to add the following to 11bp SFD?
11bp defined single UL SYNC sequence for AMP UL PPDU generated by backscattering (OOK modulated)
  The UL SYNC sequence is transmitted with the same chip rate as UL Data field

## Slide 13: SP
Do you agree to add the following to 11bp SFD?
The UL SYNC sequence for backscattering (OOK modulated) contains Manchester encoded bits and zero-energy bits

## Slide 14: SP
Do you agree to add the following to 11bp SFD?
The UL SYNC sequence for backscattering (OOK modulated) is of length-16: [0 1 1 1 0 1 0 0 0 1 0 0 1 0 z 1]
  Each logical bit “0” or “1” is Manchester encoded
  “z” is zero-energy of the same duration as one Manchester encoded bit

## Slide 15: References
[1] 11-23/2038, Close Range AMP Backscattering in 2.4GHz
[2] 11-24/1798, Backscattering UL data rate and modulation