## Slide 1: Follow-up on AMP PPDU Design
Date: 2025-03-11
Authors:
Name | Affiliation | Address | Phone | Email
Yinan Qi | OPPO |  |  | v-qiyinan@oppo.com
Weijie Xu |  |  |  | 
Chuanfeng He |  |  |  | 
Ke Wang |  |  |  | 
Shengjiang Cui |  |  |  | 
Zhisong Zuo |  |  |  | 
Doc.: IEEE 802.11-25/0316r0
March 2025

## Slide 2: Abstract
In this contribution, we discuss the remaining open issues in AMP PPDU design covering issues such as preamble, synchronization, SIG, data field, PPDU format and UL transmission configuration.
Doc.: IEEE 802.11-25/0316r0

## Slide 3
DL Preamble Design
  Preamble for Active Tx and AMP enabled devices
    Agreement: The preamble of an AMP DL PPDU includes L-STF, L-LTF, L-SIG, RL-SIG, and U-SIGs for AMP enabled non-AP STA and active TX non-AP AMP STA in 2.4 GHz [1].
    Multi-carrier OFDM with BW 20MHz
  How to configure individual fields in L-SIG?
    Rate: configured as an unsupported rate
      Differentiate from WUR where rate is always configured as MCS0
      Other legacy devices can stop reception once detecting unsupported rate
    Length: configured to indicate only the DL part without excitation fields in DL PPDU
      AP may not have the knowledge of the duration for UL transmission because e.g., lack of knowledge for payload size.
Yinan Qi (OPPO)
Slide 3
Doc.: IEEE 802.11-25/0316r0
March 2025

## Slide 4
DL Preamble Design
  How to configure individual fields in RL-SIG?
    Instead of repetition of L-SIG, may consider other options to differentiate 802.11bp PPDU from legacy PPDU
  How to configure individual fields in U-SIG?
    Two U-SIG formats available but need to choose only one for 802.11bp
    How to differentiate 802.11bp PPDU from 802.11be and 802.11bn PPDU?
      Validation fields, e.g., version, BW: for example, version field can be configured different from 802.11be and 802.11bn
    UL/DL: configured as DL if there is no excitation field and UL otherwise
Yinan Qi (OPPO)
Slide 4
Doc.: IEEE 802.11-25/0316r0
March 2025

## Slide 5
DL Preamble Design
  Additional preamble format, e.g., 802.11b preamble for backscattering
    Single carrier DSSS with BW 22MHz
    How to configure individual fields in preamble?
      SIGNAL can be configured with unsupported rate, so that other legacy devices can stop reception.
      Service field can be configured different from 802.11b or 802.11g and some bits can be used to indicate 802.11bp related information.
      Length can be configured to indicate only the DL part without excitation fields in DL PPDU.
    Differentiate 802.11bp from 802.11b and 802.11g.
Yinan Qi (OPPO)
Slide 5
Doc.: IEEE 802.11-25/0316r0
March 2025

## Slide 6
Synchronization
  Asymmetric synchronization design for UL and DL
    Different processing capability at AP and AMP non-AP STAs
    Different link budget for UL and DL
    Different sync sequences in terms of pattern and/or length for DL/UL to differentiate UL and DL
  DL synchronization design
    Synchronization sequence length: 16 bits for 1Mbps with high SNR and 32 bits for 250kbps with low SNR
    Chip duration: same chip duration for 1Mbps and 250kbps for reduced complexity at AMP non-AP STA side
  UL synchronization design
    A single synchronization sequence can be used for multiple data rates
    Chip rate can scale with data rate and short chip duration is used for higher rate with higher SNR to reduce signalling overhead
    AP can do blind detection trying various chip duration if lack of knowledge of UL data rate
Yinan Qi (OPPO)
Slide 6
Doc.: IEEE 802.11-25/0316r0
March 2025

## Slide 7
SIG Field
  DL SIG fields
    Length
    Backscatter indication: together with other fields can indicate CW info to energizers
    UL configuration to configure the following UL transmission in followed excitation field
      For backscatter devices, they can still transmit UL using excitation even without successful decoding of DL data, decouple DL data and UL
      Can be used by energizers to transmit CW
    CRC
  Pros of DL SIG
    SIG can convey useful information for energizers assuming AMP DL PPDU can be read by energizers
    Other AMP non-AP can read the length fields and go to sleep to save energy
  UL SIG might be needed in some cases
    AP has no knowledge of UL payload size, FEC if applied, and data rate if autonomously chosen by AMP non-AP devices [2]
Yinan Qi (OPPO)
Slide 7
Doc.: IEEE 802.11-25/0316r0
March 2025

## Slide 8
Payload Size
  Flexible payload size configuration for DL and UL
    Different from 802.11ba where many management and control frames are transmitted by the main radio
    Data frame
      ID(s) of AMP non-AP STAs for sensor reporting
      EH related information reporting
    Other frames
      Management frame such as triggering frame.
    For data frame, 802.11ba can still be a starting point
      Frame body is m*n
        m is the size of AMP non-AP STA ID, e.g., AID or compressed AID
        n is the number of AMP non-AP STAs to be addressed
  How to configure payload size?
    DL SIG or MAC header
Yinan Qi (OPPO)
Slide 8
Doc.: IEEE 802.11-25/0316r0
March 2025

## Slide 9
DL PPDU: Flexible BW and Waveform
  DL PPDU
    Different BW and waveforms can be considered for different fields including preamble, excitation, data, etc., to achieve optimized performance
  Active Tx
    Preamble: 20MHz with OFDM waveform
    AMP part: no less than 10 MHz but can be DSSS waveform
  Close-range backscattering
    Preamble
      20MHz with OFDM waveform
      22MHz with DSSS waveform
    AMP part
      Excitation field for activating: BW should not be too narrow
      Data field: same design as excitation
Yinan Qi (OPPO)
Slide 9
Doc.: IEEE 802.11-25/0316r0
March 2025

## Slide 10
DL PPDU: Flexible BW and Waveform
  Bi-static backscattering
    Different fields can be transmitted by separated nodes
      AP: DL sync, SIG and data
      Energizer: excitation
    Different BW and waveform is more applicable
  BW and waveform configuration
    Can either be pre-defined or flexibly configured
    Trade-off between performance and signalling overhead/complexity.
Yinan Qi (OPPO)
Slide 10
Doc.: IEEE 802.11-25/0316r0
March 2025

## Slide 11
PPDU Format
  DL PPDU format
    AMP device can be assumed with energy storage so the excitation part is purely for backscattering
    Sync may be needed for AMP devices to know when the backscattering begins
    AP has full control of the energizer to avoid misuse of excitation field
  UL PPDU format for backscattering
    UL PPDU for backscattering can be defined as follows:
      IEEE 802.11bp shall specify, in 2.4 GHz, an AMP UL PPDU for AMP non-AP STAs supporting backscattering transmission that contains at least AMP-UL-Sync field and AMP-UL-Data field.
      Note: This UL PPDU is backscattered by the AMP non-AP STA within one excitation field which can be contained in a DL PPDU
Doc.: IEEE 802.11-25/0316r0
March 2025
Notes: Preamble + Sync + excitation

## Slide 12
Summary
  The following issues are discussed and analysed in this contribution
    Preamble design
    Synchronization design for both DL and UL
    DL/UL SIG
    Payload size
    DL and UL PPDU format
Doc.: IEEE 802.11-25/0316r0
March 2025

## Slide 13: Reference
[1] “IEEE 802.11 TGbp Motion Dock,” IEEE 802.11-24/1322r6, Jan. 2025
[2] “AMP UL Transmission,” IEEE 802.11-25/0317r0, Mar. 2025
Doc.: IEEE 802.11-25/0316r0
March 2025

## Slide 14: SP 1
Doc.: IEEE 802.11-25/0316r0
March 2025
  The preamble of an AMP DL PPDU for AMP enabled non-AP STA and active TX non-AP AMP STA should be configured as follow,
    L-SIG
      Rate - configured as an unsupported rate
      Length - indicate only the DL part without excitation fields in DL PPDU
    U-SIG
      Version field - configured different from 802.11be and 802.11bn
      UL/DL - configured as DL if there is no excitation field and UL otherwise

## Slide 15: SP 2
Doc.: IEEE 802.11-25/0316r0
March 2025
  IEEE 802.11bp will specify, in 2.4 GHz, DL synchronization sequence length with length 16 bits for 1Mbps and 32 bits for 250kbps. Chip duration is the same for all data rates, e.g., 2us.

## Slide 16: SP 3
Doc.: IEEE 802.11-25/0316r0
March 2025
  IEEE 802.11bp will specify, in 2.4 GHz, a single UL synchronization sequence length with chip duration same as data field.

## Slide 17: SP 4
Doc.: IEEE 802.11-25/0316r0
March 2025
  An AMP Downlink PPDU shall contain an AMP-SIG field containing at least following information:
    Length indication
    Backscatter indication bit
    CRC
    UL configuration
      Details TBD

## Slide 18: SP 5
Doc.: IEEE 802.11-25/0316r0
March 2025
  IEEE 802.11bp will specify additionally, in 2.4 GHz, an AMP Downlink PPDU format containing at least an 802.11 preamble field and an Excitation field.
  AMP-Sync field is TBD

## Slide 19: SP 6
Doc.: IEEE 802.11-25/0316r0
March 2025
  IEEE 802.11bp shall specify, in 2.4 GHz, an AMP UL PPDU for AMP non-AP STAs supporting backscattering transmission that contains at least AMP-UL-Sync field and AMP-UL-Data field.
  Note: This UL PPDU is backscattered by the AMP non-AP STA within one excitation field which can be contained in a DL PPDU.