## Slide 1: AMP Energizer Control
Date: 2025-03-13
Authors:
Name | Affiliation | Address | Phone | Email
Yinan Qi | OPPO |  |  | v-qiyinan@oppo.com
Ke Wang |  |  |  | 
Weijie Xu |  |  |  | 
Doc.: IEEE 802.11-25/0318r0
March 2025

## Slide 2: Abstract
In this contribution, we discuss the following issues:
  AMP energizer control mechanism
  AMP energizer control signalling
Doc.: IEEE 802.11-25/0318r0

## Slide 3
Recap of Progress
  Agreement: IEEE 802.11bp defines a mechanism that allows control information to be sent by AMP AP STA to the AMP Energizer. The control information is TBD [1].
  Energizer can transmit WPT, excitation and potentially other signals, e.g., preamble, wake-up signal, etc.
  Two main challenges
    How does AP control the energizers and coordinate WPT/excitation signal transmission?
    What control information should be conveyed to the energizer?
Yinan Qi (OPPO)
Slide 3
Doc.: IEEE 802.11-25/0318r0
March 2025

## Slide 4
Wireless Energizer Control Topology [2]
  AP-AMP STA
    TGbp link for active Tx and backscatter AMP devices or legacy link for AMP enabled devices with operation frequency 2.4GHz
  Energizer-AMP STA
    Communication: TGbp link for AMP devices, e.g., excitation, preamble, etc., on 2.4GHz
    WPT: S1G
  AP-energizer:
    Both legacy link and TGbp link can be supported
    Energizer is a new type of devices and thus can be designed to receive TGbp signals
Yinan Qi (OPPO)
Slide 4
Doc.: IEEE 802.11-25/0318r0
March 2025

## Slide 5
Energizer Capability
  Energizer can be regarded as a non-AP STA and follow the conventional association/authentication procedure to connect to the AMP AP.
  Energizer may have different capability depending on design requirements.
    Energizer may not be able to operate on both 2.4GHz and S1G;
    Energizer might not be willing to active at any time if on battery;
    Etc.
  Energizer needs to report its own WPT related capability to the AMP AP proactively when connected to the AP or passively based on the request of the AP.
    Supported frequency and BW for WPT/excitation
    Maximum Tx power and whether or not the Tx power is adjustable
    ID(s) of associated AMP devices that can be wirelessly charged or excited
    Whether or not rely on battery
    Its own position
  Capability reporting only needs to be done one time.
Yinan Qi (OPPO)
Slide 5
Doc.: IEEE 802.11-25/0318r0
March 2025

## Slide 6
General WPT Procedure: Initialization
  WPT can be initialized by requesting for energizer and AMP reporting to initialize the WPT configuration.
  Report procedure can be either AP requested or autonomously done by energizer or AMP devices.
Yinan Qi (OPPO)
Slide 6
Doc.: IEEE 802.11-25/0318r0
March 2025

## Slide 7
General WPT Procedure: Charging Procedure
  WPT procedure:
    AMP requests WPT (optional)
    AP send WPT related parameters to energizer
    Energizer acks AP request and initiate WPT
    WPT and Tx/Rx procedures can repeat
  AP can coordinate the energizer and AMP STA in TDM or FDM manner. For example, channel access is done by the AP and AP reserves the channel for both energizer and AMP STA.
  WPT duration should be longer than certain threshold to guarantee the AMP devices are sufficiently charged.
Yinan Qi (OPPO)
Slide 7
Doc.: IEEE 802.11-25/0318r0
March 2025

## Slide 8
Energizer Control Signalling: Parameters
  Energizer sleep or active
  WPT frequency related information including central frequency, bandwidth, etc.
  WPT on/off
  WPT on/off duration
    Duty cycle operation related information, e.g., period, on duration, etc., when WPT is on
  Indication the operation frequency: S1G or 2.4GHz
  DL PPDU format for 2.4GHz if supported
    Wakeup signal/PPDU format or parameters to define wakeup signal/PPDU, e.g., data rate, modulation scheme, etc.
  WPT PPDU format if supported
    Charging field related parameters: starting time, BW, waveform and Tx power.
Yinan Qi (OPPO)
Slide 8
Doc.: IEEE 802.11-25/0318r0
March 2025

## Slide 9
Summary
  In this contribution, we discussed energizer capability, control mechanism and control signalling.
Yinan Qi (OPPO)
Slide 9
Doc.: IEEE 802.11-25/0318r0
March 2025

## Slide 10: Reference
[1] “IEEE 802.11 TGbp Motion Dock,” IEEE 802.11-24/1322r6, Jan. 2025
[2] “Further Consideration of WPT for AMP,” IEEE 802.11-24/1781r2, Nov. 2024.
Doc.: IEEE 802.11-25/0318r0
March 2025

## Slide 11
SP1
  Energizer should report its capability to AMP AP. The parameters to be reported is TBD.
Yinan Qi (OPPO)
Slide 11
Doc.: IEEE 802.11-25/0318r0
March 2025

## Slide 12
SP2
  The following parameters can be considered for AP to control the energizer
    Energizer sleep or active
    WPT frequency related information including central frequency, bandwidth, etc.
    WPT on/off
    WPT on/off duration
      Duty cycle operation related information, e.g., period, on duration, etc., when WPT is on
    Indication the operation frequency: S1G or 2.4GHz
Yinan Qi (OPPO)
Slide 12
Doc.: IEEE 802.11-25/0318r0
March 2025