## Slide 1: Access message for AMP
Date: 2025-3-6
Authors:
Name | Affiliation | Address | Phone | Email
Weijie Xu | OPPO |  |  | xuweijie@oppo.com
Ke Wang |  |  |  | 
Doc.: IEEE 802.11-25/0322r0
March 2025

## Slide 2: Abstract
This submission is to discuss the first access message send by AMP device after being triggered. Generally, we will discuss:
  The access message for backscattering device.
  The access message for active device.
    CDM access is able to provide more access opportunities compared without CDM(e.g. only use TDM and/or FDM) for active device.
Doc.: IEEE 802.11-25/0322r0

## Slide 3
Weijie Xu (OPPO)
Slide 3
Doc.: IEEE 802.11-25/0322r0
March 2025
  In RFID, slot-aloha is used as the access procedure.
    It uses 2-step access, RN16 is the 1st message that RFID device send to the interrogator after being queried.
    The payload size of RN16 message is much smaller than that of a EPC code message. When there is collision, the system loss of using RN16 as the 1st message is smaller than that of directly sending EPC code.
    Therefore, 2-step access can be considered for AMP, as also proposed in [2][3].
      Figure: 2-step multiple access[2]
Background(1)

## Slide 4
Background(2)
  In [1], CDM access code, as the 1st access message, was discussed on the following aspects:
    Motivation and use case of using CDM access
    Access procedure of CDM access
    Feasibility of supporting CDM access for AMP, considering non-ideal factors such as:
      Synchronization error
      Clock drifting
    Comparison of CDM codes and legacy RN16
  Based on the discussion, we have the following observations:
    For active AMP STA, there is obvious advantage of CDM access code than RN16, when there is collision on the same access resource.
    With proper selection of the CDM codes (e.g. use big cyclic shift to overcome the potential timing misalignment), the impact from synchronization error can be easily handled, at least for active AMP device, with a clock accuracy of 1000ppm
  Thus we proposed to support CDM access code for at least active AMP device[1].
Weijie Xu (OPPO)
Slide 4
Doc.: IEEE 802.11-25/0322r0
March 2025

## Slide 5
ReCap(1): Access procedure with CDM codes
Weijie Xu (OPPO)
Slide 5
Doc.: IEEE 802.11-25/0322r0
March 2025
  CDM code will be the first message from AMP device when it is triggered/polled.
  When CDM code is detected by AP, this CDM code can be used to identify AMP device for the consequent communication.
    Since the AMP device is identified, the following transmission can be scheduled by AP thus there will be no collision any more.
    Figure 1 Triggered CDM codes from multiple AMP STAs

## Slide 6
ReCap(2): Feasibility of supporting CDM access for AMP
Weijie Xu (OPPO)
Slide 6
Doc.: IEEE 802.11-25/0322r0
March 2025
  Although with low complexity, AMP device is able to generate CDM code.
      As discussed in [6], OOK waveform is proposed as the uplink waveform. There are candidate binary CDM codes (e.g. m/Gold sequence) that can work in conjunction with OOK.
  Impact of non-ideal factors
      Synchronization error
        CDM sequence from different AMP devices may be not synchronous at the beginning of transmission due to different distance from the AP or different clock drifting time
      Clock drifting
        During the transmission, the relative distance of two CDM sequence may change due to different clock drifting rate of different AMP devices.

## Slide 7
ReCap(2): Feasibility of supporting CDM access for AMP
Weijie Xu (OPPO)
Slide 7
Doc.: IEEE 802.11-25/0322r0
March 2025
  Analysis of non-ideal factors
    Analysis:
      RTT of different AMP STA
        The coverage of one AMP AP will be 10m~20m, so the RTT(Round Trip Time) is only 0.067us~0.133 us
      Drifting
        For active device with clock accuracy of 1000ppm, the max drifting time after a time duration of 2ms is 2us.
        For active device with clock accuracy of 1000ppm, for a CDM sequence of length 63, the symbol level misalignment between 2 CDM sequences is less than 1/10 OOK symbol (for one bit of the sequence)

## Slide 8
ReCap(3): Exemplary CDM Code for AMP
Weijie Xu (OPPO)
Slide 8
Doc.: IEEE 802.11-25/0322r0
March 2025
  Both M sequence and gold sequence are binary sequences. AMP device is able to generate m or gold sequence with low-complexity implementation.
    M or Gold sequence can be generated with OOK waveform
  Both m sequence and Gold sequence have good auto-correlation and cross-correlation.
  Sufficient number of sequences can be generated with m sequence/Gold sequence and their cyclic-shift sequences.
Auto-correlation of M sequence

## Slide 9
ReCap(4): Simulation
Weijie Xu (OPPO)
Slide 9
Doc.: IEEE 802.11-25/0322r0
March 2025
  Link level simulations are performed for CDM codes with the following simulation assumptions.
  Table 1: Simulation assumptions
Parameters | Values
Sequence types | m-sequence,
Number of devices / sequences | 2
Channel model | Channel D
SNR | 0.0dB
Chip duration | 2µs
Sampling rate at the AP | 20MHz
Modulation | OOK
Cyclic shift of m- and Gold sequences | 10
Sequence length | 63
Clock accuracy | +-1000ppm

## Slide 10
Case 1
Weijie Xu (OPPO)
Slide 10
Doc.: IEEE 802.11-25/0322r0
March 2025
  2 Users transmit CDM code on the same resource. 2 codes are aligned in the beginning of transmission. Channel D, 1000ppm.
    Equal or non-equal receiving power at the AP side
2 AMP STAs, equal power
2 AMP STAs, 10dB power difference

## Slide 11
Case 2
Weijie Xu (OPPO)
Slide 11
Doc.: IEEE 802.11-25/0322r0
March 2025
  2 CDM codes are not synchronous at the beginning and there is a 2us mis-alignment (Corresponding to 1 chip and 40 sampling points) between the 2 CDM sequence, Channel D, 1000ppm.
2 AMP STAs, Aligned
2 AMP STAs, 2us timing misalignment

## Slide 12
ReCap(5): Comparison of CDM codes and RN16(1)
Weijie Xu (OPPO)
Slide 12
Doc.: IEEE 802.11-25/0322r0
March 2025
  RN16 is used as access code in RFID. It is fragile in case of collision and channel fading.
  Under the same situation, CDM code is better than RN16.
      When the receiving power from multiple AMP STAs has similar power, CDM codes with similar power outperforms RN16 based on the simulations.
      When the receiving power from multiple AMP STAs are different (e.g. 10dB difference)
        For RN16, at most one RN16 may be decoded correctly and the other will fail
        For CDMA, at least one CDMA code can be correctly decoded and there is probability to correctly decode another one.

## Slide 13
ReCap(5): Comparison of CDM codes and RN16(2)
Weijie Xu (OPPO)
Slide 13
Doc.: IEEE 802.11-25/0322r0
March 2025
  When RN16 from multiple AMP STAs collides on the same resources, and the receiving power from multiple AMP STAs are similar, RN16 from all the AMP STAs can’t be decoded.
Decoding performance of RN16 when there is collision

## Slide 14
Access message for BC device(1)
  For backscattering device, especially for the device with similar device capability as RFID’s, it has poor clock accuracy, i.e., 10^4 ppm~10^5 ppm, it is difficult to support CDM access.
  Alternatively, RN16-like access message can be used for backscattering device.
  Requirements for RN16-like access message:
    Carry access information  access ID etc.
    Sufficient capability, to avoid different AMP STAs to select same random code the longer, the higher capability
    Good decoding performance  the short, the better performance
Weijie Xu (OPPO)
Slide 14
Doc.: IEEE 802.11-25/0322r0
March 2025

## Slide 15
Access message for BC device(2)
  Therefore, the following is proposed for access message for BC device
    RN16-like access code is supported for BC device
    The length of the access code can be different for different application scenario, i.e. depending on the number of deployed AMP devices
    Carry access information  access ID etc.
    An UL PPDU is defined for the access message.
Weijie Xu (OPPO)
Slide 15
Doc.: IEEE 802.11-25/0322r0
March 2025

## Slide 16
Summary
  For the access message,
    CDM access code is proposed for active AMP STA.
    Random Number is proposed for backscattering STA.
      The length of Random number can be variable depending on the use cases
      Access information can be carried in the access message.
Weijie Xu (OPPO)
Slide 16
Doc.: IEEE 802.11-25/0322r0
March 2025

## Slide 17
Straw Poll #1
Weijie Xu (OPPO)
Slide 17
Doc.: IEEE 802.11-25/0322r0
March 2025
Do you agree with the following text:
  CDM access is supported for active AMP STA.
Yes
No
Abstain

## Slide 18: Reference
IEEE 802.11-25/0035r1, CDM access for AMP
IEEE 802.11-25/0031r0 Trigger based multiple access for AMP
IEEE 802.11-25/0046r0 Channel access for Active Tx non-AP AMP STAs
Doc.: IEEE 802.11-25/0322r0
March 2025