## Slide 1: Thoughts on Dynamic Context Transfer in 11bn
Date: 2024-12-01
Authors:

## Slide 2: Abstract
Dynamic context transfer can be important to ensure data continuity in seamless roaming in next generation Wi-Fi networks.
Sequence number is one of the important parameters that can be transferred as a part of dynamic context transfer.
We discuss an issue that can occur with SN transfer and discuss a solution that can be used to address the issue.

## Slide 3: Seamless Roaming Background
Seamless roaming procedures enable a non-AP MLD to transition from current AP MLD to target AP MLD while remaining in state 4 thereby preserving the context for data transmission.
Seamless roaming can involve multiple procedures to enable a smooth transition [1]:
  Discovery stage: discover neighboring APs in the domain
  Preparation stage: prepare candidate AP MLDs and non-AP MLDs for the smooth transition
  Setup stage: setup links, near static context transfer
  Transition stage: exchange of TBD request/response frames

## Slide 4: SN Transfer
Sequence number assignment at the transmitter
  Useful for duplicate frame filtering
  Represented by a modulo 4096 counter starting at 0 and incrementing by 1 for each MSDU
As a part of the roaming procedure [2]:
  Non-AP MLD can transmit a TBD roaming request frame to the current AP MLD
  Upon reception of the TBD roaming request frame, the current AP MLD shall transfer context that is required for resuming operations with the target AP MLD. The context that can be transferred include:
    Next SN to be assigned for DL individually addressed data frame of each TID
50 | 51 | 52 | 53 | 54 |  |  |  |  |  |  |  |  |  | 
55 | 56 | 57 | 58 | 59 | 60 | … |  |  |  |  |  |  |  | 
SN assignment at current AP MLD for TID N
SN assignment at target AP MLD for TID N
Last assigned SN when SN transfer is initiated
First assigned SN at target AP MLD
Notes: Need a figure here.

## Slide 5: Problem Statement
When a roaming request is initiated by the non-AP MLD, the DL traffic can still continue to arrive as the backend application server continues to send the traffic.
The DL incoming traffic can still continue to flow to the current AP and will need sequence number assignment.
If the first unassigned SN is transferred to the target AP MLD, it may cause some issues with SN assignment with incoming MSDUs.
Buffering and not transmitting such MSDUs can result in DL data pause which may not be preferred for some applications.
50 | 51 | 52 | 53 | 54 |  |  |  |  |  |  |  |  |  | 
55 | 56 | 57 | 58 | 59 | 60 | … |  |  |  |  |  |  |  | 
SN assignment at current AP MLD for TID N
SN assignment at target AP MLD for TID N
Last assigned SN when SN transfer is initiated
First assigned SN at target AP MLD
SN cannot be assigned to new incoming MSDUs

## Slide 6: SN Reserve
AP can maintain a SN reserve to assign SN to incoming MSDUs.
Reserve size can be computed based on pre-known information. E.g., prior load/traffic characteristics of the non-AP MLD coupled with the typical time it takes to complete the network side procedures.
A procedure to update SN at the non-AP MLD will be needed. Update can either come from the current AP MLD (e.g., in the response/BAR) or from the target AP MLD.
50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | … |  |  | X |  |  | 
SN assignment at current AP MLD for TID N
Last assigned SN when SN transfer is initiated
SN reserve
Large enough to suffice for possible incoming MSDUs.

## Slide 7: Conclusion
Dynamic context transfer is a key procedure necessary to ensure data continuity.
In this contribution, we discuss an issue that can occur with SN transfer.
We propose keeping an SN reserve at the current AP MLD to address the issue.