## Slide 1: AMP DL OOK Generation
Date: 2025-03-10
Authors:
Name | Affiliation | Address | Email
Panpan Li | Huawei | Singapore | lipanpan25@huawei.com
Bin Qian |  | Shenzhen, China | 
Lumin Liu |  | Singapore | 
Lei Huang |  | Singapore | 

## Slide 2: Abstract
This contribution intend to discuss some remaining issues related to backscattering operation
  Encoding and modulation
  DL OOK generation

## Slide 3: Remaining issues related to encoding and modulation
Issues
  Encoding of AMP Downlink PPDU AMP-Data field for backscattering operation is TBD
  Modulation of AMP Uplink PPDU AMP-Sync field and AMP-Data field for backscattering operation is TBD
Proposal
  Propose to use Manchester encoding for the AMP Downlink PPDU AMP-Data field for backscattering operation.
    Keeping consistent with non-backscattering operation as mentioned in [1]
  The AMP Uplink PPDU AMP-Sync field and the AMP-Data field will use On-Off Keying (OOK) modulation for backscattering operation.
    Keep consistent with non-backscatter UL
    OOK modulation is easy to implement for STA side

## Slide 4: Remaining issues related to AMP DL OOK
Motion #30 [2]:
  The (3dB) bandwidth of the AMP DL PPDU in 2.4 GHz is at least 10 MHz for backscattering communication. The transmit spectrum mask is TBD.
OOK generation：
  [3] pointed out DSSS based OOK has advantages including better performance, no new hardware requirement and flexibility to support different data rates. Another spreading code with less randomization was proposed to replace Barker code to generate a narrow bandwidth DSSS signal.
  [4] proposed wideband DSSS-OOK for backscattering operation and new spreading sequences to achieve specific bandwidths.
  [5] proposed wideband MC-OOK generation to achieve 12-15MHz BW.
Problems to be solved:
  Generation of wideband OOK is TBD
This contribution will compare the performance of DSSS-OOK and MC-OOK for backscattering operation.

## Slide 5: Simulation results: DL
DL PPDU AMP-data field PER comparison between DSSS-OOK (11b) and MC-OOK (WUR)
  SNR is defined on 22MHz BW
DSSS based waveform achieve better performance than MC-OOK!
DSSS
MC-OOK
Simulation setting:
Data rate: 250kbps
AWGN channel
Tx side:
  Packet size = 160 bits
  Manchester encoding
  no filter
Rx side:
  Fs_Rx=2 MHz
  no LPF
Clock accuracy: 0ppm

## Slide 6: Simulation results: UL for Mono-static backscatter
UL PPDU AMP-data field PER comparison between DSSS-OOK (11b) and MC-OOK (WUR)
Simulation setting:
Data rate: 250kbps
AWGN channel
AP side:
  Packet size = 160 bits
  Manchester encoding
  Antenna isolation: 20dB
  Leakage: 0dBr
  Rx noise: -45dBr
  No Tx filter
  with Rx filter
  Non-coherent detector
STA side:
  Modulation noise: -20dBr
  Backscatter loss: 5dB
  No Tx filter
Clock accuracy: 0ppm
Note: Signal attenuation is defined as Friis channel path loss of DL+UL
DSSS
MC-OOK
Signal attenuation (dB)
0.177 | 0.158 | 0.141 | 0.125 | 0.112 | 0.099 | 0.089 | Distance (m)
Notes: 5%

## Slide 7: Simulation results: UL for Bi-static backscatter
Simulation setting:
Data rate: 250kbps
Energizer side:
  EIRP: 20dBm
  Leakage: with path loss of distance (d+1) meter
  No Tx filter
AP side:
  Rx noise: -70dBm
  with Rx filter
  Non-coherent detector
STA side:
  Packet size = 160 bits
  Manchester encoding
  Modulation noise: -20dBr
  Backscatter loss: 5dB
  No Tx filter
Clock accuracy: 0ppm
Note: Signal attenuation is defined as Friis channel path loss of distance d
DSSS
MC-OOK
Signal attenuation (dB)
AP
STA
Energizer
d
Leakage
1m
3.146 | 2.499 | 1.985 | 1.577 | 1.252 | 0.995 | 0.79 | Distance (m)
Notes: 10%

## Slide 8: Summary
This contribution discussed the AMP DL OOK generation
  DSSS OOK achieves better performance than MC-OOK.

## Slide 9: Reference
[1] 11-24-1797-00-00bp-design-considerations-of-dl-data-rate-and-sync
[2] 11-24-1322-06-00bp-tgbp-motion-dock
[3] 11-24-1802-00-00bp-ook-generation-for-amp-dl
[4] 11-25-0050-01-00bp-amp-dl-wideband-ook-generation
[5] 11-25-0051-01-00bp-signal-design-for-ook

## Slide 10: SP 1
Do you agree to add the following text to TG bp SFD?
  The AMP Downlink PPDU AMP-Data field will use Manchester encoding for backscattering operation.
  Yes
  No
  Abstain

## Slide 11: SP 2
Do you agree to add the following text to TG bp SFD?
  The AMP Uplink PPDU AMP-Sync field and the AMP-Data field will use On-Off Keying (OOK) modulation for backscattering operation.
  Yes
  No
  Abstain

## Slide 12: SP 3
Do you agree to add the following text to TG bp SFD?
  DSSS based OOK is supported for AMP DL backscattering operation.
  Yes
  No
  Abstain