## Slide 1: IMMW PPDU Format
Date: 2025-03-10
Authors:

## Slide 2: Introduction
Integrated mmWave (IMMW) PAR [1] defines the scope to leverage or reuse existing 802.11 OFDM PHY
In this presentation, we share high-level thoughts on IMMW PHY design and PPDU format
  Achieves better efficiency, design simplification and supports beam training/tracking.

## Slide 3: IMMW PHY Scope [2-8]
OFDM MIMO:
  Limit to single user (SU) OFDM PHY
  Digital MIMO limit to 2 spatial streams
Modulation and Coding:
  Reuse existing modulation and coding combinations
  Modulation limits to 64 QAM
  Coding limits to LDPC only
Tone plan
  Reuse sub-7GHz tone plan with upclocking, e.g. VHT with 8x
  Signal BW: max 1.28GHz, min 160MHz or 320MHz
Coex:
  OFDM PHY preamble no need to be decodable by DMG/EDMG devices

## Slide 4: Recap: sub-7GHz PPDU format
L-SIG
Data
11a/g
LENGHTH%3 = 0
L-LTF
L-STF
L-SIG
HT-SIG1
HT-STF/LTF/Data
L-LTF
L-STF
HT-SIG2
L-SIG
VHT-SIGA1
L-LTF
L-STF
VHT-SIGA2
L-SIG
RL-SIG
HE-SIGA1
HE-SIGA2
HE-STF/LTF/Data
L-LTF
L-STF
LENGHTH%3 = 0
LENGHTH%3 = 1
L-SIG
RL-SIG
HE-SIGA1
HE-SIGA2
HE-STF/LTF/Data
L-LTF
L-STF
LENGHTH%3 = 2
HE-SIGB
L-SIG
HE-STF/LTF/Data
RL-SIG
HE-SIGA1
HE-SIGA2
L-LTF
L-STF
HE-SIGA3
HE-SIG-A4
HT MF
VHT
HE SU/TB
HE MU
HE ER SU
L-SIG
RL-SIG
U-SIG1
U-SIG2
L-LTF
L-STF
LENGHTH%3 = 0
EHT-STF/LTF/Data
EHT MU/TB
VHT-STF/LTF/Data
PE
PE
PE
PE
UHR MU/TB
PHY version = 0
L-SIG
RL-SIG
L-LTF
L-STF
U-SIG1
U-SIG2
PHY version = 1
LENGHTH%3 = 0
UHR-STF/LTF/Data
PE

## Slide 5: IMMW PHY PPDU
IMMW PPDU design should inherit the merits of latest EHT/UHR PPDU definition in sub-7GHz
Preamble can be simplified without legacy burden
  Unified explicit PPDU format detection
  Better interoperability including future generation
  Support SU transmission, but ready to extend to advanced features
NDP format can be expanded for
  digital channel sounding, and
  analogue beam training/tracking
No Control PHY
  E.g. 160MHz SU MCS0 is the range

## Slide 6: IMMW PPDU Format
PPDU Formats:
  IMMW SU PPDU: data payload
  IMMW DUP PPDU: control frame
  IMMW NDP PPDU: variant of SU PPDU
    e.g. beam training, channel sounding, beacon

## Slide 7: IMMW SU PPDU
  Legacy portion (L-STF/LLTF): same as sub-7GHz mixed format OFDM PPDU, and reuse the same packet detection logic
    Upclocked from 20MHz tone plan, e.g. 8x upclock to 160MHz
  U-SIG: directly to indicate the forward compatibility
    U-SIG replaces old L-SIG:
      Better CRC protection: One-bit parity in L-SIG causes false trigger issues
      More coex information can be signaled
    Version independent fields: fixed definition for future generations [2].
      e.g. PHY_version_identifier, BSS Color, TXOP, DL/UL, BW, etc.
      Add LENGTH field to indicate duration of the PPDU
    May further include version dependent fields
      e.g. IMMW-SIG symbols, IMMW-SIG MCS, PPDU format
LSTF | LLTF | U-SIG | IMMW SIG | IMMW STF | IMMW LTF | Data | PE

## Slide 8: IMMW SU PPDU (Cont.)
IMMW-SIG
  Information bits needed to decode or parse the PPDU
    e.g. user specific information (MCS, Nss, coding, etc.)
  Beam training (TRN) field parameters: NDP
IMMW STF/LTF: gain and channel refinement
Data portion can reuse 11ac/11ax OFDM tone plan
PE: packet extension field
  to provide extra time for receiver to turnaround
  PE may be reused for beam refinement

## Slide 9: IMMW PPDU: Wide BW
WideBW extension
  IMMW may define multiple PPDU BW, e.g. 160MHz, 320MHz, 640MHz, 1280MHz, etc.
  Leverage the design in sub-7GHz OFDM, WideBW is extended from base BW for better coex
    L-STF to IMMW-SIG: FD duplicated from base BW
    IMMW-STF/LTF/Data/PE: use new wideBW tone plan, e.g. sub-7GHz 40MHz/80MHz/160MHz
LSTF | LLTF | U-SIG | IMMW SIG | IMMW STF | IMMW LTF | Data | PE
LSTF | LLTF | U-SIG | IMMW SIG |  |  |  | 
… | … | … | … |  |  |  | 
LSTF | LLTF | U-SIG | IMMW SIG |  |  |  | 

## Slide 10: IMMW DUP PPDU
PPDU for MAC control frames
  Needed for devices with different bandwidth can decode the control frame, e.g. (MU-)RTS/CTS/BA/ACK/NDPA
  IMMW-SIG may be skipped
LSTF | LLTF | U-SIG | IMMW SIG | Data | PE
LSTF | LLTF | U-SIG | IMMW SIG | Data | PE
… | … | … | … | Data | PE
LSTF | LLTF | U-SIG | IMMW SIG | Data | PE

## Slide 11: IMMW NDP
NDP can serve the purpose of both analogue beam training (e.g. SLS, BRP) and digital beamforming channel sounding
IMMW NDP is a variant of SU PPDU without data symbols
  One TRN field is used for channel sounding
  More TRN fields to be included for beam training
IMMW STF | IMMW LTF | IMMW LTF | IMMW LTF | … | … | PE
LSTF | LLTF | U-SIG | IMMW SIG
LSTF | LLTF | U-SIG | IMMW SIG
… | … | … | IMMW SIG
LSTF | LLTF | U-SIG | IMMW SIG
IMMW STF | IMMW LTF | IMMW LTF | IMMW LTF | … | … | PE
LSTF | LLTF | U-SIG | IMMW SIG
TRN
TRN

## Slide 12: Need of Extended Range PPDU?
Use cases
  Extend the uplink link budget to increase the data exchange range
  Extend BRP training range: no control PHY
    Legacy preamble is steered with SLS beam (or current beam)
    Bridge the gap between optimal SLS beam and optimal BRP beam
Option 1: No IMMW ER PPDU
  Limit the training range with SLS optimal beam
  Use the smallest BW PPDU for beam training
Option 2: Simple design with similar PPDU format
  E.g. extend by ~3dB with pre-amble power boost
  Serve the purpose to bridge the gap between SLS and BRP range

## Slide 13: Summary
Discuss about high-level IMMW PHY scope
  OFDM should be reused
  Limit to SU and 2ss MIMO
  Limit to 64QAM and 1.28GHz BW
  No control PHY
IMMW PPDU design philosophy
  Simple PPDU format detection state machine
  Future generation interoperability
Three PPDU Formats:
  IMMW SU PPDU, IMMW DUP PPDU, IMMW NDP PPDU
  Discussed about potential IMMW ER PPDU

## Slide 14: Reference
[1] P802.11bq_PAR, https://www.ieee802.org/11/PARs/P802.11bq_PAR.pdf
[2] 11-22-0046-01-0wng-next-generation-after-802-11be
[3] 11-22-0729-01-0wng-next-generation-after-802-11be-follow-up
[4] 11-22-1872-00-0uhr-considerations-on-phy-designs-for-mmwave-band
[5] 11-22-1395-00-0uhr-thoughts-on-high-frequency-band
[6]11-23-0066-02-0uhr-thoughts-on-utiliizing-mmwave
[7] 11-23-1878-01-immw-high-level-design-considerations-of-immw
[8] 11-23-1968-00-immw-discussion-on-general-direction-of-integrated-mmwave

## Slide 15: SP
Do you agree that IMMW defines three PPDU formats: SU PPDU, DUP PPDU and NDP PPDU?
  Note: NDP PPDU can be a variant of SU PPDU

## Slide 16: SP
Do you agree that IMMW PPDU preamble uses mixed format, starting with L-STF, L-LTF and U-SIG?

## Slide 17: SP
Do you agree that the legacy portion of the wide BW IMMW PPDU preamble is duplicated in frequency domain?