## Slide 1: Improvement on Co-BF Sounding
Date: 2025-3-9
Authors:

## Slide 2: Introduction
UHR defines 2 Co-BF sounding sequences: sequential and joint [1].
  In both sounding procedure, whether the responding AP transmit the NDP is controlled by initiating AP using UHR NDPA.
[2] puts forward that UHR Co-BF sounding reuses the EHT sounding segmentation and retransmission rules:
  A UHR Co-BF beamformer that fails to receive some or all of the feedback segments of the EHT compressed beamforming/CQI report from the UHR Co-BF beamformee shall not use a BFRP Trigger frame to request retransmission of the feedback segments. In this case, the UHR Co-BF beamformer may repeat the entire sounding sequence.
However, based on the existing mechanism, the initiating AP does not know that the responding AP fails to receive the CSI feedback from OBSS STA.
In this presentation, we will share our solution on this case.

## Slide 3: Problem
If responding AP fails to receive the CSI feedback from OBSS STA, initiating AP does not know this situation, which will cause Co-BF transmission failed.
Initiating AP may need this information and reschedule responding AP to repeat the cross-BSS sounding.
AP2 fails to receive CSI feedback from OBSS STA.
AP2 fails to receive CSI feedback from OBSS STA.

## Slide 4: Solution 1
Solicited
  After cross-BSS sounding, initiating AP triggers responding AP to report whether it has successfully received the CSI feedback from OBSS STA.
  The Cross-BSS sounding and trigger+ response may in same or different TXOP.

## Slide 5: Solution 2
Unsolicited
  When responding AP competing a TXOP, it can report to the initiating AP whether it has successfully received the CSI feedback from OBSS STA
    The CSI feedback can be from cross-BSS sounding of sequential sounding or joint sounding.
  The report frame may be a new action frame.

## Slide 6: Summary
In this contribution, we found some issues in Co-BF sounding:
  The initiating AP does not know that the responding AP fails to receive the CSI feedback from OBSS STA.
To solve this problem, two solutions are proposed:
  Solution 1: Solicited, initiating AP trigger + responding AP response.
  Solution 2: Unsolicited, responding AP report by itself.

## Slide 7: SP
Do you support include the following text to TGbn SFD?
  In UHR Co-BF sounding, defining a mechanism for responding AP to report whether it has successfully received the CSI feedback from OBSS STA.

## Slide 8: References
[1] Draft P802.11bn_D0.1
[2] 11-25-0081-00-00bn-sounding-pdt-related-issues