## Slide 1: Suggested Parameter Indication for Seamless Roaming
Date: 2024-08-01
Authors:

## Slide 2: Abstract
Near-static context transfer is one of the key aspects of seamless roaming procedure:
  Enables a non-AP MLD to prepare the target AP MLD with necessary setups prior to roam
In this contribution we discuss some information items which can benefit the device side if included in context transfer signaling:
  Suggested parameter indication: Parameters suggested by target AP MLD incase a context was not transferred/rejected by the target AP MLD.

## Slide 3: Context Transfer Background
A device may have set up more than one feature with the current AP.
Setting up each of the features one by one with the target AP can take multiple frame exchanges which is not desired.
As the device roams to a target AP, it is important that the features setup by STA with the current AP are also setup on the target AP.
Two types of context:
  Near static: setups which do not change on a short time scale.
    Limit to a few features
  Dynamic: which can keep changing on a short time scale.
Context | Type
Seq Number (SN) | Dynamic
Packet Number (PN) | Dynamic
BA context | Dynamic
BA setup | Near Static
SCS/MSCS | Near Static
EPCS | Near Static
TWT and variants (bTWT, rTWT, etc.) | Near Static
P2P TWT/CoEx session | Near Static
Example features that can benefit from context transfer

## Slide 4: Near Static Context Transfer
Near static context transfer procedure can enable a non-AP MLD to prepare a target AP MLD with necessary setups for its operation upon roam.
In this contribution, we discuss some information items whose inclusion in the context transfer signaling is critical or beneficial for the non-AP MLD.

## Slide 5: Suggested Parameter Indication
Target AP MLD may not be able to support the context of the non-AP MLD as is but may support with a modified parameter set.
  E.g., non-AP MLD has setup an SCS session with a QoS char IE indicating a delay bound of 30ms with the current AP MLD. Target AP MLD may not be able to support the same delay bound but may be able to support a higher delay bound (say 40ms).
Target AP MLD can provide suggested parameters which can be included in the context transfer response frame to the non-AP MLD.
This can enable the non-AP MLD to setup the feature faster upon roaming.
  In the above example, if the non-AP MLD chooses to roam to that target AP MLD, it can request a delay bound of 40ms upon roaming if that fits its requirements. This can enable faster convergence.
Non-AP MLD
Current AP MLD
Target AP MLD
Context transfer req
Near static context transfer
Context transfer resp<…, suggested parameter indication,…>

## Slide 6: Conclusion
In this contribution, we discussed signaling details for near static context transfer.
  Suggested parameter indication