## Slide 1: Deadline Indications for Seamless Roaming
Date: 2024-08-01
Authors:

## Slide 2: Abstract
Near-static context transfer is one of the key aspects of seamless roaming procedure:
  Enables a non-AP MLD to prepare the target AP MLD with necessary setups prior to roam
In this contribution we discuss some information items which can benefit the device side if included in context transfer signaling:
  Roam deadline indication: Indication of time until which the device has to roam to the target AP MLD for the target AP MLD to respect the context transfer.
  Timeout indication: Indication of the time until which the links at the current AP MLD can be maintained.

## Slide 3: Context Transfer Background
A device may have set up more than one feature with the current AP.
Setting up each of the features one by one with the target AP can take multiple frame exchanges which is not desired.
As the device roams to a target AP, it is important that the features setup by STA with the current AP are also setup on the target AP.
Two types of context:
  Near static: setups which do not change on a short time scale.
    Limit to a few features
  Dynamic: which can keep changing on a short time scale.
Context | Type
Seq Number (SN) | Dynamic
Packet Number (PN) | Dynamic
BA context | Dynamic
BA setup | Near Static
SCS/MSCS | Near Static
EPCS | Near Static
TWT and variants (bTWT, rTWT, etc.) | Near Static
P2P TWT/CoEx session | Near Static
Example features that can benefit from context transfer

## Slide 4: Near Static Context Transfer
Near static context transfer procedure can enable a non-AP MLD to prepare a target AP MLD with necessary setups for its operation upon roam.
In this contribution, we discuss some information items whose inclusion in the context transfer signaling is critical or beneficial for the non-AP MLD.

## Slide 5: Roam Deadline Indication
Target AP MLD may not be able to indefinitely commit to the accepted contexts.
Target AP MLD can provide a roam deadline to the non-AP MLD.
  If the non-AP MLD roams within the deadline, the target AP MLD can respect the accepted near static contexts.
  If the non-AP MLD roams after the deadline, the target AP MLD may need the non-AP MLD to re-setup all the contexts again.
Non-AP MLD
Current AP MLD
Target AP MLD
Context transfer req
Near static context transfer
Context transfer resp<…,roam deadline,…>
Roam req
Roam resp
Roam deadline

## Slide 6: Timeout Indication
There can also be a deadline that can be provided in the roam response frame.
This deadline can be a timeout period until which the links at the current AP MLD may not be deleted.
Non-AP MLD
Current AP MLD
Target AP MLD
Context transfer req
Near static context transfer
Context transfer resp
Roam req
Roam resp<..,Timeout,..>
Timeout: links at current AP MLD can be deleted after timeout

## Slide 7: Conclusion
In this contribution, we discussed signaling details for near static context transfer.
  Roam deadline indication
  Timeout indication