## Slide 1: Operational Parameter Indication for Seamless Roaming
Date: 2024-12-01
Authors:

## Slide 2: Abstract
Near-static context transfer is one of the key aspects of seamless roaming procedure:
  Enables a non-AP MLD to prepare the target AP MLD with necessary setups prior to roam
In this contribution we discuss some information items which can benefit the device side if included in context transfer signaling:
  Operational parameters upon roam: Parameters that the non-AP MLD can use upon roam.

## Slide 3: Context Transfer Background
A device may have set up more than one feature with the current AP.
Setting up each of the features one by one with the target AP can take multiple frame exchanges which is not desired.
As the device roams to a target AP, it is important that the features setup by STA with the current AP are also setup on the target AP.
Two types of context:
  Near static: setups which do not change on a short time scale.
    Limit to a few features
  Dynamic: which can keep changing on a short time scale.
Context | Type
Seq Number (SN) | Dynamic
Packet Number (PN) | Dynamic
BA context | Dynamic
BA setup | Near Static
SCS/MSCS | Near Static
EPCS | Near Static
TWT and variants (bTWT, rTWT, etc.) | Near Static
P2P TWT/CoEx session | Near Static
Example features that can benefit from context transfer

## Slide 4: Near Static Context Transfer
Near static context transfer procedure can enable a non-AP MLD to prepare a target AP MLD with necessary setups for its operation upon roam.
In this contribution, we discuss some information items whose inclusion in the context transfer signaling is critical or beneficial for the non-AP MLD.

## Slide 5: Operational Parameters Upon Roam
For some features, the non-AP MLD may need some operational parameter information from the target AP MLD if the target AP MLD accepts the context.
  Examples:
    In the case of EPCS, the non-AP MLD may need the enhanced EDCA parameters to use upon roam if the context related to EPCS is transferred to the target AP MLD.
    In the case of SCS, the non-AP MLD may need the SCS ID, service start time, service start time link ID.
Including such operation parameter information in the response frame is necessary.
Non-AP MLD
Current AP MLD
Target AP MLD
Context transfer req
Near static context transfer
Context transfer resp<…, operational parameters,…>

## Slide 6: Conclusion
In this contribution, we discussed signaling details for near static context transfer.
  Operational parameters indication