## Slide 1: Single Step Preparation and Execution for Seamless Roaming
Date: 2024-08-06
Authors:

## Slide 2: Abstract
In this contribution, we discuss a case for performing preparation and execution in a single step
  Description of the use case
  Example of how signaling can work

## Slide 3: Seamless Roaming Procedural Overview
Phase | Purpose
Enh. Discovery | Domain AP info gathering
Recommendation | Info gathering for candidate AP assessment considering: Context Load, etc.
Preparation | Prepare 1 target AP MLD for roaming (more than one is TBD) Near static context transfer
Execution | Initiate transition procedures: Dynamic context transfer DS remapping
Buffered data handling | Handling buffered data at current AP Can be considered a part of the above stage
TGbn has agreed to define procedures that enable a non-AP MLD to roam from current AP MLD to target AP MLD while remaining in state 4.
A number of contributions have discussed various procedures for seamless roaming (summarized in the table)
A number of target use cases/scenarios have also been discussed so far:
  Preparation of target AP MLD links through current AP MLD prior to roaming
  Preparation (context transfer) done through target AP MLD
  …

## Slide 4: Single Step Preparation and Execution
A non-AP MLD may not have the time to perform preparation in some cases. E.g., sudden drop in RSSI.
Consequently, the non-AP MLD may have to perform preparation and execution in a single step.
In our previous contribution[1-2], we discussed the details of signaling design.
Next, we show the example operation based on that signaling
STA
Current AP
Target AP
Preparation + Execution req
Preparation + Execution response
AP to AP communication
STA transitions to target AP
STA communicates with Target AP

## Slide 5: Example Operation: Execution and preparation in single step
EXE Resp: Modified Reconfiguration response frame format
Order | Meaning
1 | Category
2 | Protected UHR Action
3 | Dialog Token
4 | AID (optional)
5 | Transferred context indication
6 | Operation parameters
8 | Suggested parameters
10 | Count
11 | Reconfiguration Status List
12 | Group Key Data (optional)
13 | OCI element (optional)
14 | Basic Multi-link element (optional)
STA
Current AP
Exe req
Exe resp
Interaction with target
EXE Req: Modified Reconfiguration request frame format
Order | Meaning
1 | Category
2 | Protected UHR Action
3 | Dialog token
4 | Target AP MLD identifier
5 | Action indicator field: NS + R
6 | Context to be transferred
7 | Reconfiguration Multi-link element
8 | OCI element

## Slide 6: Conclusion
In this contribution we discuss a use case for performing preparation and execution in a single step.
We discuss the signaling and show an example operation.

## Slide 7: References
[1] IEEE 802.11-25/388, “Link Reconfiguration Framework for Preparation and Execution Phases of Seamless Roaming”
[2] IEEE 802.11-25/390, “Link Reconfiguration Signaling Design for Next Generation WLANs”