## Slide 1: Transmit and Receive Specifications for New MCS in 11bn
Date: 2025-03-06
Authors:
Name | Affiliations | Address | Phone | email
Alice Chen | Qualcomm Technologies Inc. |  |  | alicel@qti.qualcomm.com
Lin Yang |  |  |  | 
Daeseok Nam |  |  |  | 
Bin Tian |  |  |  | 

## Slide 2: Introduction
Transmit and receive specifications for new MCS in 11bn are TBD
  11-25/354 [1] proposed Tx EVM requirements for 4 new non-ELR MCSs
  11-25/98r0 [2] proposed Rx sensitivity and ACR/NACR requirements for 2 ELR-MCSs
In this presentation, we discuss the following
  Thoughts on IEEE spec defined testing
  Tx EVM requirements for new non-ELR MCSs in UHR MU PPDUs
  Rx minimum sensitivity and ACR/NACR requirements for new ELR MCSs

## Slide 3: Thoughts on Testing
Similar to 11n, the testing for the non-ELR MCSs is for equal modulation (EQM) only
When LDPC is used, should disable 2xLDPC
  Consistent to pre-UHR results for existing MCS

## Slide 4: Tx EVM Proposal for Non-ELR MCSs in UHR MU PPDUs
Our results are the same as [1]
Modulation | Coding rate | Relative constellation error in an UHR MU PPDU (dB)
BPSK | 1/2 | -5
QPSK | 1/2 | -10
QPSK | 2/3 | -12
QPSK | 3/4 | -13
16-QAM | 1/2 | -16
16-QAM | 2/3 | -18
16-QAM | 3/4 | -19
16-QAM | 5/6 | -20
64-QAM | 2/3 | -22
64-QAM | 3/4 | -25
64-QAM | 5/6 | -27
256-QAM | 2/3 | -29
256-QAM | 3/4 | -30
256-QAM | 5/6 | -32
… | … | …

## Slide 5: Proposal for ELR MCSs
Rx minimum sensitivity
  Same as MCS0 due to capped by CCA performance. Same as [2]
ACR/NACR
  Same as MCS0. Same as [2]
MCS | Modulation | Coding rate | Duplication | Minimum sensitivity (20 MHz PPDU) (dBm)
ELR-MCS0 | BPSK | 1/2 | 52-tone RU with four times’ duplication | -82
ELR-MCS1 | QPSK | 1/2 | 52-tone RU with four times’ duplication | -82
MCS | Modulation | Coding rate | Duplication | Adjacent channel rejection (dB) | Nonadjacent channel rejection (dB)
 |  |  |  | 20 MHz channel | 20 MHz channel
ELR-MCS0 | BPSK | 1/2 | 52-tone RU with four times’ duplication | 16 | 32
ELR-MCS1 | QPSK | 1/2 | 52-tone RU with four times’ duplication | 16 | 32

## Slide 6: Summary
IEEE 802.11bn spec defined testing should be consistent to legacy standards
  EQM only
  Not use 2xLDPC
The non-ELR MCSs follow similar Tx EVM trend as existing MCSs
ELR MCSs use same receive specification as MCS0

## Slide 7: Reference
11-25/354r0, Transmit Constellation Error for Additional MCSs, Genadiy Tsodik, et. al (Huawei)
11-25/98r0, UHR Receiver Minimum Input Sensitivity for ELR MCSs, Juan Fang, et. al (Intel)

## Slide 8: SP1
Do you agree to include the following to the 11bn SFD?
  The testing in the transmit and receive specification in IEEE 802.11bn spec should only use EQM (i.e., not use UEQM)
  The testing in the transmit and receive specification in IEEE 802.11bn spec should not use 2xLDPC, if LDPC is used

## Slide 9: SP2
Do you agree to include the following to the 11bn SFD?
  ELR MCSs use same Rx minimum sensitivity and ACR/NACR specifications as MCS0
  Supporting doc: 11-25/392r0, 11-25/98r0

## Slide 10: appendix