## Slide 1: DLTF sequence design for 60MHz DBW DRU Transmission
Date: 2025-03
Authors:
Name | Affiliation | Address | Phone | Email
Chenchen Liu | Huawei Technologies Co., Ltd | Huawei Base, Bantian, Shenzhen |  | liuchenchen1@huawei.com
Yan Xin |  |  |  | 
Jian Yu |  |  |  | 
Ming Gan |  |  |  | 

## Slide 2: Introduction
Challenges with Existing LTF Sequences
  High PAPR Issues: Current LTF sequences are unsuitable for DRU due to their high PAPR.
Need for Customized LTF Sequences
  Tailored Design: LTF sequences must be specifically designed to align with the DRU tone plan and pilot locations.
Advancements in DRU for 60MHz DBW
  IEEE Approval: DRU over 60MHz DBW was approved in the November meeting, specifically for scenarios where the highest 20MHz subchannel is punctured.
  Proposed Solutions: Tone Plan: Introduced in [1]; Pilot Design: Detailed in [1]

## Slide 3: 60 MHz DRU Tone Plan[1]
52-tone DRU i=1:12 | DRU1 [-499:14:-23, 5:14:229] | DRU2 [-492:14:-16, 12:14:236] | DRU3 [-496:14:-20, 8:14:232] | DRU4 [-489:14:-13, 15:14:239]
 | DRU5 [-498:14:-22, 6:14:230] | DRU6 [-491:14:-15, 13:14:237] | DRU7 [-495:14:-19, 9:14:233] | DRU8 [-488:14:-12, 16:14:240]
 | DRU9 [-497:14:-21, 7:14:231] | DRU10 [-490:14:-14, 14:14:238] | DRU11 [-494:14:-18, 10:14:234] | DRU12 [-487:14:-11, 17:14:241]
106-tone DRU i=1:6 | DRU1 [-499:7:-9, 5:7:243] | DRU2 [-496:7:-6, 8:7:246] | DRU3 [-498:7:-8, 6:7:244] | DRU4 [-495:7:-5, 9:7:247]
 | DRU5 [-497:7:-7, 7:7:245] | DRU6 [-494:7:-4, 10:7:248] |  | 
242-tone DRU i=1:3 | DRU1 [-499:7:-9, 5:7:243, -496:7:-6, 8:7:246, -458:21:-38, 25:21:193] |  | DRU2 [-498:7:-8, 6:7:244, -495:7:-5, 9:7:247, -451:21:-31, 32:21:200] | 
 | DRU3 [-497:7:-7, 7:7:245, -494:7:-4,10:7:248, -444:21:-24, 39:21:207] |  |  | 
DRU size | Pilot indices
52-tone DRU i=1:12 | {-373 -219 -65 173}, {-450 -296 -142 96}, {-412 -258 -104 134}, {-335 -181 -27 211}, {-386 -232 -78 160}, {-463 -309 -155 83}, {-425 -271 -117 121}, {-348 -194 -40 198}, {-399 -245 -91 147}, {-476 -322 -168 70}, {-438 -284 -130 108}, {-361 -207 -53 185}
106-tone DRU i=1:6 | {-450 -296 -142 96}, {-335 -181 -27 211}, {-463 -309 -155 83}, {-348 -194 -40 198}, {-476 -322 -168 70}, {-361 -207 -53 185}
242-tone DRU i=1:3 | {-450 -335 -296 -181 -142 -27 96 211}, {-463 -348 -309 -194 -155 -40 83 198}, {-476 -361 -322 -207 -168 -53 70 185}

## Slide 4: Proposed Sequence for 60MHz DBW Tone Plan A [1]
=[0 1 1 -1 -1 -1 1 0 1 1 -1 -1 1 -1 0 -1 1 -1 -1 1 -1 0 1 -1 1 -1 -1 1 0 1 -1 -1 -1 -1 1 0 -1 -1 1 -1 1 1 1 1 1 -1 -1 1 -1 1 1 -1 -1 1 -1 -1 1 1 -1 1 1 1 1 1 -1 -1 -1 -1 1 -1 1 -1 -1 -1 1 1 -1 1 -1 1 1 1 1 1 -1 1 1 1 1 -1 1 -1 1 -1 1 -1 1 1 1 -1 -1 -1 1 -1 1 -1 1 1 -1 -1 -1 -1 -1 -1 1 1 -1 -1 1 1 1 -1 1 1 -1 -1 1 1 1 -1 1 1 -1 1 1 -1 1 1 -1 1 -1 1 -1 -1 1 -1 -1 -1 -1 1 1 1 1 1 1 -1 -1 -1 -1 1 -1 1 1 1 -1 1 -1 1 -1 -1 1 1 -1 -1 1 -1 -1 1 -1 1 -1 -1 1 -1 1 1 1 1 -1 1 1 -1 -1 -1 -1 1 -1 -1 1 1 -1 1 1 1 -1 -1 1 1 -1 -1 1 1 1 -1 1 1 -1 1 1 -1 -1 1 -1 1 -1 1 -1 1 1 1 -1 1 1 -1 -1 -1 1 1 1 -1 -1 1 -1 -1 1 1 1 -1 1 -1 1 -1 1 -1 -1 1 -1 -1 -1 -1 -1 1 1 -1 -1 1 -1 1 -1 -1 1 -1 1 1 -1 -1 1 1 1 1 -1 -1 1 1 -1 -1 -1 -1 -1 -1 -1 1 -1 -1 -1 -1 -1 -1 1 1 -1 -1 -1 -1 1 1 1 1 1 1 -1 -1 1 1 1 1 1 -1 -1 -1 -1 -1 1 1 -1 1 -1 -1 1 1 -1 -1 1 1 -1 1 1 1 1 1 1 1 1 -1 -1 1 1 1 -1 1 -1 1 1 1 -1 -1 1 -1 1 -1 1 -1 -1 1 -1 -1 -1 -1 1 -1 -1 -1 1 1 1 -1 1 1 1 -1 -1 1 -1 1 -1 1 1 1 -1 -1 -1 1 -1 -1 -1 -1 1 -1 1 1 -1 1 1 -1 1 -1 1 -1 -1 -1 -1 -1 -1 1 -1 -1 1 -1 1 1 -1 1 1 -1 1 1 1 1 -1 1 1 1 -1 1 -1 -1 -1 -1 1 -1 1 1 -1 1 1 -1 -1 -1 1 -1 1 -1 1 -1 1 1 -1 1 -1 -1 -1 1 1 1 -1 -1 -1 1 1 1 -1 -1 1 1 1 -1 1 1 1 1 1 -1 1 0 -1 1 1 1 -1 -1 0 1 1 1 1 -1 1 0 0 0 0 0 0 0 0 1 1 -1 -1 1 1 0 1 1 1 -1 1 1 0 1 -1 -1 -1 1 1 1 -1 -1 -1 -1 1 -1 -1 1 1 1 1 1 -1 1 1 -1 -1 1 -1 1 1 1 1 1 1 1 -1 -1 1 1 1 -1 -1 -1 -1 -1 1 1 -1 1 -1 -1 1 1 1 1 -1 -1 -1 1 1 1 -1 -1 -1 -1 -1 1 1 -1 1 -1 1 1 1 -1 1 1 -1 -1 1 -1 1 1 1 1 -1 -1 1 -1 -1 1 1 1 1 1 1 1 -1 1 1 1 -1 1 -1 1 1 -1 -1 -1 1 -1 1 1 1 -1 1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 1 1 1 -1 -1 -1 -1 1 1 -1 1 -1 1 -1 1 1 1 -1 1 -1 1 1 -1 1 -1 1 -1 1 1 -1 -1 -1 -1 -1 -1 -1 1 -1 -1 -1 1 -1 1 1 1 1 1 -1 -1 -1 1 -1 1 1 -1 -1 -1 1 -1 1 -1 -1 -1 1 1 1 1 -1 1 1 -1 0 1 -1 -1 -1 1 1 0 -1 -1 -1 1 1 -1 0 -1 1 1 1 1 -1 0 -1 -1 -1 -1 -1 -1 0 1 1 1 -1 -1 1 0 0 0 0 0]

## Slide 5: PAPR Evaluation
Worst PAPR (dB) for Max Nss=2 of the proposed LTF sequence for different DRUs
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
DRU52 | 3.30 | 3.79 | 3.79 | 4.02 | 3.75 | 3.65 | 3.86 | 3.56 | 3.78 | 3.86 | 3.34 | 3.81
DRU106 | 4.33 |  | 4.34 |  | 4.23 |  | 3.96 |  | 4.32 |  | 4.30 | 
DRU242 | 5.05 |  |  |  | 5.07 |  |  |  | 5.10 |  |  | 
Max PAPR (dB) |  |  | 
RU size | 80 MHz RRU LTF | 80 MHz DLTF | Proposed 60 MHz DLTF
52-tone | 4.97 | 5.08 | 4.02
106-tone | 5.53 | 5.20 | 4.34
242-tone | 5.60 | 5.38 | 5.10

## Slide 6: Conclusion
Our DRU LTF sequences demonstrate good PAPR performance for all DRU sizes, effectively reducing potential signal distortions and enhancing transmission quality and channel estimation results.

## Slide 7: References
[1] 11-25-0154-00-00bn-alternative-dru-tone-plan-design-for-60mhz-dbw

## Slide 8: SP1
Do you agree to include the following 4xLTF sequence for DRU of 60MHz DBW into the 11bn SFD
=[0 1 1 -1 -1 -1 1 0 1 1 -1 -1 1 -1 0 -1 1 -1 -1 1 -1 0 1 -1 1 -1 -1 1 0 1 -1 -1 -1 -1 1 0 -1 -1 1 -1 1 1 1 1 1 -1 -1 1 -1 1 1 -1 -1 1 -1 -1 1 1 -1 1 1 1 1 1 -1 -1 -1 -1 1 -1 1 -1 -1 -1 1 1 -1 1 -1 1 1 1 1 1 -1 1 1 1 1 -1 1 -1 1 -1 1 -1 1 1 1 -1 -1 -1 1 -1 1 -1 1 1 -1 -1 -1 -1 -1 -1 1 1 -1 -1 1 1 1 -1 1 1 -1 -1 1 1 1 -1 1 1 -1 1 1 -1 1 1 -1 1 -1 1 -1 -1 1 -1 -1 -1 -1 1 1 1 1 1 1 -1 -1 -1 -1 1 -1 1 1 1 -1 1 -1 1 -1 -1 1 1 -1 -1 1 -1 -1 1 -1 1 -1 -1 1 -1 1 1 1 1 -1 1 1 -1 -1 -1 -1 1 -1 -1 1 1 -1 1 1 1 -1 -1 1 1 -1 -1 1 1 1 -1 1 1 -1 1 1 -1 -1 1 -1 1 -1 1 -1 1 1 1 -1 1 1 -1 -1 -1 1 1 1 -1 -1 1 -1 -1 1 1 1 -1 1 -1 1 -1 1 -1 -1 1 -1 -1 -1 -1 -1 1 1 -1 -1 1 -1 1 -1 -1 1 -1 1 1 -1 -1 1 1 1 1 -1 -1 1 1 -1 -1 -1 -1 -1 -1 -1 1 -1 -1 -1 -1 -1 -1 1 1 -1 -1 -1 -1 1 1 1 1 1 1 -1 -1 1 1 1 1 1 -1 -1 -1 -1 -1 1 1 -1 1 -1 -1 1 1 -1 -1 1 1 -1 1 1 1 1 1 1 1 1 -1 -1 1 1 1 -1 1 -1 1 1 1 -1 -1 1 -1 1 -1 1 -1 -1 1 -1 -1 -1 -1 1 -1 -1 -1 1 1 1 -1 1 1 1 -1 -1 1 -1 1 -1 1 1 1 -1 -1 -1 1 -1 -1 -1 -1 1 -1 1 1 -1 1 1 -1 1 -1 1 -1 -1 -1 -1 -1 -1 1 -1 -1 1 -1 1 1 -1 1 1 -1 1 1 1 1 -1 1 1 1 -1 1 -1 -1 -1 -1 1 -1 1 1 -1 1 1 -1 -1 -1 1 -1 1 -1 1 -1 1 1 -1 1 -1 -1 -1 1 1 1 -1 -1 -1 1 1 1 -1 -1 1 1 1 -1 1 1 1 1 1 -1 1 0 -1 1 1 1 -1 -1 0 1 1 1 1 -1 1 0 0 0 0 0 0 0 0 1 1 -1 -1 1 1 0 1 1 1 -1 1 1 0 1 -1 -1 -1 1 1 1 -1 -1 -1 -1 1 -1 -1 1 1 1 1 1 -1 1 1 -1 -1 1 -1 1 1 1 1 1 1 1 -1 -1 1 1 1 -1 -1 -1 -1 -1 1 1 -1 1 -1 -1 1 1 1 1 -1 -1 -1 1 1 1 -1 -1 -1 -1 -1 1 1 -1 1 -1 1 1 1 -1 1 1 -1 -1 1 -1 1 1 1 1 -1 -1 1 -1 -1 1 1 1 1 1 1 1 -1 1 1 1 -1 1 -1 1 1 -1 -1 -1 1 -1 1 1 1 -1 1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 1 1 1 -1 -1 -1 -1 1 1 -1 1 -1 1 -1 1 1 1 -1 1 -1 1 1 -1 1 -1 1 -1 1 1 -1 -1 -1 -1 -1 -1 -1 1 -1 -1 -1 1 -1 1 1 1 1 1 -1 -1 -1 1 -1 1 1 -1 -1 -1 1 -1 1 -1 -1 -1 1 1 1 1 -1 1 1 -1 0 1 -1 -1 -1 1 1 0 -1 -1 -1 1 1 -1 0 -1 1 1 1 1 -1 0 -1 -1 -1 -1 -1 -1 0 1 1 1 -1 -1 1 0 0 0 0 0]