## Slide 1: DSO Switch Back Rules
Date: 2025-03-08
Authors:

## Slide 2: Recap
Many Wi-Fi clients do not support the full bandwidth option supported by the AP
  While APs may support up to 320 MHz, client may support only 80 MHz, or 160 MHz
When the AP has traffic for multiple STAs, if at least one client is wideband, Multi-User OFDMA can be used to schedule Resource Units (RUs) to the wideband STA in S80 or S160
  If no such client exists, large portions of the operational bandwidth go underutilized, leading to poor spectral efficiency
  802.11bn must address such underutilization by allowing narrowband devices to use different portions of the operational bandwidth
P20
S20
S40
S80
subchannels
In-BSS Transmission to 40 MHz STA
In-BSS Transmission to 160 MHz STA
Unutilized resource
Time
Frequency
WIFI 7

## Slide 3: Recap
DSO operation comprises three parts:
  Switch from primary sub-band to DSO sub-band upon receiving the DSO initial Control frame
  Frame exchanges between the AP and the DSO STA on the DSO sub-band
  Switch back from the DSO sub-band to the primary sub-band after the end of the frame exchange sequence
Initial Control frame exchange to facilitate DSO switching
In-BSS Transmission to 80 MHz STA1
(DL)
In-BSS Transmission to 80 MHz STA2
(DL)
Time
Frequency
Ack
(UL)
Ack
(UL)
STA1 parked on P20
Subsequent frame exchanges
P20
BSS bandwidth
BSRP Trigger frame
non-HT dup PPDU
(DL)
BSR
STA2
(UL)
BSR
STA1
(UL)
PADDING
Switch back operation

## Slide 4: DSO Switch Back Rules
The DSO mechanism bears similarities with the eMLSR operations defined in 802.11be
Owing to their similarities, we propose that the switch back rules for DSO be the same as those defined in eMLSR, which involve:
  After the last transmitted or received frame, wait for an “observation period” of aSIFSTime + aSlotTime + aRxPHYStartDelay to check for more incoming frames from the AP
  If no frame addressed to the STA is received by the DSO STA until the end of the observation period, initiate switch back
 | eMLSR | DSO
Switching | Reception of ICF  switch to the link on which ICF is received | Reception of ICF  switch to the DSO sub-band indicated in the ICF
Frame exchanges | Subsequent frame exchanges are performed on the eMLSR link on which ICF was received | Subsequent frame exchanges are performed on the DSO sub-band indicated in the DSO ICF
Switch back | At the end of the frame exchanges, switch back to listening operation on all eMLSR links | At the end of the frame exchanges, switch back to the primary sub-band

## Slide 5: DSO Switch Back Operation
The entire DSO frame exchange sequence, including the switch back operation is illustrated below
In-BSS Transmission to 80 MHz STA1
(DL)
In-BSS Transmission to 80 MHz STA2
(DL)
Time
Frequency
Ack
(UL)
Ack
(UL)
STA1 parked on P20
Subsequent frame exchanges
After STA2 sends the ACK, it waits on S80 for an additional timeout interval of aSIFSTime + aSlotTime + aRxPhyStartDelay
When no frame is addressed to STA2 during the timeout interval, it initiates switch back to P20
DSO Switch Back Delay
At the end of the DSO transition delay, STA2 has parked its radio back on P20
P20
BSS bandwidth
BSRP Trigger frame
non-HT dup PPDU
(DL)
BSR
STA2
(UL)
BSR
STA1
(UL)
PADDING
Initial Control frame exchange to facilitate DSO switching

## Slide 6: Conclusions
In this presentation, we focus on the DSO switch back rules
  After the end of the DSO frame exchanges between the AP and DSO STA, the DSO STA must switch back from the DSO sub-band to the primary sub-band
We propose to have the same rules as eMLSR for a DSO STA to switch back from DSO sub-band to the primary sub-band

## Slide 7: Straw Polls
Do you agree to have the same rules as eMLSR for a DSO STA to switch back from DSO sub-band to the primary sub-band?
  Whether there are other conditions is TBD