## Slide 1: Discussion on LDPC only for MU-MIMO in 11bn
Date: 2025-03-08
Authors:
Name | Affiliations | Address | Phone | Email
Shengquan Hu | Mediatek | 2840 Junction Ave. San Jose, CA, 95134 |  | Shengquan.hu@mediatek.com
Jianhan Liu |  |  |  | Jianhan.liu@mediatek.com
Thomas Pare |  |  |  | 

## Slide 2: Discussions on LDPC only for MU-MIMO in 11bn
From 11be, limits only LDPC when RU size >= 484
11bn further limits LDPC only for the followings [1,2]:
  UEQM
  COBF
  IM
In addition, combined MU-MIMO+OFDMA is simplified & limited in 11bn [1,2], which results in:
  MU-MIMO is dis-allowed on RU242 OFDMA
  BCC for MU-MIMO is only applicable for just one case: BW 20MHz PPDU
With all above, it is worth & reasonable to consider LDPC as the only FEC coding scheme for DL/UL MU-MIMO in 11bn:
  Simplify the testing cases
  Can free up the coding bit for other potential use
Furthermore, propose that DL/UL MU-MIMO in UHR is optional for 20MHz only STA considering the support of LDPC coding is optional for BW20 PPDU in 11be

## Slide 3: Reference
[1]. Draft IEEE P802.11bn D0.1
[2]. 11-24-0209-09-00bn-specification-framework-for-tgbn

## Slide 4: SP#1
Do you agree to include the following text to the 11bn SFD?
  LDPC is the only FEC coding scheme for DL/UL MU-MIMO in 11bn

## Slide 5: SP#2
Do you agree to include the following text to the 11bn SFD?
  DL/UL MU-MIMO in UHR is optional for 20MHz only STA