## Slide 1: NPCA follow-up
Date: 2025-03-08
Authors:

## Slide 2: Conditions to transition to the NPCA PC
In 11bn D0.1, we have already agreed on a set of conditions that need to be respected to transition from the BSS primary channel (PC) to the NPCA PC
  When receiving an OBSS PPDU or OBSS control frame exchange
  If the NPCA duration is sufficient, based on information in the OBSS PPDU(s)…
  …
We propose to define one additional condition in this presentation.

## Slide 3: Additional condition to transition to the NPCA PC
If the NPCA STA operating on the BSS PC has its intra-BSS NAV which is set to a non-zero value, that means that its associated AP is currently operating on the BSS primary channel and for the time until the intra-BSS NAV reaches zero.
  During that time, it seems obvious that the NPCA STA should never transition to the NPCA PC because it’s associated AP will stay on the BSS PC
  With current NPCA conditions, this could happen if the NPCA STA receives an OBSS PPDU while its intra-BSS NAV is non-zero
To fix this issue, we simply propose that an NPCA STA shall not switch to the NPCA PC if its intra-BSS NAV is non-zero.

## Slide 4: Channel puncturing on NPCA PC
When an NPCA STA operates on the NPCA PC, it is not allowed to transmit on the channels that are occupied by the OBSS PPDU that triggered to transition of the NPCA STA to the NPCA PC.
This OBSS PPDU occupies the primary 20/40/80/160 of the NPCA BSS
If the OBSS PPDU occupies 20 MHz and the NPCA BSS BW is 320MHz, that means that the NPCA STA on the NPCA PC will only be able to use a BW of 160MHz, while it could use a BW of 280MHz for instance.
It is clearly a loss of efficiency that we need to fix.

## Slide 5: Solutions
Dynamic puncturing would be the most efficient solution to adapt to the exact OBSS BW, requiring inclusion of the punctured channels in the NPCA ICF frame
  This mode was however not defined in 11be and adds in complexity
Static puncturing (using an NPCA Disabled Subchannel Bitmap) specifically applied when operating on the NPCA PC would allow to use a larger BW in most of the cases with a fixed puncturing
  NPCA DSB could puncture the primary 80MHz of the 320MHz BSS for instance so that PPDUs on the NPCA PC could use 240MHz everytime the OBSS PPDU occupies 80MHz or less
  Being static, it is slightly less efficient than dynamic puncturing but is much simpler and allows to reuse a mechanism that is already defined and implemented

## Slide 6: Proposal
Define an NPCA Disabled Subchannel bitmap
  Which identifies the subchannels that are punctured when operating on the NPCA PC
Ensure puncturing pattern are valid and ensure that punctured channels in the Disabled subchannel bitmap (if any) are also punctured in the NPCA Disabled subchannel bitmap
Reuse existing procedure in 35.15.2 to apply puncturing when transmitting on the NPCA PC

## Slide 7: Straw poll 1
Do you agree to add the following to the 11bn SFD:
  An NPCA STA shall not switch to the NPCA PC if its intra-BSS NAV is non-zero.

## Slide 8: Straw poll 2
Do you agree to add the following to the 11bn SFD:
  An NPCA AP may advertise an NPCA Disabled Subchannel Bitmap that indicates the subchannels that are punctured when an NPCA STA operates on the NPCA Primary channel.
  The NPCA Disabled subchannel Bitmap shall satisfy the following requirements:
    The puncturing pattern indicated by the NPCA Disabled Subchannel Bitmap is a valid non-OFDMA puncturing pattern as defined in 36.3.2.1
    A 20 MHz subchannel indicated as punctured in the Disabled Subchannel Bitmap of the EHT Operation element (if any) is also indicated as punctured in the NPCA Disabled Subchannel Bitmap.
  if the AP advertises an NPCA Disabled Subchannel Bitmap and UHR NPCA STA transmits a PPDU on the NPCA primary channel, the UHR NPCA STA shall follow the same rules as 35.15.2 except that instead of Disabled Subchannel Bitmap it shall use the most recently exchanged NPCA Disabled Subchannel Bitmap.
  If the AP does not advertise an NPCA Disabled Subchannel Bitmap, a UHR NPCA STA shall follow the rules defined in 35.15.2.