## Slide 1: AMP Information Exchange and MAC SAP Interface
Date: 2025-05-10
Authors:

## Slide 2: Assumption of AMP Reader (AP) and AMP Tag (STA)
In AMP tag, the MAC layer and the up layer of MAC layer are tightly integrated.
  In one TXOP, after the up layer of MAC layer receives MAC indication primitive as the request from the MAC layer, the up layer of MAC layer can send the request primitive as the response.
In AMP reader, the MAC layer and the up layer of MAC layer are loosely integrated.
  In one TXOP, the AMP reader’s UP layer of MAC layer can’t transmit more than one request primitive.

## Slide 3: Primitive Definition (1)
AMP reader’s primitive
  Request primitive option
    Tag type
      Backscatter tag, non-backscatter tag
    RA (recipient ID)
      Unicast or broadcast ID (one-bit indication may replace the broadcast ID in frame header)
      It seems that TA is not required for the frame transmitted by the AMP reader.
    Data
      Information being exchanged from reader to tag
    Responding delay
      The time (starting at the end of the soliciting PPDU) required by the tag to prepare the responding frame.
    Responding frame length
    Random Slot number
      This is required when broadcast ID is required
    Threshold for random access, e.g. for accessing aloha slot
    Tx data rate
      Being not required if link adaptation is done in MAC layer
    Rx data rate
      Being not required if link adaptation is done in MAC layer

## Slide 4: Primitive Definition (2)
AMP reader’s primitive
  Indication primitive
    Tag type
      Backscatter tag, non-backscatter tag
    TA (transmitter ID)
      Unicast ID
        This one may not be needed.
    Data
      Information being exchanged from tag to reader
    Status
      Success, failure
        If the status is failure, the other parameters in the primitive are not valid

## Slide 5: Primitive Definition (3)
AMP tag’s primitive
  Request primitive
    Tag type
      Backscatter tag, non-backscatter tag
    TA (transmitter ID)
      Unicast ID
        This one may not be needed.
    Data
      Information being exchanged from tag to reader
    Responding frame length
      This may not be needed if the Data parameter can provide this information.
    Tx data rate

## Slide 6: Primitive Definition (4)
AMP tag’s primitive
  Indication primitive
    Tag type
      Backscatter tag, non-backscatter tag
    RA (recipient ID)
      Unicast ID
    Transaction ending indication
    Data
      Information being exchanged from tag to reader

## Slide 7: Primitives and MAC Frame Exchanges
Single TXOP is enough when the AP has single request.
Query Command
CTS
11 PHY
Header
Random
Trigger
Frame with STA ID
(CRC code)
Unicast
Trigger
(Query)
Frame (EPC)
EPC
CF End
(broadcast RAIID,
Data (Query))
(Data(EPC))
EPC
(Data(Query))
Data((EPC))
11bp PPDU
11 PPDU
11 PHY
Header
TXOP
Query
Contention through slot aloha.

## Slide 8: Primitives and MAC Frame Exchanges
Multiple TXOPs are required when the AP has multiple requests.
Query Command
CTS
11 PHY
Header
Random
Trigger
Frame with STA ID
(CRC code)
Unicast
Trigger
(Query)
Frame (EPC)
EPC
CF End
(broadcast RAIID,
Data (Query))
EPC
(Data(Query))
Data((EPC))
PPDU 1
11bp PPDU
11 PPDU
11 PHY
Header
Frame
(Authentication
response))
Unicast
Trigger
(Authentication)
11 PHY
Header
Authentication
CTS
Authentication)
Authentication response
(Data (Authentication) )
(Data (Authentication response))
Authentication
Response
(Unicast RAIID, delay of response,
Data(Authentication) )
(Data (Authentication response))
(Data(EPC))
Query
TXOP 1
TXOP 2
AP assumes no error if no response is received from the STA within delay of response.
Contention through slot aloha.

## Slide 9: Primitives and MAC Frame Exchanges
Multiple TXOPs are required when the AP has multiple requests.
11bp PPDU
11 PPDU
Frame
(responding data))
Unicast
Trigger
(Read)
11 PHY
Header
BP PHY
Header
Read
CTS
Read
Responding data
(Data (Authentication) )
(Data (Responding data))
Responding data
(Unicast RAIID,
Data(Read) )
(Data (Responding data))
TXOP 2
Query Command
CTS
11 PHY
Header
Random
Trigger
Frame with STA ID
(CRC code)
Unicast
Trigger
(Query)
Frame (EPC)
EPC
CF End
(broadcast RAIID,
Data (Query))
EPC
(Data(Query))
Data((EPC))
PPDU 1
11 PHY
Header
(Data(EPC))
Query
TXOP 1
Contention through slot aloha.