## Slide 1: Low Latency Operation with DPS
Date: 2025-03-12
Authors:

## Slide 2: Abstract
TGbn agreed Dynamic Power Saving (DPS) method
  DPS mode can be changed with ICF and ICR exchange.
    Lower capability mode (LCM) and higher capability mode (HCM) can be enabled with ICF and ICR exchange.
R-TWT was adopted in 11be for low latency traffic support.
  In order to support low latency traffic during R-TWT SP, both AP and STAs should be in HCM.
  When either an AP or a STA in LCM, ICF and ICR exchange shall be performed before R-TWT SP.
  After R-TWT SP, ICF and ICR exchange is required to change DPS mode into LCM.
In this contribution, autonomous DPS mode change is discussed.

## Slide 3: R-TWT with DPS
In order to support low latency traffic during R-TWT SP, both AP and STAs should be in HCM.
  When either an AP or a STA in LCM, ICF and ICR exchange shall be performed before R-TWT SP.
  After R-TWT SP, ICF and ICR exchange is required to change DPS mode into LCM.

## Slide 4: R-TWT and Autonomous DPS mode change
When R-TWT is setup, DPS mode can be autonomously changed before R-TWT SP and after R-TWT SP.
  DPS mode can be autonomously change into HCM before R-TWT SP.
  DPS mode can be autonomously change into LCM after R-TWT SP.
With autonomous DPS mode change for periodic low latency traffic support, additional power saving gain can be achieved.

## Slide 5: R-TWT and Autonomous DPS mode change
R-TWT SP with UL traffic
R-TWT SP with DL traffic

## Slide 6: Summary
This submission proposed autonomous DPS mode change for R-TWT
  DPS mode can be autonomously change into HCM before R-TWT SP.
  DPS mode can be autonomously change into LCM after R-TWT SP.
With autonomous DPS mode change for periodic low latency traffic support, additional power saving gain can be achieved.